## Slide 1: ELEN 21/COEN 21: Introduction to Logic Design
Lectures 1 & 2: Logic Circuits
Radhika S. Grover
Electrical Engineering Department
Santa Clara University
rgrover@scu.edu

## Slide 2: Lecture 1: Introduction to logic circuits
Overview:
Basic Definitions
Truth Tables
Basic Theorems and Properties of Boolean Algebra
Boolean Functions
Canonical and Standard Forms
Other Logic Operations
Digital Logic Gates

## Slide 3: A binary switch
x
1
=
x
0
=
(a) Two states of a switch
S
x
(b) Symbol for a switch

## Slide 4: Basic functions
(a) The logical AND function (series connection)
S
Power
supply
S
S
Power
supply
S
(b) The logical OR function (parallel connection)
Light
Light
x1
x2
x1
x2

## Slide 5: An inverting circuit
S
Light
Power
supply
R
x

## Slide 6: Truth tables
A truth table is a table of all possible combinations of the variables showing the relation between
- the values the variables can take and
- the result of the operation.
Truth table show operations in a compact form.

## Slide 7: Truth table for AND, OR operations

## Slide 8: Boolean Algebra
A set of elements is any collection of objects having a common property.
Common Postulates :
Closure : A set S is closed w.r.t. a binary operator if, for every pair of elements of S, the binary operator specifies a rule for obtaining a unique element of S.
E.g. set of natural numbers N = {1, 2, 3, 4..} is closed w.r.t. binary operator + but not binary operator −.

## Slide 9: Basic Definitions
Associative Law: A binary operator on a set S is said to be associative whenever
Commutative Law: A binary operator on a set S is said to be commutative whenever
Identity Law: A set S is said to have an identity element with respect to a binary operation on S if there exists an element e S with the property

## Slide 10: Basic Definitions cont.
Inverse: A set S having the identity element e with respect to a binary operator is said to have an inverse whenever for every x S there exists and element y S such that
Distributive Law: If and · are two binary operators on a set S, is said to be distributive over whenever
A field is a set of elements together with two binary operators, each having properties 1 through 5, and both operators combined to give property 6.

## Slide 11: Boolean Algebra
Boolean algebra has a set of elements B and two binary operators + and · provided the following (Huntington) postulates are satisfied:
1 (a) Closure with respect to the operator +.
(b) Closure with respect to the operator ·.
2 (a) An identity element with respect to + denoted by 0 : x + 0 = 0 + x = x.
(b) An identity element with respect to · designated by 1: x · 1 = 1 · x = x.
3(a) Commutative with respect to +: x + y = y + x
(b) Commutative with respect to · : x · y = y · x

## Slide 12: Boolean Algebra cont.
4 (a) · is distributive over +: x ·(y + z) = (x · y) + (x · z)
(b) + is distributive over ·: x + (y · z) = (x + y) · (x + z)
5. For every element x B, there is an element x’ B called complement of x such that (a) x + x’ = 1 and
(b) x · x’ = 0
6. There exists at least two elements, x, y B such that x ≠ y.
+ and · have operation rules equivalent to AND and OR.

## Slide 13: Difference between Boolean algebra and arithmetic/ordinary algebra
Associative law holds for Boolean algebra, while Huntington postulates do not include associative law.
Distributive law of + over · is valid for Boolean algebra, but not ordinary algebra.
Boolean algebra does not have subtraction or division operations.
Complement is not available in ordinary algebra
Ordinary algebra deals with real numbers. Two-valued Boolean algebra ( or boolean algebra) deals only with two elements: 0 and 1.

## Slide 14: Duality
Duality principle: Every algebraic expression deducible from the postulates of Boolean algebra remains valid if the operators and identity elements are interchanged.
i.e. simply interchange OR and AND operators and replace 1’s by 0’s and 0’s by 1’s.

## Slide 15: Basic Theorems
Theorem 1(a): x + x = x
Proof: x + x = (x + x) · 1 from postulate 2(b)
= (x + x) · (x + x’) (5a)
= x + xx’ (4b)
= x + 0 (5b)
= x (2a)

## Slide 16: Basic Theorems cont.
Theorem 1(b): x · x = x
Proof: x · x = (xx + 0) from postulate 2(a)
= xx + xx’ (5b)
= x(x + x’) (4a)
= x · 1 (5a)
= x (2b)

## Slide 17: Basic Theorems cont.
Theorem 2(a): x + 1 = 1
Proof: x + 1 = 1 · (x + 1) from postulate 2(b)
= (x + x’) · (x + 1) (5a)
= x + x’ · 1 (4b)
= x + x’ (2b)
= 1 (5a)
Theorem 2(b): x · 0 = 0 by duality

## Slide 18: Basic Theorems cont.
Theorem 3: (x’)’ = x
Proof: x + x’ = 1 and x · x’ = 0 from postulate 5
Complement of x’ is x and (x’)’
Since complement is unique,
(x’)’ = x

## Slide 19: Basic Theorems cont.
Theorem 6(a): x + xy = x
Proof: x + xy = x · 1 + xy from postulate 2(b)
= x(1 + y) (4a)
= x(y + 1) (3a)
= x · 1 (2a)
= x (2b)
Theorem 6(b): x (x + y ) = x by duality

## Slide 20: Summary of Postulates and Theorems of Boolean Algebra
Postulate 2 (a) x+0 = x (b) x·1=x
Postulate 5 (a) x+x’ =1 (b) x·x’=0
Theorem 1 (a) x+x = x (b) x·x=x
Theorem 2 (a) x+1=1 (b) x·0=0
Theorem 3 (x’)’ = x
Postulate 3 (a) x+y = y+x (b) xy = yx
Theorem 4 (a) x+(y+z) = (x+y)+z (b) x(yz) = (xy)z
Postulate 4 (a) x(y+z) = xy+xz (b)x+yz = (x+y)(x+z)
Theorem 5 (a) (x+y)’=x’y’ (b) (xy)’ = x’ + y’
Theorem 6 (a) x + xy = x (b) x(x + y) = x

## Slide 21: Example: Verify Theorem 6(a) using truth tables
x y xy x + xy
0 0 0 0
0 1 0 0
1 0 0 1
1 1 1 1
Verify the other theorems using truth tables.

## Slide 22: Operator Precedence
Operator precedence for evaluating Boolean expressions is:
Parenthesis
NOT
AND
OR
E.g. (x+y)’ , x’y’

## Slide 23: Basic gates
x
1
x
2
x
n
x
1
x
2
¼
x
n
+
+
+
x
1
x
2
x
1
x
2
+
x
1
x
2
x
n
x
1
x
2
x
1
x
2
×
x
1
x
2
¼
x
n
×
×
×
(a) AND gates
(b) OR gates
x
x
(c) NOT gate

## Slide 24: Boolean Functions
Boolean function F1 = x +y’z

## Slide 25: Other Boolean functions
Implement Boolean functions F2 = x’y’z + x’yz + xy’ and F3 = xy’ + x’z

## Slide 26: Literal
Each term in a Boolean expression is implemented with gates.
Each variable within the term is an input to the gate.
Literal is a single variable within a term that may be complemented or not.
Example: F2 has 3 terms and 8 literals.
How many terms and literals does F3 have?

## Slide 27: Example
Simplify x(x’ + y) to a minimum number of literals.
Simplify (x+y)(x+y’) to a minimum number of literals.

## Slide 28: Exercise
Simplify using Boolean algebra:
AB+A(B+C)+B(B+C)
(AB’(C+BD)+A’B’)C
A’BC+AB’C’+A’B’C’+AB’C+ABC

## Slide 29: Complement of a function
Complement of function F is F’.
Obtained by interchanging 1’s for 0’s and 0’s for 1’s.
Complement can be through DeMorgan’s Theorems (Theorem 5): (x+y)’ = x’y’ and (xy)’ = x’ + y’
Prove the three-variable form of DeMorgan’s theorem:
(A+B+C)’ = A’B’C’

## Slide 30: 3-variable form of DeMorgan’s theorem
(A + B + C)’ = (A + x)’ let B+C=x
= A’x’ theorem 5(a)
= A’(B+C)’ substitute B+C=x
= A’(B’C’ ) theorem 5(a)
= A’B’C’ theorem 4(b)

## Slide 31: Exercise
Apply DeMorgan’s theorem:
(A+B+C)’D
(ABC+DE)’
Simplify:
(AB+AC)’+A’B’C

## Slide 32: Representing a function
A function can be represented in one of the following ways:
Standard form
Canonical form

## Slide 33: Standard forms
Standard forms:
  Sum of products : Boolean expression containing AND terms.
  e.g. F = y’ + xy +x’yz’
  Product of sums: Boolean expression containing OR terms.
  e.g. F = x(y’+z)(x’ + y + z)
Non-Standard forms:
  E.g. F = AB + C(D + E)

## Slide 34: Exercise
Convert the following expressions to SOP form
AB+B(CD+EF)
(A+B)(B+C+D)

## Slide 35: Canonical forms
Canonical form: Boolean function expressed as a sum-of-minterms or product-of-maxterms.
E.g. f1=x’y’z + xy’z’ + xyz = m1 + m4 + m7
E.g. f2 = (x + y + z)(x + y + z’)(x + y’ + z)(x’ + y + z)
=M0M1M2M4

## Slide 36: Maxterms and Minterms
Minterms : A product term in which each of the n variables of an n variable function appears once.
represented as mj
Maxterms : dual of Minterms
represented as Mj
Sum of Minterms is also called canonical sum–of–products
Product of Maxterms is also called canonical product-of-sums

## Slide 37: Minterms for function with 3 binary variables
x y z Minterm Minterm designation
0 0 0 x’y’z’ m0
0 0 1 x’y’z m1
0 1 0 x’yz’ m2
0 1 1 x’yz m3
1 0 0 xy’z’ m4
1 0 1 xy’z m5
1 1 0 xyz’ m6
1 1 1 xyz m7

## Slide 38: Maxterms for function with 3 binary variables
x y z Maxterm Maxterm designation
0 0 0 x+y+z M0
0 0 1 x+y+z’ M1
0 1 0 x+y’+z M2
0 1 1 x+y’+z’ M3
1 0 0 x’+y+z M4
1 0 1 x’+y+z’ M5
1 1 0 x’+y’+z M6
1 1 1 x’+y’+z’ M7

## Slide 39: Example
Express the Boolean function F = A + B’C in a sum of minterms.
(Hint: Write A as AB(C+C’) + AB’(C+C’) and B’C as B’ (C+C’))
Convert the following expressions to canonical SOP form
AB+B(CD+EF)
(A+B)(B+C+D)

## Slide 40: Short notation for functions
F(A, B, C) = ∑m(1, 4, 5, 6, 7) (sum of minterms)
The same function can also be expressed as:
F(A, B, C) = ∏(0, 2, 3) (product of maxterms)
F’(A, B, C) = ∑(0, 2, 3) = m0 + m2 + m3
Therefore, (F’(A, B, C))’ = F(A, B, C)
= (m0 + m2 + m3)’
= M0 M2 M3
= ∏M(0, 2, 3)

## Slide 41: Exercise
Find the minimal SOP and minimal POS realizations of the following truth table:

## Slide 42: Solution
f
(a) A minimal sum-of-products realization
f
(b) A minimal product-of-sums realization
x
1
x
2
x
3
x
2
x
1
x
3
Notes: Hint
X2’x3+x3’x1=x2’x3+x3’x1+x1X2’
=(x2’+x3’)(x3+x1)

## Slide 43: Exercise: Deriving a function from a truth table
Express the following functions in truth tables, and then derive the function from the truth table in sum-of-products form and product-of-sums form.
F = x + y
F = xy’
F = xy + x’y’
F = x + yz
F = x + y’
Draw the gate level representations for each of these functions.

## Slide 44: Other logic operations
XOR f = xy’ + x’y
NOR f = (x + y)’
Complement f = x’
Identity f = 1
XNOR f = xy + x’y’
NAND f = (xy)’
Give the truth tables for each of the above logic operations

## Slide 45: Digital logic gates

## Slide 46: 7404
(b) Structure of 7404 chip
V
DD
Gnd

## Slide 47: The 74244 buffer chip

## Slide 48: An implementation of f = x1x2 + x2’x3.
VDD
x
1
x
2
x
3
f
7404
7408
7432

## Slide 49: Summary
Introduction to logic circuits
Truth tables
Boolean algebra: postulates and theorems
Minimizing a function using boolean algebra
SOP, POS
Designing a logic circuit from a truth table
CMOS transistors
Standard gates