## Slide 1: Chapter 1
Introduction

## Slide 2: WHY YOU SHOULD LEARN ASSEMBLY
To create system software for new processors:
  Compilers, Optimizers, Assemblers, Linkers, Device Drivers.
To better understand the limitations of fundamental data types:
  Precision, Range, Overflow, Representation Error
To better understand high level languages:
  Visualizing pass-by-value, pass-by-reference, recursion, pointers, and writing code to take advantage of memory hierarchies based on locality of reference

## Slide 3: WHEN ASSEMBLY IS NEEDED
To optimize performance:
  Implementing code fragments that account for most of the execution time.
  Using fixed-point arithmetic when the processor has no floating-point instructions
For code not easily implemented in a high-level language:
  Reversing the order of bits and bytes
Low-level access to hardware resources:
  Device drivers, interrupt routines.
Reverse engineering to understand and eradicate malware

## Slide 4: COMPUTER COMPONENTS
Main Memory
(1 GB = 109 bytes)
Disk Drive
(1 TB = 1012 bytes)
Registers
(16 x 32-bits)
Arithmetic and Logic Unit (ALU)
Control Unit
Central Processing Unit (CPU)
nanoseconds
(10-9 sec)
microseconds
(10-6 sec)
milliseconds
(10-3 sec)

## Slide 5: Terminology
Radix
  Binary
  Octal
  Hexadecimal
Bit (Binary Digit)
Byte
Word
  Half-Word
  Double-Word
Representation/Interpretation
Range
  Overflow
Resolution/Precision
Unsigned
Signed
  2’s complement
  Sign Plus Magnitude
Memory
  Address
Register
Opcode
Immediate Constant
Label

## Slide 6: WHAT ASSEMBLY LANGUAGE LOOKS LIKE
Assembler directives
Comment lines
Executable Instructions
Label
Instruction Operands
Comments
Instruction Mnemonic
("OpCode")

## Slide 7: HOW ASSEMBLERS WORK
Pass 1: Source code is processed one line at a time, from beginning to end. A "Location Counter" keeps track of the memory address of each line and is used to enter each label and its memory address into a "Symbol Table".
Pass 2: Source code is processed a second time, starting over at the beginning. Instruction mnemonics are replaced by their binary coded representation, using the symbol table to replace each label reference by its corresponding memory address.
Original source code
Label addresses determined
Label references resolved
Assembler Pass 2
Assembler Pass 1
Identifier | Relative Address
L1 | 1234
x | 4764
...
L1: LDRB R0,x+1
...
x: .byte 3,5,7
...
...
1234 LDRB R0,x+1
...
4764 .byte 3,5,7
...
...
1234 LDRB R0,[#4765]
...
4764 .byte 3,5,7
...
Location Counter
Symbol Table

## Slide 8: HARDWARE ENVIRONMENT STM32F429ZI Discovery Board
Touch-sensitive color display
240x320 pixels
ARM Cortex-M4F:
180 MHz 32-bit CPU
2MB of flash memory
256KB RAM (variables)
3-axis Gyroscope
FPU & DSP Instructions
CRC32 hardware
USB connector for power and downloading code
USB connector for thumb drive
Rear View
Front View
Programmable push button
Reset button

## Slide 9: Signed Integer Data Types

## Slide 10: Unsigned Integer Data Types

## Slide 11: IDENTIFIER CONVENTIONS
Variable Names
  All lowercase
  Append digits to indicate size in bits
  Prefix with ‘s’ for signed, ‘u’ for unsigned
Function Names
  Capitalize 1st letter of each word
Macros and Symbolic Constants
  All Caps