## Slide 1: Chapter 10
Working with Fixed-Point Real Numbers

## Slide 2: What Are Fixed-Point Reals?
A way to represent a real number using an integer.
Integers imply a binary point at the far right.
    Binary point far right: 00101101.  +4510
We can imagine the binary point to be anywhere:
    Binary point midway: 0010.1101  +2.812510

## Slide 3: Why Fixed-Point Reals?
Many inexpensive CPU chips designed for embedded applications do not have a hardware Floating-Point Unit (FPU).
Software libraries that emulate a FPU can be used but are very slow.
Many embedded applications are multi-threaded. Using a FPU significantly increases the context-switch time.

## Slide 4: Q FORMAT AND THE IMAGINARY BINARY POINT
A way to specify the position of the binary point
“Q” followed by the number of bits to the right of the binary point:
Sometimes use Qm.n, where m = # integer bits and n = # fractional bits.
Integer | Q | Implied | Interpretation |  | 
+7110 (010001112) | Q0 | 01000111. | +71/20 | = | +71.0000010
 | Q3 | 01000.111 | +71/23 | = | +8.8750010
−5710 (110010002) | Q2 | 110001.11 | −57/22 | = | −14.2500010
 | Q5 | 110.00111 | −57/25 | = | −1.7812510
Q8.0
Q5.3
Q6.2
Q3.5

## Slide 5: ADDITION AND SUBTRACTION OF FIXED-POINT REALS
Easy as long as operands have same Q format
  Just use regular integer addition or subtraction:
Operand | Integer | Q | Interpretation |  | 
A | +3010 | Q3 | +30/23 | = | +3.7510
B | −5410 | Q3 | -54/23 | = | −6.7510
Result | Integer | Q | Interpretation |  | 
A+B | −2410 | Q3 | -24/23 | = | −3.0010
A−B | +8410 | Q3 | +84/23 | = | +10.5010

## Slide 6: ADDITION AND SUBTRACTION OF FIXED-POINT REALS
Must pre-align operands w/different Q formats must be
Shift the operand w/fewer fractional bits left:
Operand | Integer | Q | Interpretation |  | 
A | +3010 | Q3 | +30/23 | = | +3.7510
B | −5410 | Q5 | -54/25 | = | −1.687510
Result | Integer | Q | Interpretation |  | 
A+B | +6610 | Q5 | +66/25 | = | +2.062510
Operand | Integer | Q | Interpretation |  | 
A | +12010 | Q5 | +120/25 | = | +3.7510
B | −5410 | Q5 | -54/25 | = | −1.687510

## Slide 7: MULTIPLICATION OF FIXED-POINT REALS
Consider what happens when you multiply two decimal reals:
1.53
×2.3
The digits of the product are determined without regard to the decimal points.
    Then the decimal point is inserted so that the number of fractional digits is the sum of those in the two operands.
153
×23
459
306
3519
3.519

## Slide 8: MULTIPLICATION OF FIXED-POINT REALS
Same as in decimal, but Q format changes
  The number of fractional bits in the product is the sum of those in the operands.
Operand | Integer | Q | Interpretation |  | 
A | +3010 | Q3 | +30/23 | = | +3.750010
B | +5110 | Q2 | +51/22 | = | +12.750010
Result | Integer | Q | Interpretation |  | 
A×B | +153010 | Q5 | +1530/25 | = | +47.812510

## Slide 9: INTEGER DIVISION
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
Dividend:
Divisor:
Quotient:
Division is often considered the inverse of multiplication. When the remainder is zero, the dividend is the product of the divisor and quotient. Thus the number of bits in the dividend should be the sum of those in the divisor and quotient.
Radix point
Radix point
Radix point
In integer division, the radix point of all operands is at the far right.

## Slide 10: FIXED-POINT REAL DIVISION
31 |  |  |  |  |  |  |  |  |  |  |  |  |  | 17 | 16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
15 |  |  |  |  |  | 9 | 8 |  |  |  |  |  |  |  | 0
Dividend:
Divisor:
Quotient:
Multiplication point of view:
The number of fractional digits in the dividend is the number in the divisor plus the number in the quotient.
Radix point (Q17)
Radix point
(Q8)
Radix point
(Q9)
Division point of view:
The number of fractional bits in the quotient is the number in the dividend less the number in the divisor.

## Slide 11: DIVISION OF FIXED-POINT REALS
Integer division, but Q format changes
  The number of fractional bits in the quotient is the number in the dividend less those in the divisor
Operand | Integer | Q | Interpretation |  | 
A | +126410 | Q5 | +1265/25 | = | +39.500010
B | +8310 | Q3 | +83/23 | = | +10.375010
Result | Integer | Q | Interpretation |  | 
A÷B | +1510 | Q2 | +15/22 | = | +3.750010 (Err: 1.50%)

## Slide 12: DIVISION: IMPROVING ACCURACY
Operand | Integer | Q | Interpretation |  | 
A | +126410 | Q5 | +1264/25 | = | +39.500010
B | +8310 | Q3 | +83/23 | = | +10.375010
Result | Integer | Q | Interpretation |  | 
A÷B | +1510 | Q2 | +15/22 | = | +3.750010 (Err: 1.50%)
Shift dividend left before dividing
  Increases Q factor of dividend and thus
  Increases Q factor of quotient and thus
  Increases number of fractional digits of quotient
23×A | +1011210 | Q8 | +10112/28 | = | +39.500010
(23×A)÷B | +12110 | Q5 | +121/25 | = | +3.7812510 (Err: 0.682%)

## Slide 13: DIVISION: IMPROVING ACCURACY
Operand | Integer | Q | Interpretation |  | 
23×A | +1015310 | Q8 | +10153/28 | = | +39.500010
B | +8310 | Q3 | +83/23 | = | +10.375010
Result | Integer | Q | Interpretation |  | 
(23×A+B/2)÷B | +12210 | Q5 | +122/25 | = | +3.8125010 (Err: 0.138%)
Increase the magnitude of dividend by half that of the divisor before dividing
  Rounds the least-significant bit of quotient
  Subtract (don’t add) when dividend is negative

## Slide 14: FIXED-POINT USING A UNIVERSAL Q16.16 FORMAT
Uses the same Q format for all variables
Q16.16 fits in a single 32-bit word
No pre-alignment needed to add or subtract
Product: 64 bits  32 bits x 32 bits (SMULL)
  Q16.16 result is the middle 32 bits
Double-length dividend must be in Q32.32 format so that quotient will be Q16.16

## Slide 15: Q16.16 × Q16.16 Multiplication
64-bit integer product
fractional part
whole part
0
63
32
31
Product (Q16.16)
Multiplier (Q16.16)
Multiplicand (Q16.16)
whole part
fractional part
31
0
32-bit integer multiplicand
whole part
fractional part
×
31
0
32-bit integer multiplier
SMULL
Some loss of range
Some loss of precision
47
16
15
48
discarded
discarded
Integer part
fractional part

## Slide 16: Example: Q8.8 × Q8.8 Multiplication
+4.2510 = 00000100.010000002 = 108810 (Q8.8)
×-3.7510 = 11111100.010000002 = -96010 (Q8.8)
1088 × -960 = -104448010
= FFF0.100016 (Q16.16)
= F0.1016 (Q8.8)
= -15.937510

## Slide 17: Example: Q16 Area of a Triangle
Q16 AreaOfTriangle(Q16 b, Q16 h) ;
AreaOfTriangle:
SMULL R0,R1,R0,R1 // R1.R0 = Q32.32 product b x h
LSR R0,R0,16 // Extract middle 32 bits
ORR R0,R0,R1,LSL 16
LSR R0,R0,1 // Divide by 2
BX LR
The second LSR can be eliminated by shifting right by 17 bits instead of 16.

## Slide 18: Interpreting a Q16.16 Real
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1
Implied position of Q16 binary point.
Interpret the 32-bit value as a signed 2's complement integer.
  (Implied binary point located at far right)
  001110001011110001112 = 23239110
Move implied binary point to middle of 32-bit value.
  (Divide integer by 216 = 65536)
  232391 / 65536 = 3.54610
Implied position of integer binary point.

## Slide 19: Converting Q16.16 to float
float Q16ToFloat(Q16 x)
{
return x / 65536.0 ;
}
Must be a floating-point constant
NOTE: When not using a floating-point processor, the C run-time library provides a (slow) software emulation of this floating-point division. Avoid using this function in any loop or repetitive computation.

## Slide 20: Creating a Q16.16 Real Constant
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
Implied position of the binary point.
typedef int32_t Q16 ; // NOTE: Container is an integer
Q16 x = 3.7 ; // NO: truncates to integer 3 (not 3.0)
Q16 x = (int32_t) (65536 * 3.7 + 0.5) ; // YES
For rounding
Multiply by 216 so that binary point is in the middle

## Slide 21: Converting float to Q16.16
Q16 FloatToQ16(float x)
{
float rounding ;
if (x >= 0.0) rounding = +0.5 ;
else rounding = -0.5 ;
return (int32_t) (65536 * x + rounding) ;
}
NOTE: When not using a floating-point processor, the C run-time library provides a (slow) software emulation of this floating-point calculation. Avoid using this function in any loop or repetitive computation.

## Slide 22: Example: Q16 Volume of a Sphere
Q16 VolumeOfSphere(Q16 r) ;
VolumeOfSphere:
SMULL R1,R2,R0,R0 // R2.R1 = Q32.32 product r squared
LSR R1,R1,16 // Extract Q16.16 product into R1
ORR R1,R1,R2,LSL 16
SMULL R0,R1,R1,R0 // R1.R0 = Q32.32 product r cubed
LSR R0,R0,16 // Extract Q16.16 product into R0
ORR R0,R0,R1,LSL 16
LDR R1,=274516 // R1 = (4*pi)/3 x 65536
SMULL R0,R1,R0,R1 // R1.R0 = Q32.32 volume
LSR R0,R0,16 // Extract Q16.16 product into R0
ORR R0,R0,R1,LSL 16
BX LR

## Slide 23: Q16 ÷ Q16 Division
Quotient (Q16.16)
fractional part
filled with 0’s
sign-extension
whole part
0
63
47
16
32
31
Dividend (Q16.16)
÷
whole part
fractional part
31
0
Divisor (Q16.16)
whole part
fractional part
31
0
  The ARM SDIV instruction is only 32 bits ÷ 32 bits
Double-length 64-bit integer dividend
32-bit integer divisor
32-bit integer quotient
Dividend (Q32.32)

## Slide 24: Example: Q8 ÷ Q8 Division
+4.2510 = 04.4016 = 108810 (Q8.8)
÷-3.7510 = FC.4016 = -96010 (Q8.8)
04.4016 = 0004.400016 = 27852810 (Q16.16)
278528 ÷ -960 = -290.1333…  -29010 (Q8.8)
= -1.132812510
Real answer = -1.1333… (loss of precision)

## Slide 25: Q16.16 × Q16.16 Multiplication
Q16.16 variable y has 16 fractional bits
Q16.16 variable has 16 fractional bits
31 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 0
31 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 0
63 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 32 | 31 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 0
×
LDR R0,x // R0  x (Q16.16)
LDR R1,y // R1  y (Q16.16)
SMULL R0,R1,R0,R1 // R1.R0  xy (Q32.32)
LSR R0,R0,16 // Extract middle 32 bits
ORR R0,R0,R1,LSL 16
STR R0,z // R0  z (Q16.16)
Thus the 64-bit Q32.32 product will have 32 fractional bits
6 instructions,
6 clock cycles

## Slide 26: Multiplying Q16.16 by Q32.0 Integer
Q16.16 variable has 16 fractional bits
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
31 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 0
63 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 32 | 31 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 0
×
Q32.0 integer N has 0 fractional bits
The 64-bit Q0.32 product will have 32 fractional bits
LDR R0,x // R0  x (Q16.16)
LDR R1,N // R1  N (Q32.0)
MUL R0,R0,R1 // R0  Nx (Q16.16)
STR R0,y // R0  y
4 instructions,
4 clock cycles

## Slide 27: Multiplying Q16.16 by Q0.32 Fraction
Q16.16 variable has 16 fractional bits
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
31 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 0
63 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 32 | 31 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 0
×
LDR R0,x // R0  x (Q16.16)
LDR R1,F // R1  F (Q0.32)
SMULL R0,R1,R0,R1 // R1.R0  Fx (Q16.48)
STR R1,y // R0  y (Q16.16)
Q0.32 fraction F has 32 fractional bits
The 64-bit product will have 48 fractional bits (Q16.48)  Use most-significant half of product
4 instructions,
4 clock cycles

## Slide 28: Constant Multiples of a Q16
LDR R0,x // R0  x (in Q16 format)
RSB R0,R0,R0,LSL 3 // R0  8x – 1x = 7x
STR R0,y // R0  y (in Q16 format)
Calculation | As Integer | Q16
R0 | 245,760 | +3.75
R0,LSL 3 | 1,966,080 | +30.00
R0,LSL 3 – R0 | 1,720,320 | +26.25
The Q16 format is really data type int32_t, so we can create multiples of Q16 values the same way we create multiples of integer values.

## Slide 29: Dividing Q16.16 by a Q32.0 Integer
31 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 0
31 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 0
31 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 0
÷
Q16.16 variable has 16 fractional bits
Q32.0 integer N has 0 fractional bits
The 32-bit Q16.16 quotient will have 16 fractional bits
LDR R0,x // R0  x (in Q16 format)
LDR R1,N // R1  N (in Q0 format)
SDIV R0,R0,R1 // R0  x/N (in Q16 format)
STR R0,y // R0  y

## Slide 30: Dividing Q16.16 by Integer Constant
LDR R0,x // R0  x (in Q16 format)
ASR R1,R0,2 // R1  000?? Or 111??
ADD R0,R0,R1,LSR 29 // R0  R0 + (0 or 7)
ASR R0,R0,3 // R0  x / 8
STR R0,y // R0  y (in Q16 format)
The Q16 format is really data type int32_t, so we can use the same technique for dividing by a constant that we used for integer values.

## Slide 31: Q32.32 FORMAT
Range of Q16.16 is only ±32768
Resolution of Q16.16 is only ~1.5×10-5
Next convenient choice is Q32.32
  Q32.32 Add/Subtract takes only 2 instructions
  Q32.32 Multiplication can be made efficient
  Q32.32 Division is difficult to impossible
    Most divisors are constants  Multiply by 1/K
  Used in SONY Playstation

## Slide 32: Creating Q32 Constants (w/out FP)
typedef int64_t Q32 ;
Q32 Q32Ratio(int32_t top, int32_t btm)
{
int32_t rounding = (top >= 0) ? +btm/2 : -btm/2 ;
return (((Q32) top << 32) + rounding) / btm ;
}
int64_t =
Choose sign to increase the magnitude of top
Real number expressed as a ratio of two integers
The Q32 representation of 1.0 is 0000 0001 0000 000016
This 64-bit division requires executing a loop on a 32-bit CPU, so limit how frequently function Q32Ratio is called.
Multiplication before integer division!

## Slide 33: Printing Q32 Values (w/out FP)
void PrintQ32(Q32 x)
{
int k ;
if (x < 0) { putchar('-') ; x = -x ; }
printf("%u", Upper32Bits(x)) ;
putchar('.') ;
for (k = 0; k < 5; k++)
{
Upper32Bits(x) = 0 ;
x = 10 * x ;
printf(“%d”, Upper32Bits(x)) ;
}
}
"5" is the number of fractional digits to print.
Decimal values must be printed in sign+magnitude.
Print magnitude of the integer part.
Print magnitude of the fractional part.

## Slide 34: Q32.32 × Q32.32 Multiplication
Must be fast – no loops!
Strategy:
  Compute: 128 bits  64 bits × 64 bits (unsigned)
  Convert unsigned product to 2’s complement
  Extract the middle 64 bits

## Slide 35: Decomposing Unsigned Integer Multiplication
  Break the decimal number 1234 into two halves:
    123410 = 102×12 + 34 = 1200 + 34
  Break a 64-bit unsigned integer into two 32-bit halves:
    AU = 232AHI + ALO = AHI00…………0 + ALO
  Then the 128-bit product of two 64-bit unsigned integers is:
    AUBU = (232AHI + ALO) (232BHI + BLO)
    = 264AHIBHI + 232(AHIBLO + ALOBHI) + ALO BLO
32 zeroes
Each partial product is 64 bits  32 bits x 32 bits (use UMULL instruction)

## Slide 36: 64×64 Unsigned Integer Multiplication
AHIBHI
AHIBLO
+
ALOBHI
+
ALOBLO
+
63
63
63
63
0
0
0
0
AUBU
0
127
Add AHIBHI to bits 127-64 of result
Add AHIBLO and ALOBHI to bits 95-32 of result and propagate any carries

## Slide 37: Example Using 8-Bit Operands
AU = 111010002 (23210) Note: 23210×4410 = 1020810
BU = 001011002 ( 4410)
AHI = 11102 (1410) ALO = 10002 ( 810)
BHI = 00102 ( 210) BLO = 11002 (1210)
AUBU = 28AHIBHI + 24(AHIBLO + ALOBHI) + ALOBLO
= 28×14×2 + 24(14×12 + 8×2) + 8×12
= 256×28 + 16×(168 + 16) + 96
= 7168 + 2944 + 96 = 1020810

## Slide 38: Convert Result to 2’s Complement
Polynomial interpretation for unsigned:
AU = 263A63 + 262A62 + … 20A0
Polynomial interpretation for 2’s complement:
AS = -263A63 + 262A62 + … 20A0
Thus: AS = AU - 2×263A63 A63 = sign bit
AS = AU when A ≥ 0
= AU - 264 when A < 0

## Slide 39: Convert Result to 2’s Complement
AS | BS | Signed 2’s complement product (ASBS)
≥ 0 | ≥ 0 | ASBS = AUBU
≥ 0 | < 0 | ASBS = AU(BU – 264) = AUBU – 264AU
< 0 | ≥ 0 | ASBS = (AU – 264)BU = AUBU – 264BU
< 0 | < 0 | ASBS = (AU – 264)(BU – 264) = AUBU – 264AU – 264BU + 2128
Discard: 2128 doesn’t affect 128-bit result
If AS < 0, subtract all 64 bits of BU from the most-significant half of the 128-bit unsigned product AUBU
If BS < 0, subtract all 64 bits of AU from the most-significant half of the 128-bit unsigned product AUBU

## Slide 40: Convert Result to 2’s Complement
AUBU
0
127
A63×B
B63×A
ASBS
0
127
−
−
63
63
0
0
If A <0, subtract B from the most-significant half of unsigned product
If B <0, subtract A from the most-significant half of unsigned product

## Slide 41: Example Using 8-Bit Operands
AS = 111010002 (-2410) Note: -2410×4410 = -105610
BS = 001011002 (+4410)
AUBU = 0010 0111 1110 00002 (1020810)
─ 0010 1100
ASBS = 1111 1011 1110 00002 (-105610)
AS < 0  subtract B from MS half

## Slide 42: Example Using 4.4 Operands
AS = 1110.10002 (-1.5010) Note: -1.5010×2.7510 = -4.12510
BS = 0010.11002 (+2.7510)
AUBU = 0010 0111 1110 00002 (1020810)
─ 0010 1100
ASBS = 1111 1011 1110 00002 (-105610)
1011.11102 (-4.12510)
AS < 0  subtract B from MS half

## Slide 43: Q32.32 × Q32.32 Multiplication
// int64_t Q32Product(int64_t A, int64_t B)
// A is in register pair R1.R0 (R1=MSW(A), R0=LSW(A))
// B is in register pair R3.R2 (R3=MSW(B), R2=LSW(B))
Q32Product:
PUSH {R4} // Preserve R4
// Compute R12.R4 = middle of 128-bit unsigned product
UMULL R12,R4,R0,R2 // LSW:R4 = MSHalf of LSW(A)xLSW(B)
MUL R12,R1,R3 // MSW:R12 = LSHalf of MSW(A)xMSW(B)
UMLAL R4,R12,R0,R3 // R12.R4 += 64 bits of LSW(A)xMSW(B)
UMLAL R4,R12,R1,R2 // R12.R4 += 64 bits of MSW(A)xLSW(B)
// Convert unsigned result to signed and leave in R1.R0
AND R1,R2,R1,ASR 31 // R1 = (A < 0) ? LSW(B) : 0
SUB R12,R12,R1 // R12 = (A < 0) ? (R12 – LSW(B)) : R12
AND R3,R0,R3,ASR 31 // R3 = (B < 0) ? LSW(A) : 0
SUB R1,R12,R3 // R1 = (B < 0) ? (R12 – LSW(A)) : R12
MOV R0,R4 // Copy LSW(result) to R0
POP {R4} // Restore R4
BX LR // Return to calling program.
MUL
AHIBHI
UMLAL
+ ALOBHI
UMLAL
+ AHIBLO
AUBU
AND/SUB
– BLO
AND/SUB
– ALO
R12
R4
UMULL
ALOBLO
ASBS
Execution Time: 17 clock cycles

## Slide 44: Q32.32 × Q32.0 Multiplication B is an Integer (BLO = 0)
AHIBHI
AHIBLO
+
ALOBHI
+
ALOBLO
+
63
63
63
63
0
0
0
0
AUBU
0
127
A63×B
B63×A
ASBS
0
127
−
−
63
63
0
0
Keep only middle 64 bits
The bits we would normally keep here are those of BLO, which happen to be all 0’s.

## Slide 45: Q32.32 × Q32.0 Multiplication B is an Integer (BLO = 0)
// int64_t Q32xInteger(int64_t A, int32_t Bhi)
Q32xInteger:
  UMULL R12,R3,R0,R2 // R3.R12 = Alo x Bhi
  MLA R3,R1,R2,R3 // R3 += Ahi x Bhi
  AND R2,R0,R2,ASR 31 // R2 = Bhi<0 ? Alo : 0
  SUB R1,R3,R2 // R1 = R3–R2 (MSHalf)
  MOV R0,R12 // R0 = LSHalf of product
  BX LR
Execution Time: 9 clock cycles (vs 17)
MLA
AHIBHI
AUBU
AND/SUB
– ALO
R3
R12
UMULL
ALO BHI
ASBS
R1
R0
Note: There is a similar savings when B is a purely fractional value (BHI = 0)

## Slide 46: Example: Area of a Circle
Q32 CircleArea(Q32 radius)
  {
  Q32 pi = Q32Ratio(314159, 100000) ;
  Q32 rSquared = Q32Product(radius, radius) ;
  return Q32Product(pi, rSquared) ;
  }

## Slide 47: Example: Discriminant
Q32 Discriminant(Q32 a, Q32 b, Q32 c)
  {
  Q32 bSquared = Q32Product(b, b) ;
  Q32 ac = Q32Product(a, c) ;
  return bSquared – (ac << 2) ;
  }
4 × a × c
Regular addition and subtraction operators work.
Left-shift works to multiply by 2k because we are using a fixed-point representation. (Won’t work with floating-point!)

## Slide 48: Example: Average
Q32 Average(Q32 a[], int32_t n)
  {
  Q32 total ;
  int32_t k ;
  total = 0 ;
  for (k = 0; k < n; k++)
  {
  total += a[k] ;
  }
  return Q32Ratio(total, n) ;
  }

## Slide 49: Q32.32 ÷ Q32.32 Division
Quotient (Q32.32)
fractional part
filled with 0’s
sign-extension
whole part
0
127
95
32
64
63
Dividend (Q32.32)
÷
whole part
fractional part
63
0
Divisor (Q32.32)
whole part
fractional part
63
0
Double-length 128-bit integer dividend
64-bit integer divisor
64-bit integer quotient
Cannot be decomposed into a straight-line sequence of 32-bit ARM divide instructions
Must use a loop (64 iterations)
Implement unsigned 128 ÷ 64
Use wrapper function for signed

## Slide 50: Q32.32 ÷ Q32.32 Division Wrapper Function for Signed #’s
extern uint64_t UQ32Quotient(uint64_t dividend, uint64_t divisor) ; #define MSWord(x) ((int32_t *) &x)[1] int64_t Q32Quotient(int64_t dividend, int64_t divisor) { uint64_t quotient ; int negate = 0 ; if ((MSWord(dividend) ^ MSWord(divisor)) < 0) negate = 1 ; if (dividend < 0) dividend = -dividend ; if (divisor < 0) divisor = -divisor ; quotient = UQ32Quotient((uint64_t) dividend, (uint64_t) divisor) ; return negate ? –((int64_t) quotient) : (int64_t) quotient ; }

## Slide 51: Unsigned Division: N-Bits ÷ N-Bits
Example: 4-bit dividend ÷ 4-bit divisor = 1310 ÷ 210 = 11012 ÷ 00102
0110
0010 1101 0010 0001101
0010
0011
0010
0010
0010
0001
0010
0001
Quotient = 6
Remainder = 1
We must prepend three 0’s to the dividend in order to compare the divisor to the first dividend digit.
(1) Divisor > dividend, so don’t subtract; quotient bit = 0
(2) Divisor ≤ dividend, so subtract; quotient bit = 1
(3) Divisor ≤ dividend, so subtract; quotient bit = 1
(4) Divisor > dividend, so don’t subtract; quotient bit = 0

## Slide 52: Unsigned Division: N-Bits ÷ N-Bits
Example: 4-bit dividend ÷ 4-bit divisor = 1310 ÷ 210 = 11012 ÷ 00102
Zero-Extend dividend to 2N bits: 0000 1101
Shift dividend left 1 bit: 0001 1010 MSW(dividend) < divisor, do nothing
Shift dividend left 1 bit: 0011 0100 MSW(dividend) ≥ divisor, subtract divisor, add 1 -0010+0001
0001 0101
Shift dividend left: 0010 1010 MSW(dividend) ≥ divisor, subtract divisor, add 1 -0010+0001
0000 1011
Shift dividend left : 0001 0110 MSW(dividend) < divisor, do nothing
Quotient = 6
Remainder = 1
4-bit divisor
Repeat 4 times
MS Bit of Quotient

## Slide 53
UNSIGNED Q32 ÷ Q32 DIVISION
#define MSWord(x) ((uint32_t *) &x)[1] uint64_t UQ32Quotient(uint64_t dividend, uint64_t divisor) { uint64_t upper64, lower64 ; // 128-bit unsigned dividend int k // Put 64-bit dividend in middle of 128 bits upper64 = (uint64_t) MSWord(dividend) ; lower64 = dividend << 32 ; // if (upper64 >= divisor) OVERFLOW! for (k = 0; k < 64; k++) { // The next 3 lines of code shift // a 128-bit value left by 1 bit upper64 <<= 1 ; if (MSWord(lower64) & 0x80000000) upper64 ¦= 1 ; lower64 <<= 1 ; if (upper64 >= divisor) { upper64 -= divisor ; lower64 ¦= 1 ; } } // upper64 = Remainder, lower64 = Quotient return lower64 ; }
Execution time = O(n), where n = # bits (64)
Use reciprocal multiplication whenever possible!
  Overflow is now possible for more than a zero divisor

## Slide 54
// uint64_t UQ32Quotient(uint64_t dividend, uint64_t divisor) .global UQ32Quotient UQ32Quotient: PUSH {R4,R5} LDR R5,=0 // upper64 = MSW(dividend) MOV R4,R1 MOV R1,R0 // lower64 = LSW(dividend) << 32 LDR R0,=0 LDR R12,=0 // k = 0 L1: CMP R12,64 // k < 64 ? BHS L4 LSL R5,R5,1 // upper64.lower64 <<= 1, C = MSbit ORR R5,R5,R4,LSR 31 LSL R4,R4,1 ORR R4,R4,R1,LSR 31 LSL R1,R1,1 ORR R1,R1,R0,LSR 31 LSL R0,R0,1 CMP R5,R3 // if upper64 > divisor, goto L2 BHI L2 BLO L3 CMP R4,R2 BLO L3 L2: SUBS R4,R4,R2 // upper64 -= divisor SBC R5,R5,R3 ORR R0,R0,1 // lower64 ¦= 1 L3: ADD R12,R12,1 // k++ B L1 // repeat L4: POP {R4,R5} BX LR // Return (quotient in lower64) .end
Q32÷Q32 DIVISION
Assembly for unsigned 128 ÷ 64