## Slide 1: Chapter 11
Multimedia Processing

## Slide 2: Multimedia Data
Massive Amounts of Data
  One 1280x1024 color Image: 4 MBytes
  One minute of CD quality stereo: 11 MBytes
  One minute of HD video: 14 GBytes
High Data Rates
  Audio: 44,100 16-bit stereo samples/sec
  = 1.4 Mbits/sec (11.4
  Video: 60 1280x1024 color frames/sec
  = 236 Mbits/sec (

## Slide 3: Multimedia Data
Audio, Images, Graphics, Animation, Video
  Scalar Arithmetic used to increase volume, intensity, contrast, etc.
  Vector Arithmetic (e.g., dot product) used in computer graphics
  Matrix arithmetic used to compute perspective projections
  Audio, Images, Video: Must prevent (rather than detect) overflow
Efficient Processing
  Simple arithmetic operations repeated millions of times
  Basic operations must be made efficient
  Instructions must operate on multiple data simultaneously

## Slide 4: Multimedia Data Representation
255 (white)
0 (black)
0 (black)
0
0
0
255
255
255
+32767
-32768
0
8-bit mono-chrome images
24-bit
(3x8-bit) color images
16-bit audio channel

## Slide 5: Parallel Processing: SIMD (Single Instruction, Multiple Data)
Each SIMD instruction performs arithmetic on multiple integers simultaneously:
Four 8-bit integers
  or
Two 16-bit integers
31 | 24 | 23 | 16 | 15 | 8 | 7 | 0
31 | 16 | 15 | 0
SIMD processing offers 2x to 4x improvement in processing speed.

## Slide 6: Simple SIMD: B&W Negative (1 pixel = 1 byte)
// void SIMD_Invert(uint8_t src[], uint8_t dst[], uint32_t count) ;
  .global SIMD_Invert
SIMD_Invert:
loop: CBZ R2,done // test for completion (count = 0)
  LDR R3,[R0],4 // Get next four bytes, bump adrs
  MVN R3,R3 // Invert all four values
  STR R3,[R1],4 // Store all four values, bump adrs
  SUB R2,R2,4 // decrement the count by 4
  B loop // repeat until done
done: BX LR // return
31 | 24 | 23 | 16 | 15 | 8 | 7 | 0
00001111 |  | 01010101 |  | 11001100 |  | 00000000 | 
31 | 24 | 23 | 16 | 15 | 8 | 7 | 0
11110000 |  | 10101010 |  | 00110011 |  | 11111111 | 

## Slide 7: SIMD Subtraction
Operation | Ops | Format |  | GE[3] | GE[2] | GE[1] | GE[0]
Signed Subtraction | 4x8 | SSUB8 | Rd,Rn,Rm | Rn31..24 ≥ Rm31..24 | Rn23..16 ≥ Rm23..16 | Rn15..8 ≥ Rm15..8 | Rn7..0 ≥ Rm7..0
Unsigned Subtraction | 4x8 | USUB8 | Rd,Rn,Rm |  |  |  | 
Signed Subtraction | 2x16 | SSUB16 | Rd,Rn,Rm | Rn31..16 ≥ Rm31..16 |  | Rn15..0 ≥ Rm15..0 | 
Unsigned Subtraction | 2x16 | USUB16 | Rd,Rn,Rm |  |  |  | 
None of these instructions affect the N, C, Z, V or Q flags. |  |  |  |  |  |  | 
SIMD Selection |  |  |  |  |  |  | 
Operation | Ops | Format |  | GE[3] | GE[2] | GE[1] | GE[0]
Select Bytes | 4x8 | SEL | Rd,Rn,Rm | 1: Rn31..24 0: Rm31..24 | 1: Rn23..16 0: Rm23..16 | 1: Rn15..8 0: Rm15..8 | 1: Rn7..0 0: Rm7..0
31 | 30 | 29 | 28 | 27 |  | 19 | 18 | 17 | 16 |  | 0
N | C | Z | V | Q | . . . | GE [3] | GE [2] | GE [1] | GE [0] | . . . | 
But they do affect the GE (Greater than or Equal) flags:
31 | 30 | 29 | 28 | 27 |  |  |  |  |  |  | 0
N | C | Z | V | Q | . . . |  |  |  |  |  | 

## Slide 8: SIMD Compare and Select
31 | 24 | 23 | 16 | 15 | 8 | 7 | 0
7 |  | 15 |  | 9 |  | 3 | 
31 | 24 | 23 | 16 | 15 | 8 | 7 | 0
12 |  | 8 |  | 32 |  | 51 | 
31 | 24 | 23 | 16 | 15 | 8 | 7 | 0
12 |  | 8 |  | 32 |  | 51 | 
31 | 24 | 23 | 16 | 15 | 8 | 7 | 0
7 |  | 15 |  | 9 |  | 3 | 
─
─
─
─
GE[3] = 1 (12 ≥ 7) | GE[2] = 0 (8 < 15) | GE[1] = (32 ≥ 9) | GE[0] = 1 (51 ≥ 3)
GE[3] = 1 | GE[2] = 0 | GE[1] = 1 | GE[0] = 1
31 | 24 | 23 | 16 | 15 | 8 | 7 | 0
12 |  | 15 |  | 32 |  | 51 | 
Step 1: SIMD Subtract
Step 2: SIMD Select
Reverse the operands to select the minimums

## Slide 9: Finding Maximums
12 | 129 | 32 | 113
15 | 8 | 48 | 51
5 | 223 | 207 | 35
59 | 37 | 219 | 29
3 | 27 | 75 | 93
0 | 0 | 0 | 0
SEL R1,R0,R1
SSUB8 R12,R0,R1
R1
R0
R0
R0
R0
R0
1 | 1 | 1 | 1
GE Flags
SSUB8 R12,R0,R1
SSUB8 R12,R0,R1
SSUB8 R12,R0,R1
SSUB8 R12,R0,R1
3 | 27 | 75 | 93
1 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
0 | 0 | 0 | 1
3 | 27 | 75 | 93
15 | 8 | 48 | 51
15 | 27 | 75 | 93
5 | 223 | 207 | 35
15 | 223 | 207 | 93
59 | 37 | 219 | 29
59 | 223 | 219 | 93
12 | 129 | 32 | 113
59 | 223 | 219 | 113

## Slide 10: Searching for Minimum Integer in an Array
// int32_t SIMD_Find4Mins(int8_t a[], int32_t n) ;
.global SIMD_Find4Mins
SIMD_Find4Mins:
LDR R2,[R0],4 // Load initial minimums
loop: SUBS R1,R1,4 // Decrement count, bump adrs
BEQ done // Test for completion
LDR R3,[R0],4 // Get next group of 4 bytes
SSUB8 R12,R3,R2 // Compare to minimums
SEL R2,R2,R3 // Select the minimums
B loop // Repeat
done: MOV R0,R2 // Copy minimums to R0
BX LR // Return
a[3] | a[2] | a[1] | a[0]
a[7] | a[6] | a[5] | a[4]
a[n-1] | a[n-2] | a[n-3] | a[n-4]
min3 | min2 | min1 | min0
Input to function SIMD_Find4Mins
(array of bytes)
32-bits returned by the function
The smallest integer will be the smallest of the four that are returned.

## Slide 11: SIMD Addition
Operation | Ops | Format |  | GE[3] | GE[2] | GE[1] | GE[0]
Signed Addition | 4x8 | SADD8 | Rd,Rn,Rm | Rn31..24 + Rm31..24 ≥ 0 | Rn23..16 + Rm23..16 ≥ 0 | Rn15..8 + Rm15..8 ≥ 0 | Rn7..0 + Rm7..0 ≥ 0
Unsigned Addition | 4x8 | UADD8 | Rd,Rn,Rm | Rn31..24 + Rm31..24 ≥ 28 | Rn23..16 + Rm23..16 ≥ 28 | Rn15..8 + Rm15..8 ≥ 28 | Rn7..0 + Rm7..0 ≥ 28
Signed Addition | 2x16 | SADD16 | Rd,Rn,Rm | Rn31..16 + Rm31..16 ≥ 0 |  | Rn15..0 + Rm15..0 ≥ 0 | 
Unsigned Addition | 2x16 | UADD16 | Rd,Rn,Rm | Rn31..16 + Rm31..16 ≥ 216 |  | Rn15..0 + Rm15..0 ≥ 216 | 
None of these instructions affect the N, C, Z, V or Q flags. |  |  |  |  |  |  | 
  Signed: GE=1 => Sum ≥ 0 (may or may not have had an overflow)
Unsigned: GE=1 => Overflow
GE flags more useful with SIMD subtraction than SIMD addition!

## Slide 12: SIMD Multiplication
Instruction | Format |  | Operation | Notes
Signed Dual Multiply Add or Subtract | SMUAD{X} | Rd,Rn,Rm | Rd (Rn 15..0 Rm 15..0) (Rn31..16 Rm 31..16) | 1,2,3
 | SMUSD{X} | Rd,Rn,Rm | Rd (Rn 15..0 Rm 15..0) (Rn31..16 Rm 31..16) | 1,2,3
Signed Multiply Accumulate or Subtract Dual | SMLAD{X} | Rd,Rn,Rm,Ra | Rd Ra (Rn 15..0 Rm 15..0) (Rn 31..16 Rm 31..16) | 1,2,3
 | SMLSD{X} | Rd,Rn,Rm,Ra | Rd Ra (Rn 15..0 Rm 15..0) (Rn 31..16 Rm 31..16) | 1,2,3
Signed Multiply Accumulate or Subtract Long Dual | SMLALD{X} | Rdlo,Rdhi,Rn,Rm | Rdhi.Rdlo | 1,3
 | SMLSLD{X} | Rdlo,Rdhi,Rn,Rm | Rdhi.Rdlo | 1,3
Instruction | Format |  | Operation | Notes
Signed Dual Multiply Add or Subtract | SMUAD{X} | Rd,Rn,Rm |  | 1,2,3
 | SMUSD{X} | Rd,Rn,Rm |  | 1,2,3
Signed Multiply Accumulate or Subtract Dual | SMLAD{X} | Rd,Rn,Rm,Ra |  | 1,2,3
 | SMLSD{X} | Rd,Rn,Rm,Ra |  | 1,2,3
Signed Multiply Accumulate or Subtract Long Dual | SMLALD{X} | Rdlo,Rdhi,Rn,Rm |  | 1,3
 | SMLSLD{X} | Rdlo,Rdhi,Rn,Rm |  | 1,3
Notes:
Appending "X" to mnemonic changes operands to (×
Sets the Q flag if an addition or subtraction results in overflow, but does not saturate.
None of these instructions affect the N, C, Z or V flags.

## Slide 13: SMUAD R0,R1,R2
31 | 16 | 15 | 0
31 | 16 | 15 | 0
31 |  |  | 0
31 |  |  | 0
R1
R2
R0
+
31 | 16 | 15 | 0
31 | 16 | 15 | 0

## Slide 14: SIMD Integer Dot Product
[n-2] | [n-1]
[n-2] | [n-1]
× | 
× | 
× | ×
× | ×
× | ×
[0] | [1]
[2] | [3]
[2] | [3]
[0] | [1]
SMLAD
// int32_t SIMD_DotProduct
// (int16_t a[], int16_t b[], uint32_t n);
  .global SIMD_DotProduct
SIMD_DotProduct:
PUSH {R4} // Preserve registers R4
  LDR R3,=0 // Initialize the result
loop: CBZ R2,done // Test for completion (n = 0)
  LDR R4,[R0],4 // Get two 16-bit values from a
  LDR R12,[R1],4 // Get two 16-bit values from b
  SMLAD R3,R4,R12,R3 // Add 32-bit product to total
  SUB R2,R2,2 // Decrement n by 2
  B loop // Repeat until done
done: MOV R0,R3 // Copy result to R0 for return
POP {R4} // Restore registers R4
BX LR // Return
The Dot Product is used extensively in computer graphics, such as finding the angle between two vectors or the projection of one vector onto another.

## Slide 15
  // void SIMD_FIR(Q15 g[], Q15 y[], uint32_t length, Q15 f[4]]) ;
  .global SIMD_FIR
  SIMD_FIR: // Require: |sum of f[i]| < 1.0
  PUSH {R4-R6} // Preserve registers
  LDRD R5,R4,[R3] // Get the four f coefficients
  ROR R5,R5,16 // R5<31..16>=f[0]; R5<15..0>=f[1]
  ROR R4,R4,16 // R4<31..16>=f[2]; R4<15..0>=f[3]
  MOV R6,0 // Begin w/three 0’s prepended to g:
  LDRH R12,[R0] // g[-3] thru g[-1] = 0, and
  LSL R12,R12,16 // g[0] loaded from input.
  loop: CBZ R2,done // Test for completion (length = 0)
  SMUAD R3,R4,R6 // R3 = f[0]*g[i] + f[1]*g[i-1]
  SMLAD R3,R5,R12,R3 // + f[2]*g[i-2] + f[3]*g[i-3]
  LSR R3,R3,15 // Select Q1.15 format bits
  STRH R3,[R1],2 // Store filtered result (y[i])
  LSR R6,R6,16 // Shift the input samples by 1:
  ORR R6,R6,R12,LSL 16 // R6 = 2nd and 3rd input sample
  LSR R7,R12,16 // R12 = 4th input sample
  LDRH R3,[R0],2 // R3 = 5th input sample, i++
  ORR R7,R12,R3,LSL 16 // R12 = 4th and 5th input sample
  SUB R2,R2,1 // Decrement length
  B loop // Repeat
  done: POP {R4-R6} // Restore registers
  BX LR // Return
SMUAD
SMLAD
SIMD Finite Impulse Filter
Finite Impulse Filters are used in signal processing to implement almost any sort of frequency response, such as removing high frequency noise.

## Slide 16: SATURATION (LIMITING) INSTRUCTIONS
Instruction | Format |  | Operation
Signed Saturate | SSAT | Rd,n,Op2 | Rd ─1 Op2 = Rm or Rm,ASR # or Rm,LSL #
Unsigned Saturate | USAT | Rd,n,Op2 | Rd 1 Op2 = Rm or Rm,ASR # or Rm,LSL #
Instruction | Format |  | Operation
Signed Saturate | SSAT | Rd,n,Op2 | 
Unsigned Saturate | USAT | Rd,n,Op2 | 
Given a value, these instructions limit it to the range of an N-bit representation.
LDRB R0,rgb_red // This code doubles the intensity of the
USAT R0,8,R0,LSL 1 // 8-bit red RGB component of a pixel, and
STRB R0,rgb_red // limits the result to avoid overflow.
The Q flag is set when saturation occurs; no other flags are affected.
Yes
Yes
SSAT: min =
USAT: min = 0
SSAT: max =
USAT: max = 1

## Slide 17
Instruction | Format |  | Operation | Operands
Signed Saturating Add | QADD QADD8 QADD16 | Rd,Rn,Rm Rd,Rn,Rm Rd,Rn,Rm | Rd 1 Rd 1 Rd 1 | 1×32 4×8 2×16
Signed Saturating Subtract | QSUB QSUB8 QSUB16 | Rd,Rn,Rm Rd,Rn,Rm Rd,Rn,Rm | Rd 1 Rd 1 Rd 1 | 1×32 4×8 2×16
Unsigned Saturating Add | UQADD8 UQADD16 | Rd,Rn,Rm Rd,Rn,Rm | Rd 1 Rd 1 | 4×8 2×16
Unsigned Saturating Subtract | UQSUB8 UQSUB16 | Rd,Rn,Rm Rd,Rn,Rm | Rd 1 Rd 1 | 4×8 2×16
Instruction | Format |  | Operation | Operands
Signed Saturating Add | QADD QADD8 QADD16 | Rd,Rn,Rm Rd,Rn,Rm Rd,Rn,Rm |  | 1×32 4×8 2×16
Signed Saturating Subtract | QSUB QSUB8 QSUB16 | Rd,Rn,Rm Rd,Rn,Rm Rd,Rn,Rm |  | 1×32 4×8 2×16
Unsigned Saturating Add | UQADD8 UQADD16 | Rd,Rn,Rm Rd,Rn,Rm |  | 4×8 2×16
Unsigned Saturating Subtract | UQSUB8 UQSUB16 | Rd,Rn,Rm Rd,Rn,Rm |  | 4×8 2×16
SATURATING ARITHMETIC
Each instruction works on a single 32-bit value, two 16-bit values, or four 8-bit values all at once. The Q flag is set when saturation occurs; no other flags are affected.
For example, these instructions are used to process video (three 8-bit RGB values/pixel)

## Slide 18: UQADD8 R0,R1,R2
31 | 24 | 23 | 16 | 15 | 8 | 7 | 0
100 |  | 135 |  | 221 |  | 97 | 
31 | 24 | 23 | 16 | 15 | 8 | 7 | 0
200 |  | 235 |  | 255 |  | 197 | 
+
+
+
+
31 | 24 | 23 | 16 | 15 | 8 | 7 | 0
100 |  | 100 |  | 100 |  | 100 | 
<= 255
<= 255
<= 255
<= 255
200
235
321
197
R1
R2
R0
UQADD8 is used to simultaneously increase the brightness of four RGB components of a digital image without overflow.

## Slide 19: The Q Flag (bit 27 in the APSR)
The Q flag is a “Dual-Purpose” flag:
Set when SIMD multiply instructions overflow the product
Set when saturating instructions limit their result
The Q flag is a “Sticky” flag:
SIMD & saturating instructions can set Q to 1, but not clear it.
Only way to clear Q is to use MRS and MSR instructions.
There is no condition code or conditional branch that tests the Q flag!

## Slide 20
Instruction | Format |  | Operation
Move (copy) the contents of a general-purpose register into the APSR flags. | MSR | APSR_nzcvq,Rn | NZCVQ  Rn (bits 31-27) (Bits 26-0 of PSR are unaffected)
Move (copy) the contents of the APSR into a general-purpose register. | MRS | Rd,APSR | NZCVQ  Rd (bits 31-27) (Bits 26-0 of Rd are filled with 0’s)
Copying flags to/from Registers
// Clearing the Q flag:
MRS R0,APSR // Copy flags to R0
BIC R0,R0,1<<27 // Clear Q flag to 0
MSR APSR_nzcvq,R0 // Copy R0 to flags
// Testing the Q flag:
MRS R0,APSR // Copy flags to R0
TST R0,1<<27 // Check value of Q
BNE QFlagSet // Branch if Q=1