## Slide 1: Chapter 4
Copying Data

## Slide 2: LOAD/STORE ARCHITECTURE
Main Memory
Registers
Arithmetic & Logice Unit (ALU)
All computations (add, subtract, etc.) are performed in the ALU.
Instruction operands and results are held in registers.
But Variables reside in main memory.
“Load”: Copy a variable from memory into a register to use its value.
“Store”: Copy a variable from a register back into memory to change its value.

## Slide 3: INSTRUCTIONS FOR COPYING DATA
constant
  Constant to Register:
  MOV, MVN, MOVW, MOVT, LDR*
  “Load Register” Instructions:
  LDR, LDRD, LDRB, LDRH, LDRSB, LDRSH
Register to Register: MOV
  “Store Register” Instructions:
  STR, STRD, STRB, STRH
Main Memory
Registers

## Slide 4: REGISTER  CONSTANT
MOV R0,100 // R0  100
MVN R0,100 // R0  ~100 (-101)
MOV R0,-100 // R0  -100
// Assembler replaces this by MVN R0,99
MOVW R0,1000 // R0  1000
MOVW R0,100000 & 0xFFFF // LS 16 bits
MOVT R0,100000 >> 16 // MS 16 bits
Limited to an 8-bit pattern, anywhere within 32 bits
16-bit unsigned integers
An arbitrary 32-bit constant

## Slide 5: The LDR Pseudo-Instruction
Format: LDR Rd,=constant
Instruction Format |  | Width | Flags
MOV | Rd,imm12 | 32 | 
MOVS | Rd,imm8 | 16 | NZ
MOVW | Rd,imm16 | 32 | 
MVN | Rd,imm12 | 32 | 
The equals sign distinguishes this pseudo-instruction from a real LDR instruction.
The pseudo-instruction is replaced by one of the following if possible, else it is replaced by a real LDR that loads the constant from memory:
The 32-bit MOV is used inside an IT block (Chapter 6)
A “pseudo-instruction” is not a real ARM instruction. When used, the assembler replaces it with an equivalent operation using a real instruction.

## Slide 6: WRITING INTEGER CONSTANTS
Decimal: 123
Binary: 0b10110111
Octal: 0123
Hexadecimal: 0xFACE
ASCII Character 'a'
  (8 bits)

## Slide 7: REGISTER  MEMORY (32-BITS) Load Register with Word
LDR R0,word32 // Copies the value // held in the 32-bit // memory location // labeled "word32" // into register R0. | 
word32
register R0
  Used with data of type int32_t, uint32_t, and all pointers

## Slide 8: REGISTER PAIR  MEMORY (64-BITS) Load Register with DoubleWord
LDRD R0,R1,dword64 // Copies the lower // half of the value // held in the 64-bit // memory location // labeled "dword64" // into register R0, // and the upper half // into R1. | 
dword64 (bits 32-63)
register R1
dword64 (bits 0-31)
register R0
  Used with data of type int64_t and uint64_t
&dword64 + 4
&dword64
  The 64-bit operand must be word aligned (located at a mod 4 adrs) or an address fault will occur.

## Slide 9: Copying variables < 32 bits wide (32-bit register copy must have same value)
Unsigned
Signed (2’s complement)

## Slide 10: REGISTER  MEMORY (8-BITS UNSIGNED) Load Register with (Unsigned) Byte
LDRB R0,ubyte8 // Copies the unsigned // value held in the // 8-bit memory location // labeled "ubyte8" into // bits 0-7 of register // R0 and 0’s into bits // 8-31. | 
ubyte8
register R0
24 zeroes
  Used with data of type uint8_t

## Slide 11: REGISTER  MEMORY (16-BITS UNSIGNED) Load Register with (Unsigned) HalfWord
LDRH R0,uhalf16 // Copies the unsigned // value held in the // 16-bit memory location // labeled "uhalf16" into // bits 0-15 of register // R0 and 0’s into bits // 16-31. | 
uhalf16
register R0
16 zeroes
  Used with data of type uint16_t

## Slide 12: REGISTER  MEMORY (8-BITS SIGNED) Load Register with Signed Byte
LDRSB R0,sbyte8 // Copies the signed // value held in the // 8-bit memory location // labeled "sbyte8" // into bits 0-7 of // register R0 and 24 // copies of bit 7 of // sbyte8 into bits 8-31. | 
sbyte8
register R0
24 copies of bit 7
  Used with data of type int8_t

## Slide 13: REGISTER  MEMORY (16-BITS SIGNED) Load Register with Signed HalfWord
LDRSH R0,shalf16 // Copies the signed // value held in the // 16-bit memory // location labeled // "shalf16" into bits // 0-15 of R0 and 16 // copies of bit 15 of // shalf16 into bits // 16-31. | 
shalf16
register R0
16 copies of bit 15
  Used with data of type int16_t

## Slide 14: REGISTER  REGISTER Move Instruction
MOV R0,R1
// Copies all 32 bits
// of the value held
// in register R1 into
// the register R0
register R0
register R1

## Slide 15: REGISTER  MEMORY (32-BITS) Store Register (to) Word
STR R0,word32
// Copies all 32 bits
// of the value held
// in register R0 into
// the 32-bit memory
// location labeled
// "word32".
word32
register R0
  Used with data of type int32_t, uint32_t, and all pointers

## Slide 16: REGISTER PAIR MEMORY (64-BITS) Store Register (to) DoubleWord
STRD R0,R1,dword64
// Copies the contents
// of register R0 into
// the lower half, and
// register R1 into the
// upper half, of the
// 64-bit memory location
// labeled "dword64".
register R1
dword64 (bits 32-63)
register R0
dword64 (bits 0-31)
  Used with data of type int64_t and uint64_t
&dword64 + 4
&dword64
  The 64-bit operand must be word aligned (located at a mod 4 adrs) or an address fault will occur.

## Slide 17: REGISTER  MEMORY (8-BITS) Store Register (to) Byte
STRB R0,byte8
// Copies bits 0-7 of
// the value held in
// register R0 into
// the 8-bit memory
// location labeled
// "byte8".
register R0
byte8
Register bits 8-31 are not copied.
  Used with data of type int8_t and uint8_t

## Slide 18: REGISTER  MEMORY (16-BITS) Store Register (to) HalfWord
STRH R0,half16
// Copies bits 0-15
// of the value held
// in register R0
// into the 16-bit
// memory location
// labeled "half16".
register R0
Register bits 16-31 are not copied.
half16
  Used with data of type int16_t and uint16_t

## Slide 19: Variable Y  Variable X (32 bits) Common Coding Mistake
LDR R0,x
LDR R1,y
MOV R1,R0
  The second LDR instruction doesn’t move Y into R1, it merely makes a copy of its value. Thus the MOV doesn’t change Y, it only changes the copy in R1.
Register R1
Register R0
?
?
x (in memory)
y (in memory)
1000
?
?
?
1000
1000
?
?
1000
1000
1000
1000
?
1000

## Slide 20: Variable Y  Variable X (32 bits) Correct Coding Solution
Register R0
x (in memory)
y (in memory)
?
1000
?
LDR R0,x
STR R0,y
1000
1000
?
1000
1000
1000

## Slide 21: DATA COPYING INSTRUCTIONS
32-bit register(s)
int_32, uint_32, pointer
int_64, uint_64
uint_8
int_8
LDRB/STRB
LDRSB/STRB
LDRH/STRH
LDRSH/STRH
LDR/STR
LDRD/STRD
int_16
uint_16
  Pointers are always 32 bits wide. Copy with LDR and STR.

## Slide 22: EXAMPLES OF COPYING DATA
Source | 8-bit destination | 16-bit destination | 32-bit destination | 64-bit destination
Constant | LDR R0,=5 STRB R0,dst8 | LDR R0,=5 STRH R0,dst16 | LDR R0,=5 STR R0,dst32 | LDR R0,=5 LDR1 R1,=0 STRD R0,R1,dst64
8-bit Variable | LDRB R0,src8 STRB R0,dst8 | LDRB2 R0,src8 STRH R0,dst16 | LDRB2 R0,src8 STR R0,dst32 | LDRB2 R0,src8 LDR3 R1,=0 STRD R0,R1,dst64
16-bit Variable | LDRB R0,src16 STRB R0,dst8 | LDRH R0,src16 STRH R0,dst16 | LDRH4 R0,src16 STR R0,dst32 | LDRH4 R0,src16 LDR3 R1,=0 STRD R0,R1,dst64
32-bit Variable | LDRB R0,src32 STRB R0,dst8 | LDRH R0,src32 STRH R0,dst16 | LDR R0,src32 STR R0,dst32 | LDR R0,src32 LDR3 R1,=0 STRD R0,R1,dst64
64-bit Variable | LDRB R0,src64 STRB R0,dst8 | LDRH R0,src64 STRH R0,dst16 | LDR R0,src64 STR R0,dst32 | LDRD R0,R1,src64 STRD R0,R1,dst64
1 Replace with LDR R1,=-1 if source operand is a negative constant.
2 Replace with LDRSB if source operand is signed.
3 Replace with ASR R1,R0,31 if source operand is signed.
4 Replace with LDRSH if source operand is signed.

## Slide 23: Determining an Operand Address
2496 | x
Address of x is a constant, determined before execution
LDR R0,x // To the assembler, the symbol
// “x” represents the address
// of the variable. The address
// is a constant, determined
// before execution begins.
15 | 11 | 10 | 8 | 7 | 0
01001 |  | 000 |  | Displacement constant | 
LDR (PC-relative) |  | R0 |  | Address of x (distance from instruction) | 

## Slide 24: Determining an Operand Address
p
*p
Address of *p must be computed at run-time.
LDR R0,p // R0  p (adrs of *p)
LDR R1,[R0] // R1  *p
15 | 11 | 10 | 6 | 5 | 3 | 2 | 0
01101 |  | 00000 |  | 000 |  | 001 | 
LDR (imm. offset) |  | Offset |  | R0 |  | R1 | 

## Slide 25: Determining an Operand Address
Address of a[2] is a constant, determined before execution.
2488 | a[3]
2484 | a[2]
2480 | a[1]
2476 | a[0]
Address of a[k] must be computed at run-time.
ADR R0,a // R0  &a[0] (a constant)
LDR R1,k // R1  k
LDR R2,[R0,R1,LSL 2]
LDR R0,a+8 // R0  &a[2] (a constant)
15 | 11 | 10 | 8 | 7 | 0
01001 |  | 000 |  | Displacement constant | 
LDR (PC-relative) |  | R0 |  | Address of a[2] (Distance from instruction) | 
31 |  |  |  |  |  |  |  |  |  |  | 20 | 19 |  |  | 16 | 15 |  |  | 12 | 11 |  |  |  |  | 6 | 5 | 4 | 3 |  |  | 0
111110000101 |  |  |  |  |  |  |  |  |  |  |  | 0000 |  |  |  | 0010 |  |  |  | 000000 |  |  |  |  |  | 10 |  | 0001 |  |  | 
LDR (Register Offset Mode) |  |  |  |  |  |  |  |  |  |  |  | R0 |  |  |  | R2 |  |  |  |  |  |  |  |  |  | LSL 2 |  | R1 |  |  | 

## Slide 26: ADDRESSING MODES (Calculating a Memory Address)
Immediate Offset Mode:
  [R0]
  [R0,4]
Register Offset Mode:
  [R0,R1]
  [R0,R1,LSL 2]
Pre-Indexed Mode:
  [R0,4]!
Post-Indexed Mode:
  [R0],4
Use these in loops to reduce the number of instructions.
1. R0  R0 + 4
2. R0 provides address
1. R0 provides address
2. R0  R0 + 4

## Slide 27: Review: Pointer Arithmetic
int16_t a16[5] ;
a16[4] |  | a16[3] |  | a16[2] |  | a16[1] |  | a16[0] | 
1009 | 1008 | 1007 | 1006 | 1005 | 1004 | 1003 | 1002 | 1001 | 1000
p16 |  |  | 
2003 | 2002 | 2001 | 2000
p16 |  |  | 
1000 |  |  | 
2003 | 2002 | 2001 | 2000
p16 |  |  | 
1002 |  |  | 
2003 | 2002 | 2001 | 2000
int16_t *p16 ;
p16 = &a16[0] ;
p16 = p16 + 1 ;
Note: Each member of the array is an object consisting of 2 bytes.
A pointer holds a 32-bit address; thus all pointers are 32 bits wide.
The data type (int16_t) used to declare the pointer refers to the size of the objects that it points to.
Adding 1 to a pointer causes it to point to the next object. Since each object is 2 bytes, this must increase the address by 2.

## Slide 28: IMMEDIATE OFFSET MODE
Syntax | Address | Examples
[Rn{,constant}] | Rn + constant | [R5,100] [R5]
Rn
+
constant
Instruction Register
Immediate Offset Address

## Slide 29: IMMEDIATE OFFSET: POINTERS & ARRAYS
Function in C | Function in assembly
void f1(int32_t *p32) { *p32 = 0 ; *(p32 + 1) = 0 ; } | f1: LDR R1,=0 // R1 <-- 0 STR R1,[R0] // R1 --> memory[R0] STR R1,[R0,4] // R1 --> memory[R0+4] BX LR // return
Function in C | Function in assembly
void f2(int32_t a32[]) { a32[0] = 0 ; a32[1] = 0 ; } | f2: LDR R1,=0 STR R1,[R0] STR R1,[R0,4] BX LR
  Array and pointer parameters are treated the same
  Pointer arithmetic! Adding 1 to p32 adds 4 to address.

## Slide 30: REGISTER OFFSET MODE
Syntax | Address | Example
[Rn,Rm] | Rn + Rm | [R4,R5]
[Rn,Rm,LSL constant] | Rn + (Rm << constant) | [R4,R5,LSL 2]
Rm
Rn
+
left shifter
z
constant
Instruction Register
Register Offset
Address
(#bits to shift left)

## Slide 31: ADR versus LDR
LDR R0,operand ; LDR copies the contents of a memory
; operand (i.e., a variable) into a register.
ADR R0,operand ; ADR copies the address of a memory
; operand (i.e., a constant) into a register.
Function call in C | Code produced by the compiler
void f1(int32_t *) ; int32_t s32 ; ● ● ● f1(&s32) ; ● ● ● | ● ● ● ADR R0,s32 // load R0 with &s32 BL f1 // call function f1 ● ● ●

## Slide 32: Subscripting: a16[k] = 0
a16[6] |  |  | 1252
a16[5] |  |  | 1250
a16[4] |  |  | 1248
a16[3] |  |  | 1246
a16[2] |  |  | 1244
a16[1] |  |  | 1242
a16[0] |  |  | 1240
1240
+
3 (k)
Instruction Register
R2 (subscript)
LDRH R0,[R1,R2,LSL 1]
Shifter
R1 (starting address)
LDR R0,=0 // R0  0 (data)
ADR R1,a16 // R1  starting address of array
LDR R2,k // R2  subscript (k=3)
STRH R0,[R1,R2,LSL 1] // R0  a16[k]
R0 (data)
0
#bits to shift left = 1 (2 x R2)

## Slide 33: REGISTER OFFSET: POINTERS & ARRAYS
Function in C | Function in assembly
void f1(int8_t *p8, int16_t *p16, int32_t k32) { *(p8 + k32) = 0 ; *(p16 + k32) = 0 ; } | f1: LDR R3,=0 STRB R3,[R0,R2] STRH R3,[R1,R2,LSL 1] BX LR
Function in C | Function in assembly
void f2(int8_t a8[], int16_t a16[], int32_t k32) { a8[k32] = 0 ; a16[k32] = 0 ; } | f2: LDR R3,=0 STRB R3,[R0,R2] STRH R3,[R1,R2,LSL 1] BX LR
  Pointer arithmetic!
  R2,LSL 1 = 2*k32.

## Slide 34
s.x32
s.z64 (bits 63..32)
s.z64 (bits 31..0)
not used
s.y16
1000 – 1003
1004 – 1007
1008 – 100B
100C – 100F
Addresses
4 bytes (32 bits)
struct
{
uint32_t x32 ; // 4 bytes
uint16_t y16 ; // 2 bytes
uint64_t z64 ; // 8 bytes
} s ;
POINTERS AND STRUCTURES
To optimize speed, C places each member of a structure in memory so that it can be retrieved using the minimum number of memory accesses:
16-bit data is placed on an even (mod 2) address.
32 and 64-bit data is placed on a mod 4 address.
So even though this structure only contains 14 bytes of data, it occupies 16 bytes of memory.

## Slide 35
#pragma pack(1)
struct
{
uint16_t a16 ; // 2 bytes uint32_t b32 ; // 4 bytes
uint16_t c16 ; // 2 bytes
uint32_t d32 ; // 4 bytes
} s2 ;
#pragma pack()
POINTERS AND STRUCTURES
struct
{
uint16_t a16 ; // 2 bytes uint32_t b32 ; // 4 bytes
uint16_t c16 ; // 2 bytes
uint32_t d32 ; // 4 bytes
} s1 ;
unused
s1.b32
s1.a16
s1.d32
s1.c16
1000 – 1003
1004 – 1007
1008 – 100B
100C – 100F
Addresses
4 bytes (32 bits)
unused
s1.c16
s1.b3231..16
s1.a16
s1.d32
1000 – 1003
1004 – 1007
1008 – 100B
Addresses
4 bytes (32 bits)
s1.b3215..0
Optimized for speed (default)
Optimized to conserve memory

## Slide 36
Function Call in C | Accessing s2.d32
#pragma pack(1) struct { uint16_t a16 ; uint32_t b32 ; uint16_t c16 ; uint32_t d32 ; } s2 ; #pragma pack() f(&s2) ; | f: // R0 = &s2 ... // R1 = s2->d32 LDR R1,[R0,8] … BX LR
POINTERS AND STRUCTURES
Function Call in C | Accessing s1.d32
struct { uint16_t a16 ; uint32_t b32 ; uint16_t c16 ; uint32_t d32 ; } s1 ; f(&s1) ; | f: // R0 = &s1 ... // R1 = s1->d32 LDR R1,[R0,12] … BX LR

## Slide 37
Note:
8 and 16-bit ints are promoted to native CPU word size before use in expressions, thus…
Functions receive 8 and 16-bit parameters as 32-bit ints on our processor (Cortex-M4F).
// R0 = s8 (sign-extended to 32-bits)
f1: ADD R0,R0,1 // R0 = s8 + 1
BX LR
int32_t f1(int8_t s8)
{
return s8 + 1 ;
}

## Slide 38
int32_t f2(int8_t *ps8)
{
return *ps8 + 1 ;
}
// R0 = ps8 (a 32-bit ptr to int8_t)
f2: LDRSB R0,[R0] // R0 = *ps8
ADD R0,R0,1 // R0 = *ps8 + 1
BX LR

## Slide 39
int32_t f3(int16_t *ps16)
{
return *(ps16 + 1) ;
}
// R0 = ps16 (a 32-bit ptr to int16_t)
f3: ADD R0,R0,2 // R0 = ps16 + 1
LDRSH R0,[R0] // R0 = *(ps16 + 1)
BX LR
f3: LDRSH R0,[R0,2]
BX LR

## Slide 40
int32_t f4(int32_t a32[])
{
return a32[1] ;
}
// R0 = a32 (a 32-bit ptr to int32_t)
f4: ADD R0,R0,4 // R0 = a32 + 1
LDR R0,[R0] // R0 = a32[1]
BX LR
f4: LDR R0,[R0,4]
BX LR

## Slide 41
int32_t f5(int32_t a32[], int32_t k32)
{
return a32[k32] ;
}
// R0 = a32 (a 32-bit ptr to int32_t)
// R1 = k32 (a 32-bit int)
f5: LSL R1,R1,2 // R1 = k32 (scaled)
ADD R0,R0,R1 // R0 = a32 + k32
LDR R0,[R1] // R0 = a32[k32]
BX LR
f5: LDR R0,[R0,R1,LSL 2]
BX LR

## Slide 42
int32_t f6(int32_t a32[], int32_t k32)
{
return (a32+k32)[0] ;
}
int32_t f6(int32_t a32[], int32_t k32)
{
return *(a32+k32) ;
}
// R0 = a32 (a 32-bit ptr to int32_t)
// R1 = k32 (a 32-bit int)
f6: LSL R1,R1,2 // R1 = k32 (scaled)
ADD R0,R0,R1 // R0 = a32 + k32
LDR R0,[R1] // R0 = *(a32 + k32)
BX LR // R0 = (a32+k32)[0]
f6: LDR R0,[R0,R1,LSL 2]
BX LR

## Slide 43
int16_t *f7(int16_t *ps16)
{
return ps16 + 1 ;
}
// R0 = ps16 (a 32-bit ptr to int16_t)
f7: ADD R0,R0,2 // R0 = ps16 + 1
BX LR

## Slide 44
Note:
pps16 is a pointer to a pointer to an int16_t.
*pps16 is a pointer to an int16_t.
**pps16 is an int16_t
// R0 = pps16 (a 32-bit ptr to int16_t *)
f8: LDR R0,[R0] // R0 = *pps16
LDRSH R0,[R0] // R0 = **pps16
BX LR
int32_t f8(int16_t **pps16)
{
return **pps16 ;
}

## Slide 45
Note:
pps16 is a pointer to a pointer to an int16_t.
(pps16 + 1) is a pointer to the next pointer to an int16_t.
*(pps16 + 1) is a pointer to an int16_t
**(pps16 + 1) is an int16_t
// R0 = pps16 (a 32-bit ptr to ptr to int16_t)
f9: ADD R0,R0,4 // R0 = pps16 + 1
LDR R0,[R0] // R0 = *(pps16 + 1)
LDRSH R0,[R0] // R0 = **(pps16 + 1)
BX LR
int32_t f9(int16_t **pps16)
{
return **(pps16 + 1) ;
}
f9: LDR R0,[R0,4]
LDRSH R0,[R0]
BX LR

## Slide 46
f10: LDR R0,[R0]
LDRSH R0,[R0,2]
BX LR
// R0 = pps16 (a 32-bit ptr to ptr to int16_t)
f10: LDR R0,[R0] // R0 = *pps16
ADD R0,R0,2 // R0 = *pps16 + 1
LDRSH R0,[R0] // R0 = *(*pps16 + 1)
BX LR
int32_t f10(int16_t **pps16)
{
return *(*pps16 + 1) ;
}

## Slide 47
int32_t f11(int32_t s32)
{
int32_t f12(void) ;
return s32 + f12() ;
}
// R0 = s32 (a 32-bit signed int)
f11: PUSH {R4, LR} // preserve R4 and LR
    MOV R4, R0 // R4 = s32
    BL f12 // R0 = f12()
    ADD R0, R0, R4 // R0 = f12() + s32
    POP {R4, PC} // restore R4 and PC

## Slide 48
int32_t f13(int32_t s32)
{
int32_t *f14(void) ;
return s32 + *f14() ;
}
// R0 = s32 (a 32-bit signed int)
f13: PUSH {R4, LR} // preserve R4 and LR
MOV R4, R0 // R4 = s32
BL f14 // R0 = f14()
LDR R0,[R0] // R0 = *f14()
ADD R0, R0, R4 // R0 = *f14() + s32
POP {R4, PC} // restore R4 and PC

## Slide 49: PRE-INDEXED MODE
Rn
+
constant
Instruction Register
Pre-Indexed Address
Updates Rn BEFORE using it to provide the address.
Syntax | Address | Example | Side Effect
[Rn,constant]! | Rn+ constant | [R5,4]! | R5  R5 + 4
ADD R1,R1,4
LDR R0,[R1]
LDR R0,[R1,4]!
Eliminates 1 instruction

## Slide 50: POST-INDEXED MODE
Rn
constant
Instruction Register
Post-Indexed Address
+
LDR R0,[R1]
ADD R1,R1,4
LDR R0,[R1],4
Eliminates 1 instruction
Syntax | Address | Example | Side Effect
[Rn],constant | Rn | [R5],4 | R5  R5 + 4
Updates Rn AFTER using it to provide the address.

## Slide 51
// Copy 44 bytes: mem[R1]  mem[R0] // (To update R0 & R1, append ! to each) LDMIA R0,{R2-R12} // regs  mem[R0] STMIA R1,{R2-R12} // regs  mem[R1] | 
COPYING A BLOCK OF DATA QUICKLY
Instruction | Syntax |  | Operation | Notes
Load Multiple registers, Increment After | LDMIA | Rn!,{register list} | registers  memory Rn = Rn + 4 x #registers | Addresses start with the address in Rn Updates Rn only if write-back flag (!) is appended to Rn.
Store Multiple registers, Increment After | STMIA | Rn!,{register list} | registers  memory Rn = Rn + 4 x #registers | 
Note: LDMIA SP!,{reglist} is equivalent to POP {reglist}.
  Data must be word aligned (located at a mod 4 adrs) or an address fault will occur.

## Slide 52
COPYING A BLOCK OF DATA QUICKLY
// Copy 44 bytes: mem[R1-44]  mem[R0-44] // (To update R0 & R1, append ! to each) LDMDB R0,{R2-R12} // regs <-- mem[R0] STMDB R1,{R2-R12} // regs --> mem[R1]
Instruction | Syntax |  | Operation | Notes
Load Multiple registers, Decrement Before | LDMDB | Rn!,{register list} | Rn = Rn - 4 x #registers registers  memory | Addresses end just before address in Rn Updates Rn only if write-back flag (!) is appended to Rn.
Store Multiple registers, Decrement Before | STMDB | Rn!,{register list} | Rn = Rn - 4 x #registers registers  memory | 
Note: STMDB SP!,{reglist} is equivalent to PUSH {reglist}.
  Data must be word aligned (located at a mod 4 adrs) or an address fault will occur.

## Slide 53
// void Copy512Bytes(void *dst, const void *src) Copy512Bytes: PUSH {R4-R11} // Preserve registers R4 - R11 .rept 11 LDMIA R1!,{R2-R12} STMIA R0!,{R2-R12} .endr // Copy the remaining 7*4 = 28 bytes LDMIA R1,{R2-R8} STMIA R0,{R2-R8} POP {R4-R11} // Restore registers R4 - R11 BX LR // Return
COPYING A BLOCK OF DATA QUICKLY
Each LDMIA/STMIA pair copies 11 words of 4 bytes (44 bytes) from mem[R1] to mem[R0], and adds 44 to R0 and R1 in preparation for the next pair.
The .rept 11 and .endr directives insert 11 copies of the LDMIA/STMIA instruction pair, copying 484 bytes total.
This leaves 28 more bytes (for a total of 512) to be copied.
This approach trades memory for speed. A loop would use fewer instructions, but each repetition of a loop requires executing a branch instruction that takes time to flush and refill the instruction pipeline.