## Slide 1: Chapter 7
Manipulating Bits

## Slide 2: BIT-MANIPULATION
Bitwise Operations: AND, OR, NOT, etc.
Shift Operations
Bit-Field Operations: Clear, Insert, Extract
Miscellaneous (Reverse Bits/Bytes, Count 0’s)
Bit-Banding (Hardware feature of ARM CPU)

## Slide 3: Review: AND, OR, Exclusive-OR
a | b | a AND b
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
a = 0
a = 1
0
b
a | b | a OR b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
a = 0
a = 1
b
1
a | b | a XOR b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a = 0
a = 1
b
b
If a=0, output = 0
If a=1, output = b
b
a
b
a
If a=0, output = b
If a=1, output = b
b
a
If a=0, output = b
If a=1, output = 1

## Slide 4: Review: Bitwise Operators
a = | a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
b = | b7 | b6 | b5 | b4 | b3 | b2 | b1 | b0
result = | c7 | c6 | c5 | c4 | c3 | c2 | c1 | c0
Each bit position of the result depends only on bits in the same position within the operands.

## Slide 5: Examples: Bitwise Operations
 | b3 | b2 | b1 | b0
& | 0 | 1 | 0 | 0
 | 0 | b2 | 0 | 0
 | b3 | b2 | b1 | b0
& | 1 | 0 | 1 | 1
 | b3 | 0 | b1 | b0
 | b3 | b2 | b1 | b0
¦ | 0 | 1 | 0 | 0
 | b3 | 1 | b1 | b0
 | b3 | b2 | b1 | b0
^ | 0 | 1 | 0 | 0
 | b3 | b2 | b1 | b0
Use bitwise OR to set a single bit to 1
Use bitwise AND to clear a single bit to 0
Use bitwise AND to isolate/test a single bit
Use bitwise XOR to change a single bit

## Slide 6: APPLICATIONS OF BITWISE OPERATIONS
Test the value of a single bit in a word
    if ((word & (1 << 5)) != 0) …
Calculate the remainder when dividend ≥ 0
    rem = a % 16  mod = a & 0xF
Determine if an integer is an odd number
    (a % 2) == 1  (a & 1) == 1
Determine if an integer is divisible by 2k
    (a % 8) == 0  (a & 0x7) == 0
  Calculating % takes more ARM CPU instructions than calculating &.

## Slide 7: BITWISE INSTRUCTIONS
Instruction | Syntax | Operation | Flags
Bitwise AND | AND{S} Rd,Rn,Op2 | Rd  Rn & Op2 | N,Z,C
Bitwise OR | ORR{S} Rd,Rn,Op2 | Rd  Rn ¦ Op2 | N,Z,C
Exclusive OR | EOR{S} Rd,Rn,Op2 | Rd  Rn ^ Op2 | N,Z,C
Bit Clear | BIC{S} Rd,Rn,Op2 | Rd  Rn & ~Op2 | N,Z,C
Bitwise OR NOT | ORN{S} Rd,Rn,Op2 | Rd  Rn ¦ ~Op2 | N,Z,C
Move NOT | MVN{S} Rd,Rn | Rd  ~Rn | N,Z,C
AND R0,R0,1 << 5 // Isolate bit #5
AND R0,R0,~(1 << 5) // Clear bit #5 to 0
TST R0,1 << 5 // Test bit #5 (TST is like AND, but discards result)
ORR R0,R0,1 << 5 // Set bit #5 to a 1
EOR R0,R0,1 << 5 // Change the value of bit #5
BIC R0,R0,1 << 5 // Clear bit #5 to 0

## Slide 8: APPLICATIONS OF BITWISE OPERATIONS
Set a bit to 1 without LDR R0,x affecting other bits: ORR R0,R0,1<<5
    X |= (1 << 5) ; STR R0,X
Clear a bit to 0 without LDR R0,x affecting other bits: BIC R0,R0,1<<5
    X &= ~(1 << 5) ; STR R0,x
Change a bit without LDR R0,x affecting other bits: EOR R0,R0,1<<5
    X ^= (1 << 5) ; STR R0,x

## Slide 9: APPLICATIONS OF SHIFTING
Multiplication by 2k: 2k×A = A << k
Division by 2k: A÷2k = A >> k (sort of)
Subscript Scaling: &a32[k] = &a32[0] + 4×k
Creating Multiples: 7×A = 8×A - 1×A

## Slide 10: SHIFT INSTRUCTIONS
Instruction | Syntax | Operation | Flags | Notes
Logical Shift Left | LSL{S} Rd,Rn,bits | Rd  Rn << bits | N,Z,C | Zero fills
Logical Shift Right | LSR{S} Rd,Rn,bits | Rd  Rn >> bits | N,Z,C | Zero fills
Arithmetic Shift Right | ASR{S} Rd,Rn,bits | Rd  Rn >> bits | N,Z,C | Sign extends
Rotate Right | ROR{S} Rd,Rn,bits | Rd  Rn >> bits | N,Z,C | right rotate
Rotate Right w/Extend | RRX{S} Rd,Rn | Rd  Rn >> 1 | N,Z,C | right shift, fill w/C
  Append "S" to capture the last bit shifted out in the carry (C) flag.
0
source
destination
0
source
destination
source
destination
source
destination
source
destination
C
C

## Slide 11: 3 PLACES WHERE SHIFT CAN BE USED
ROR R0,R1,R2 // R0  R1 rotated right R2 times
ADD R0,R1,R2,LSR 3 // R0  R1 + (R2 >> 3)
STR R0,[R1,R2,LSL 2] // R0  mem32[R1+4×R2]
As a regular shift instruction.
To provide a pre-shifted copy of the value in a register as the last operand of an instruction.
To multiply a subscript (R2) by the # of bytes per element in a subscripted array reference.
The only context in which the shift count may be a variable (e.g., R2 here).
  Only a Logical Shift Left (LSL) may be used in this context.

## Slide 12: ASR versus Integer Division
Operand | Example | Correct Result | Integer Result | Binary Operand | ASR Result (Binary) | ASR Result (Decimal)
Positive & even | +10 ÷ 2 | +5.0 | +5 | 00001010 | 00000101 | +5
Positive & odd | +11 ÷ 2 | +5.5 | +5 | 00001011 | 00000101 | +5
Negative & even | –10 ÷ 2 | –5.0 | –5 | 11110110 | 11111011 | –5
Negative & odd | –11 ÷ 2 | –5.5 | –5 | 11110101 | 11111010 | –6
  ASR truncates towards negative infinity.
Integer division truncates the quotient towards zero.
LDR R0,dividend
ASR R1,R0,31 // R1 = -1 (all 1’s) if dividend is negative, else 0
SUB R0,R0,R1 // Add 1 to negative dividends
ASR R0,R0,1 // Use ASR to divide by 2
STR R0,quotient

## Slide 13: Multiplying by a Constant
  2K×R: 2×R, 4×R, 8×R, 16×R, ...
  Ex: LSL R0,R1,2 // R0 = (4 × R1)
  (2K+1)×R: 3×R, 5×R, 9×R, 17×R, ...
  Ex: ADD R0,R1,R1,LSL 2 // R0 = R1 + (4 × R1)
  +(2K-1)×R: 3×R, 7×R, 15×R, 31×R, 63×R, ...
  Ex: RSB R0,R1,R1,LSL 2 // R0 = (4 × R1) – R1
  –(2K-1)×R: -3×R, -7×R, -15×R, -31×R, -63xR, ...
  Ex: SUB R0,R1,R1,LSL 2 // R0 = R1 – (4 × R1)

## Slide 14: 64-BIT LOGICAL SHIFT LEFT (by k bits, where k is a constant)
R1
R0
STRD R0,R1,data64
b63
b32
b31
b0
LDRD R0,R1,data64
• • •
• • •
LSL R1,R1,1
b62
b320
b0
b31
• • •
• • •
ORR R1,R1,R0,LSR 31
b62
b31
b0
b31
• • •
• • •
b10
b30
• • •
LSL R0,R0,1
b62
b31
• • •

## Slide 15: 64-BIT LOGICAL SHIFT LEFT (by n bits, where n is a variable)
LDRD R0,R1,data64
LSL R1,R1,1
ORR R1,R1,R0,LSR 31
LSL R0,R0,1
STRD R0,R1,data64
LDRD R0,R1,data64
LDR R2,n
LSL R1,R1,R2
RSB R3,R2,32
LSR R3,R0,R3
ORR R1,R1,R3
LSL R0,R0,R2
STRD R0,R1,data64

## Slide 16: 64-BIT ROTATES (by 1 bit)
// uint64_t RotateRight64(uint64_t dword64) RotateRight64: LSRS R1,R1,1 // Shift MSW right, capture bit 32 ORR R1,R1,R0,LSL 31 // Insert bit 0 into bit 63 RRX R0,R0 // Shift LSW right, enter carry BX LR // Return // uint64_t RotateLeft64(uint64_t dword64) RotateLeft64: ADDS R0,R0,R0 // Shift 64-bits left by 1 bit and ADCS R1,R1,R1 // capture the MS bit in carry. ADC R0,R0,0 // Insert carry into LS bit position. BX LR // Return

## Slide 17: A Fast Absolute Value Function
// uint32_t AbsValue(int32_t s32) AbsValue: // s32 < 0: else: EOR R1,R0,R0,ASR 31 // R1 = ~s32 R1 = s32 SUB R0,R1,R0,ASR 31 // R0 = ~s32 + 1 R0 = s32 BX LR // Return
  Fast! Avoids using making a compare and branch so that the instruction pipeline never stalls.
All 1’s if s32 < 0
All 0’s if s32 ≥ 0
-1 if s32 < 0
0 if s32 ≥ 0

## Slide 18: An Integer Power Function
uint32_t ipow(uint32_t x, uint32_t n)
{
uint32_t result ;
result = 1 ;
while (n != 0)
{
if (n & 1) result *= x ;
n >>= 1 ;
x *= x ;
}
return result ;
}
ipow: // R0 = x, R1 = n
// R2 = result
  MOV R2,1
loop: CBZ R1,done
LSRS R1,R1,1
IT CS
MULCS R2,R2,R0
MUL R0,R0,R0
B loop
done: MOV R0,R2
BX LR
()()() //

## Slide 19: Structure Bitfields
struct
{
unsigned gender : 1; // 0 = male, 1 = female
unsigned siblings : 4; // 0-15
unsigned hair : 2; // 0=black, 1=brown, etc.
unsigned eyes : 2; // 0=brown, 1=blue, 2=green
unsigned weight : 9; // 0-511
unsigned ethnicity : 4; // 0=Caucasian,1=Asian, etc…
unsigned : 3; // unused
unsigned age : 7 ; // 0-127
} packed ;
packed.eyes = garbage;
31 |  |  |  |  |  | 25 | 24 |  | 22 | 21 |  |  | 18 | 17 |  |  |  |  |  |  |  | 9 | 8 | 7 | 6 | 5 | 4 |  |  | 1 | 0
age |  |  |  |  |  |  | unused |  |  | ethnicity |  |  |  | weight |  |  |  |  |  |  |  |  | eyes |  | hair |  | siblings |  |  |  | 
LDR R0,packed
AND R0,R0,~(0b11 << 7)
LDR R1,garbage
AND R1,R1,0b11
ORR R0,R0,R1,LSL 7
STR R0,packed

## Slide 20: BITFIELD INSTRUCTIONS & APPLICATIONS
Extract an unsigned bitfield member from a structure
    uint32_t count = s.number ;
Instruction | Syntax | Operation | Notes
Bit Field Clear | BFC Rd,lsb,width | Rd<bits>  0 | 
Bit Field Insert | BFI Rd,Rn,lsb,width | Rd<bits>  Rn<lsb’s> | 
Signed Bit Field Extract | SBFX Rd,Rn,lsb,width | Rd  Rn<bits> | Sign extends
Unsigned Bit Field Extract | UBFX Rd,Rn,lsb,width | Rd  Rn<bits> | Zero extends
Extract a signed bitfield member from a structure
    int32_t balance = s.total ;
Insert a bitfield member into a structure
s.age = 21 ;
Clear a bitfield structure member to all 0’s
    s.total = 0 ;
  The lsb and width parameters must be constants.

## Slide 21: INSERTING BITFIELDS Version 1: Without BFI Instruction
// uint16_t PackTime(uint32_t hour, uint32_t min, uint32_t sec) PackTime: LSL R0,R0,11 // move hour into position at far left AND R1,R1,0x3F // restrict minutes to 0-63 ORR R0,R0,R1,LSL 5 // insert into packed time LSR R2,R2,1 // divide seconds by 2 AND R2,R2,0x1F // restrict seconds/2 to 0-31 ORR R0,R0,R2 // insert into packed time BX LR
15 |  |  |  | 11 | 10 |  |  |  |  | 5 | 4 |  |  |  | 0
hour |  |  |  |  | minutes |  |  |  |  |  | secs ÷ 2 |  |  |  | 
6 bits
5 bits
11 bits
7 Instructions

## Slide 22: INSERTING BITFIELDS Version 2: With BFI Instruction
// uint16_t PackTime(uint32_t hour, uint32_t min, uint32_t sec) PackTime: LSL R0,R0,11 // move hour into position at far left BFI R0,R1,5,6 // insert minutes into bits 5-10 of R0 LSR R2,R2,1 // divide the seconds by two BFI R0,R2,0,5 // insert seconds/2 into bits 0-4 of R0 BX LR
15 |  |  |  | 11 | 10 |  |  |  |  | 5 | 4 |  |  |  | 0
hour |  |  |  |  | minutes |  |  |  |  |  | secs ÷ 2 |  |  |  | 
6 bits
5 bits
11 bits
5 Instructions

## Slide 23: EXTRACTING UNSIGNED BITFIELDS Version 1: Without UBFX Instruction
// void UnpackDate(uint16_t date, uint32_t *y, uint32_t *m, uint32_t *d) UnpackDate: LSR R12,R0,9 // Move year – 1900 to far right ADD R12,R12,1900 // Add 1900 to fix the year STR R12,[R1] // Store year via the pointer LSR R12,R0,5 // Move month to the far right AND R12,R12,0xF // restrict month to4 bits STR R12,[R2] // Store month via the pointer AND R12,R0,0x1F // restrict day to 5 bits STR R12,[R3] // store day via the pointer BX LR // Return
15 |  |  |  |  |  | 9 | 8 |  |  | 5 | 4 |  |  |  | 0
year - 1900 |  |  |  |  |  |  | month |  |  |  | day |  |  |  | 
7 bits
4 bits
5 bits
9 Instructions

## Slide 24: EXTRACTING UNSIGNED BITFIELDS Version 2: With UBFX Instruction
// void UnpackDate(uint16_t date, uint32_t *y, uint32_t *m, uint32_t *d) UnpackDate: UBFX R12,R0,9,7 // Extract year–1900 from bits 15-9 of R0 into R12 ADD R12,R12,1900 // Add 1900 to get the year STR R12,[R1] // Store the year via the pointer in 2nd parameter UBFX R12,R0,5,4 // Extract the month from bits 8-5 of R0 into R12 STR R12,[R2] // Store month via the pointer in 3rd parameter UBFX R12,R0,0,5 // Extract the day from bits 4-0 of R0 into R12 STR R12,[R3] // Store the day via the pointer in 4th parameter BX LR // Return
15 |  |  |  |  |  | 9 | 8 |  |  | 5 | 4 |  |  |  | 0
year - 1900 |  |  |  |  |  |  | month |  |  |  | day |  |  |  | 
7 bits
4 bits
5 bits
8 Instructions

## Slide 25: EXTRACTING SIGNED BITFIELDS Version 1: Without SBFX Instruction
// void Unpack(uint16_t date, int32_t *p1, int32_t *p2, int32_t *p3) UnpackDate: LSL R12,R0,16 // Move s1 to far left of 32-bit register ASR R12,R12,25 // Move s1 to far right, sign extending STR R12,[R1] // Store s1 via the pointer p1 LSL R12,R1,23 // Move s2 to far left of 32-bit register ASR R12,R12,28 // Move s2 to the far right, sign extending STR R12,[R2] // Store s2 via the pointer p2 LSL R12,R0,27 // Move s3 to far left of 32-bit register ASR R12,R12,27 // Move s3 to the far right, sign extending STR R12,[R3] // store day via the pointer BX LR // Return
15 |  |  |  |  |  | 9 | 8 |  |  | 5 | 4 |  |  |  | 0
s1 |  |  |  |  |  |  | s2 |  |  |  | s3 |  |  |  | 
7 bits
4 bits
5 bits
10 Instructions

## Slide 26: EXTRACTING SIGNED BITFIELDS Version 2: With SBFX Instruction
// void Unpack(uint16_t date, int32_t *p1, int32_t *p2, int32_t *p3) UnpackDate: SBFX R12,R0,9,7 // Extract s1 as a signed 32-bit integer STR R12,[R1] // Store s1 via the pointer p1 SBFX R12,R0,5,4 // Extract s2 as a signed 32-bit integer STR R12,[R2] // Store s2 via the pointer p2 SBFX R12,R0,0,5 // Extract s3 as a signed 32-bit integer STR R12,[R3] // store day via the pointer BX LR // Return
15 |  |  |  |  |  | 9 | 8 |  |  | 5 | 4 |  |  |  | 0
s1 |  |  |  |  |  |  | s2 |  |  |  | s3 |  |  |  | 
7 bits
4 bits
5 bits
7 Instructions

## Slide 27: MISCELLANEOUS OPERATIONS
Instruction | Syntax | Operation
Count Leading Zeros | CLZ Rd,Rn | Rd  CountZeroes(Rn)
Reverse Bits | RBIT Rd,Rn | Rd  RevBits(Rn)
Reverse byte order of word | REV Rd,Rn | Rd  RevByteOrder(Rn)
Reverse the bytes within an operand (needed in network software)
Count leading zeroes (used in DSP to efficiently implement normalization)
Reverse the bits within an operand (to convert between big and little endian bit ordering)
  None of these operations can be implemented efficiently in a HLL like C.

## Slide 28: APPLICATIONS OF BIT-BANDING
Fast access to individual bits in memory or I/O
Only 1 instruction required to access a single bit
No bitwise-AND, bitwise-OR, or shifting required
"Atomic" access to manage a "mutex".
Atomic: An atomic operation completes without preemption / interruption.
Mutex: Used in operating systems, networking and multi-threaded software to arbitrate access to a shared resource.

## Slide 29: BIT-BAND REGIONS & ALIASES
32MB Bit-Band Alias
42000000-43FFFFFF16
1MB Bit-Band Region
40000000-400FFFFF16
31MB of I/O
40100000-41FFFFFF16
256 KB of I/O Space
32MB Bit-Band Alias
22000000-23FFFFFF16
1MB Bit-Band Region
20000000-200FFFFF16
31MB of RAM
20100000-21FFFFFF16
256 KB of Memory Space
  Each individual bit in a bit-band region corresponds to an entire word in its bit-band alias.
1 bit
1 word
1 bit
1 word

## Slide 30: BIT-BAND MAPPING
 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
2000100016 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0
…
A byte in the "bit-band region"
Corresponding 32-bit words in the "bit-band alias"
2202000C16 | 00000000 00000000 00000000 00000000
2202000816 | 00000000 00000000 00000000 00000000
2202000416 | 00000000 00000000 00000000 00000001
2202000016 | 00000000 00000000 00000000 00000000
2202001016 | 00000000 00000000 00000000 00000001
2202001416 | 00000000 00000000 00000000 00000001
2202001C16 | 00000000 00000000 00000000 00000001
2202001816 | 00000000 00000000 00000000 00000000

## Slide 31: FINDING THE ALIAS ADDRESS
Starting address of Bit-Band Region
  Example: Access bit 3 in 2000100016
  Bit-Band Region offset = 2000100016 – 2000000016 = 0100016
  Bit-Band Alias address = 2200000016 + 3210 × 0100016 + 4 × 3
  = 2200000016 + (0100016 << 5) + (3 << 2)
  = 2202000C16
31 |  |  |  |  |  | 25 | 24 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 5 | 4 |  | 2 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0
Bit-Band Alias address = 2200000016 + 32 × Bit-Band Region offset + 4 × bit number
  Read or write to this address accesses bit 3 at address 2000100016
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 32: BIT-BAND FUNCTION
// uint32_t *BitBandAliasAddress(void *BitBandAdrs, int BitNum) ; // BitBandAdrs: The address of data in the bit band region // BitNum: The number (0-31) of the bit within the data .globl BitBandAliasAddress BitBandAliasAddress: SUB R0,R0,0x20000000 // compute bit band offset LSL R0,R0,5 // insert offset into alias address ADD R0,R0,R1,LSL 2 // add 4 times the bit number (0-31) ADD R0,R0,0x22000000 // add base adrs of alias region BX LR