## Slide 1: Review
Chapter 5: Integer Arithmetic

## Slide 2: Integer Addition
Instructions: ADD{S}, ADC{S}
Format Examples:
  ADD R0,R1,5 // R0  R1 + 5
  ADD R0,R1,R2 // R0  R1 + R2
  ADD R0,R1,R2,LSL 2 // R0  R1 + (R2 << 2)
Flags: Append “S” to capture result characteristics in NCVZ
Overflow:
  Unsigned: Carry Flag (C) = 1
  Signed: Overflow Flag (V) = 1 (Set when CN≠CN-1)
Multiple precision addition: ADDS  ADC

## Slide 3: Integer Subtraction
Instructions: SUB{S}, SBC{S}, RSB{S}
Format Examples:
  SUB R0,R1,5 // R0  R1 - 5
  SUB R0,R1,R2 // R0  R1 - R2
  SUB R0,R1,R2,LSL 2 // R0  R1 - (R2 << 2)
Flags: Append “S” to capture result characteristics in NCVZ
Overflow:
  Unsigned: Carry Flag (C) = 0
  Signed: Overflow Flag (V) = 1 (Set when CN≠CN-1)
Multiple precision subtraction: SUBS  SBC

## Slide 4: Single-Length 32x32 Integer Multiplication
Instructions: MUL{S}, MLA, MLS
Signed vs. Unsigned: Use same instruction
Format Examples:
  MUL R0,R1,R2 // R0  R1 × R2
  MLA R0,R1,R2,R3 // R0  R3 + R1 × R2
  MLS R0,R1,R2,R3 // R0  R3 - R1 × R2
Flags: Append “S” (only MUL) to capture result characteristics in NZ
Overflow: May happen but impossible to detect

## Slide 5: Double-Length 32x32 Integer Multiplication
Instructions: UMULL, SMULL, UMLAL, SMLAL
Signed vs. Unsigned: Use different instructions!
Signed Instruction Formats:
  SMULL R0,R1,R2,R3 // R1.R0  R2 × R3
  SMLAL R0,R1,R2,R3 // R1.R0  R1.R0 + R2 × R3
Unsigned Instruction Formats:
  UMULL R0,R1,R2,R3 // R1.R0  R2 × R3
  UMLAL R0,R1,R2,R3 // R1.R0  R1.R0 + R2 × R3
Flags: Unaffected
Overflow: Can’t happen

## Slide 6: Single-Length 64x64 Integer Multiplication
Not used
Not used
AHIBHI
× 264
  ALOBLO
Not used
AHIBLO
× 232
Not used
ALOBHI
× 232
  3rd: UMULL(ALOBLO)
2nd: MLA(ALOBHI)
1st: MUL(AHIBLO)
AHI (Upper Half)
32 bits
32 bits
ALO (Lower Half)
BHI (Upper Half)
BLO (Lower Half)
  A = 232AHI + ALO
  B = 232BHI + BLO
  A×B = (232AHI + ALO)(232BHI + BLO)
  = 264AHIBHI + 232(AHIBLO + ALOBHI) + ALOBLO

## Slide 7: Single-Length 32÷32 Integer Division
Instructions: SDIV, UDIV
Signed vs. Unsigned: Use different instructions!
Signed Instruction Format:
  SDIV R0,R1,R2 // R0  R1 ÷ R2
Unsigned Instruction Format:
  UDIV R0,R1,R2 // R0  R1 ÷ R2
Flags: Unaffected
Overflow:
  Division by zero
  Full-scale negative divided by -1
Remainder: Use MLS (dividend – divisor × quotient)

## Slide 8: Chapter 5 Problems

## Slide 9: Chapter 5, Problem 1a
  int64_t a, b ;
  a = a + b ;
  LDRD R0,R1,a // R1.R0  a
LDRD R2,R3,b // R3.R2  b
ADDS R0,R0,R2 // Add LS halves
ADC R1,R1,R3 // Add MS halves
STRD R0,R1,a // Store result
a63-32
R1
a31-0
R0
b63-32
b31-0
R3
R2
R0
R1
a63-32
a31-0
C
Memory:
Memory:
CPU:
+
+

## Slide 10: Chapter 5, Problem 1b
  int64_t a ;
  a -= 5 ;
  LDRD R0,R1,a // R1.R0  a
SUBS R0,R0,5 // Sub LS half of 5
SBC R1,R1,0 // Sub MS half of 5
STRD R0,R1,a // Store result
a63-32
R1
a31-0
R0
R0
R1
a63-32
a31-0
C
+
─ ─
─
+
0
5
Memory:
Memory:
CPU:
~
~Bout

## Slide 11: Chapter 5, Problem 1c
  int32_t a, b, c ;
c = a * b ;
  LDR R0,a // R0  a
LDR R1,b // R1  b
MUL R0,R0,R1 // R0  a * b
STR R0,c // Store result
R0 = a
R1 = b
a
b
R0 = a*b
c
Memory:
Memory:
CPU:
×

## Slide 12: Chapter 5, Problem 1d
  uint32_t a, b, c ;
  c = a * b ;
  LDR R0,a // R0  a
LDR R1,b // R1  b
MUL R0,R0,R1 // R0  a * b
STR R0,c // Store result
R0 = a
R1 = b
a
b
R0 = a*b
c
The code for single-length multiplication is identical for signed and unsigned.
Memory:
Memory:
CPU:
×

## Slide 13: Chapter 5, Problem 1e
  int32_t a, b, c ;
c = a / b ;
  LDR R0,a // R0  a
LDR R1,b // R1  b
SDIV R0,R0,R1 // R0  a / b
STR R0,c // Store result
R0 = a
R1 = b
a
b
R0 =a/b
c
Memory:
Memory:
CPU:
÷

## Slide 14: Chapter 5, Problem 1f
  uint32_t a, b, c ;
c = a / b ;
  LDR R0,a // R0  a
LDR R1,b // R1  b
UDIV R0,R0,R1 // R0  a / b
STR R0,c // Store result
R0 = a
R1 = b
a
b
R0 = a/b
c
Replace the signed SDIV instruction with an unsigned UDIV instruction.
Memory:
Memory:
CPU:
÷

## Slide 15: Chapter 5, Problem 1g
  int32_t a, b, c ;
c = a % b ;
  LDR R0,a // R0  a
LDR R1,b // R1  b
SDIV R2,R0,R1 // R2  a/b
MLS R0,R2,R1,R0 // R0  a – b*(a/b)
STR R0,c // Store result
R0 = a
R1 = b
a
b
R2 = a/b
R0 = a-b*(a/b)
+
─
c
Memory:
Memory:
CPU:
÷
×

## Slide 16: Chapter 5: Programming Problem 2
int32_t Discriminant(int32_t a, int32_t b, int32_t c)
{
return b*b – 4*a*c ;
}
Discriminant: // R0=a, R1=b, R2=c
MUL R1,R1,R1 // R1 = b*b
LSL R0,R0,2 // R0 = 4*a
MLS R0,R0,R2,R1 // R0 = b*b – 4*a*c
BX LR
R1 = b
R2 = c
R0 = a
R1 = b*b
R0 = 4*a
R0=b*b-4*a*c
+
─
+
─
2
CPU:
<<
×
×

## Slide 17: Chapter 5: Programming Problem 3
uint32_t Volume(uint32_t height, uint32_t width, uint32_t length)
{
return height * width * length ;
}
Volume: // R0=height, R1=width, R2=length
MUL R0,R0,R1 // R0 = height * width
MUL R0,R0,R2 // R0 = height * width * length
BX LR
R1 = width
R2 = length
R0 = height
R0 = h * w
R0 = h * w * l
×
×
CPU: