## Slide 1: Chapter 12
Rational and Complex Arithmetic

## Slide 2: Why Rational Numbers?
int main()
{
float x ;
x = (0.5 – 0.4 – 0.1) ;
if (x == 0.0) printf("Zero\n") ;
else printf("Non-Zero\n") ;
return 0 ;
}

## Slide 3: Aggregate Data Types
An aggregate data type is one that contains more than one value.
Examples in C:
Arrays and structs.
Applications:
Complex numbers (have a real and an imaginary part)
Rational numbers (expressed as the ratio of two integers)

## Slide 4: Arrays, Structs and Functions
Functions and arrays:
An array parameter is passed as its address
A function may not return an array.
Functions and structs:
A struct parameter is passed by value (a copy)
A function may return a struct
Not a good choice for Complex or Rational.

## Slide 5: Using a Structure as a Container
We could use a struct to create a programmer–defined data type:
typedef struct typedef struct
{ {
float real ; int top ;
float imag ; int btm ;
} COMPLEX ; } RATIONAL ;
COMPLEX x = {1.5, -3.7} ; RATIONAL x = {1, 3} ;

## Slide 6: Pros and Cons of Structures
Advantage of struct:
Cleaner and intuitive C syntax for accessing member elements
Disadvantage of struct:
Since the size of a struct is not limited, compilers may call a (slow) memory-to-memory copy routine to create the pass-by-value copy.

## Slide 7: The AAPCS, the FPU, and Structures
Parameters that are a struct of 1-4 floats or 1-4 doubles are passed in a sequence of sequentially numbered floating-point registers
typedef struct {float a, b, c, d} STUFF ;
void foo(STUFF) ; // function prototype
STUFF x = {1.1, -3.2, 7.1. -10.8} ;
…
foo(x) ;
…
VLDR S0,x.a
VLDR S1,x.b
VLDR S2,x.c
VLDR S3,x.d
BL foo
…

## Slide 8: The AAPCS, the FPU, and Structures
Functions return a struct of 1-4 floats or 1-4 doubles in a sequence of floating-point registers starting with S0 or D0.
typedef struct {float a, b, c, d} STUFF ;
STUFF foo(void) ; // function prototype
STUFF x = {1.1, -3.2, 7.1. -10.8} ;
…
x = foo() ;
…
BL foo
VSTR S0,x.a
VSTR S1,x.b
VSTR S2,x.c
VSTR S3,x.d
…

## Slide 9: The AAPCS and Structures of Ints
The AAPCS doesn't use a sequence of integer registers for structures containing 1-4 integers because there are only four integer registers that can be used for function parameters.
We need a different strategy when the member elements are not floats! (E.g., integers or fixed-point reals)

## Slide 10: Using a Native Data Type as a Container
Data Type | Bits | Passed In Registers | Use as a container for …
uint32_t | 32 | R0-R3 | (4) 8-bit integers, or (2) 16-bit integers or fixed-point reals
uint64_t | 64 |  | (8) 8-bit integers, or (4) 16-bit or (2) 32-bit integers or fixed-point reals
double | 64 | D0-D7 | (2) single-precision reals (floats)
Registers determined by native data type
Most efficient choices based on registers

## Slide 11: Using a Native Data Type as a Container
COMPLEX foo(COMPLEX) ;
COMPLEX c ;
c = foo(c) ;
VLDR D0,c
BL foo
VSTR D0,c
typedef double COMPLEX ;
#define REAL(x) ((float *) &x)[0]
#define IMAG(x) ((float *) &x)[1]
COMPLEX c ;
REAL(c) = 3.5 ; IMAG(c) = -2.1 ;
printf(“c=(%f,%f)\n”, REAL(c), IMAG(c)) ;
D0 is another name for the register pair S0,S1
Parameters are passed and result returned in floating-point registers.

## Slide 12: Using a Native Data Type as a Container
typedef uint64_t RATIONAL ;
#define TOP(x) ((int *) &x)[0]
#define BTM(x) ((int *) &x)[1]
RATIONAL r ;
TOP(r) = 1 ; BTM(r) = 3 ;
printf("r = %d/%d", TOP(r), BTM(r)) ;
RATIONAL foo(RATIONAL) ;
RATIONAL r ;
r = foo(r) ;
LDRD R0,R1,r
BL foo
STRD R0,R1,r
Parameters are passed and result returned in integer registers.

## Slide 13: Using uint32_t to Hold a Rational Number
31 | 16 | 15 | 0
top (int16_t) |  | bottom (int16_t) | 

## Slide 14: Using uint32_t to Hold a Rational Number
Instruction | Format |  | Operation | 
Signed Multiply Halfwords | SMULBB | Rd,Rn,Rm | Rd Rn<15..0> Rm<15..0> | Rd btm(Rn) btm(Rm)
 | SMULBT | Rd,Rn,Rm | Rd Rn<15..0> Rm<31..16> | Rd btm(Rn) top(Rm)
 | SMULTB | Rd,Rn,Rm | Rd Rn<31..16> Rm<15..0> | Rd (Rn) btm(Rm)
 | SMULTT | Rd,Rn,Rm | Rd Rn<31..16> Rm<31..16> | Rd (Rn) top(Rm)
Instruction | Format |  | Operation | 
Signed Multiply Halfwords | SMULBB | Rd,Rn,Rm |  | 
 | SMULBT | Rd,Rn,Rm |  | 
 | SMULTB | Rd,Rn,Rm |  | 
 | SMULTT | Rd,Rn,Rm |  | 

## Slide 15: Using uint32_t to Hold a Rational Number
// a + b: RATIONAL RAdd(RATIONAL a, RATIONAL b) ;
// a - b: RATIONAL RSub(RATIONAL a, RATIONAL b) ;
// a * b: RATIONAL RMul(RATIONAL a, RATIONAL b) ;
// a / b: RATIONAL RDiv(RATIONAL a, RATIONAL b) ;
RAdd: SMUADX R2,R0,R1 // top = TOP(R0)*BTM(R1) + BTM(R0]*TOP(R1]
SMULBB R3,R0,R1 // btm = BTM(R0)*BTM(R1)
PKHBT R0,R3,R2,LSL 16 // sum = (top << 16) | btm
BX LR
RSub: SMUSDX R2,R1,R0 // top = TOP(R0)*BTM(R1) - BTM(R0]*TOP(R1]
SMULBB R3,R0,R1 // btm = BTM(R0)*BTM(R1)
PKHBT R0,R3,R2,LSL 16 // diff = (top << 16) | btm
BX LR
RMul: SMULTT R2,R0,R1 // top = TOP(R0)*TOP(R1)
SMULBB R3,R0,R1 // btm = BTM(R0)*BTM(R1)
PKHBT R0,R3,R2,LSL 16 // prod = (top << 16) | btm
BX LR
RDiv: SMULTB R2,R0,R1 // top = TOP(R0)*BTM(R1)
SMULBT R3,R0,R1 // btm = BTM(R0)*TOP(R1)
PKHBT R0,R3,R2,LSL 16 // quot = (top << 16) | btm
BX LR

## Slide 16: Using uint32_t to Hold a Rational Number
0x1234
0x5678
0x1234
0xDEF0
0x9ABC
0xDEF0
Rn
Rd
Rm
0x1234
0x5678
0x9ABC
0x5678
0x9ABC
0xDEF0
Rn
Rd
Rm
PKHBT Rd,Rn,Rm
PKHTB Rd,Rn,Rm
Instruction | Format |  | Operation
Pack Halfwords | PKHBT | Rd,Rn,Rm{,shift} | Rd<15..00> Rn<15..00> Rd<31..16> Rm<31..16>
 | PKHTB | Rd,Rn,Rm{,shift} | Rd<31..16> Rn<31..16> Rd<15..00> Rm<15..00>
Note: Rm may be pre-shifted by appending an LSL or ASR shift modifier. |  |  | 
Instruction | Format |  | Operation
Pack Halfwords | PKHBT | Rd,Rn,Rm{,shift} | 
 | PKHTB | Rd,Rn,Rm{,shift} | 
Note: Rm may be pre-shifted by appending an LSL or ASR shift modifier. |  |  |