## Slide 1: Chapter 3
Writing Functions in Assembly

## Slide 2: Approach
Most of a program is written in a high-level language (HLL) such as C
  easier to implement
  easier to understand
  easier to maintain
Only a few functions are written in assembly
  to improve performance, or
  because it’s difficult or impossible to do in a HLL.

## Slide 3: Creating a Program
Linker
Execu-table Program
Librarycode
Compiler
Assembler
Object code
Object code
Library header files
C sourcecode
ASM sourcecode
Most of code, including function main
A few small functions

## Slide 4: Consequence
Assembly functions must be compatible with:
  How the C compiler invokes the execution of a function
  How the C compiler passes parameters to functions
  How the C compiler expects to receive results from functions
  How the C compiler uses CPU registers

## Slide 5: FUNCTION CALL AND RETURN Simple Call-Return in C
● ● ● f1() ; ● ● ● | void f1(void) { ● ● ● return ; }
Suspend the current sequence
Record the return address
Transfer control to the function
Execute the function
Use the recorded return address to go back and resume the suspended code.
Branch with Link Instruction (BL)
Branch Indirect Instruction (BX)

## Slide 6: FUNCTION CALL AND RETURN ARM instructions used to call and return from functions
Instruction | Format |  | Operation
Branch with Link | BL | label | Function Call: LR  return address, PC  address of label
Branch Indirect | BX | LR | Function Return: PC  LR
LR (aka R14) and PC (aka R15) are two of the 16 registers inside the CPU.
LR is the “Link Register” – used w/function calls to hold the return address
PC is the “Program Counter” – holds the address of the next instruction.

## Slide 7: FUNCTION CALL AND RETURN Simple Call-Return in Assembly
● ● ● BL f1 ● ● ● | f1: ● ● ● BX LR
The “Branch with Link” instruction (BL) saves the the address of the instruction immediately following it (the return address) in the Link Register (LR).
The “Branch Indirect” instruction (BX) copies the return address from LR into PC, thus transferring control back to where the function had been called.
Consider: There is only one Link Register. What if inside function f1 there is a call to another function?

## Slide 8: FUNCTION CALL AND RETURN Nested Call-Return in Assembly
● ● ● BL f1 ● ● ● | f1: ● ● ● BL f2 ● ● ● BX LR | f2: ● ● ● BX LR
Modifies the link register (LR), writing over f1’s return address!
Saves the contents of LR on the stack.
Restores the contents of LR from the stack.
PUSH {LR}
POP {LR}
Saves the return address in LR
Copies the saved return address from LR back into PC

## Slide 9: FUNCTION CALL AND RETURN ARM instructions used in functions that call other functions
Instruction | Format |  | Operation
Push registers onto stack | PUSH | register list | SP  SP – 4 × #registers Copy registers to mem[SP]
Pop registers from stack | POP | register list | Copy mem[SP] to registers, SP  SP + 4 × #registers
SP is one of the 16 CPU registers (R13) – holds the address of the top of the stack.
1000 | Pushed data
996 | Pushed data
992 | Top of stack
988 | 
984 | 
980 | 
976 | 
972 | 
SP | 992
(register R13)
(memory)
Unused Stack
Space
“register list” format: { reg, reg, reg-reg, …}

## Slide 10: Optimizing Function Calls
f1: PUSH {LR}
●
●
●
BL f2
●
●
●
POP {PC}
f1: PUSH {LR}
●
●
●
BL f2
●
●
●
POP {LR}
BX LR

## Slide 11: Optimizing Function Calls
● ● ● BL f1 ● ● ● | f1: ● ● ● B f2 | f2: ● ● ● BX LR
● ● ● BL f1 ● ● ● | f1: ● ● ● BL f2 BX LR | f2: ● ● ● BX LR
PUSH {LR}
POP {LR}

## Slide 12: ARM PROCEDURE CALL STANDARD Registers used as input parameters
Register | AAPCS Name | Usage
R0 | A1 | 1st parameter
R1 | A2 | 2nd parameter
R2 | A3 | 3rd parameter
R3 | A4 | 4th parameter
One register is used for each 8, 16 or 32-bit parameter.
A sequential register pair is used for each 64-bit parameter.

## Slide 13: ACCESSING PARAMETERS INSIDE THE FUNCTION How parameters are passed to a function by the compiler
C Function Call | Compiler Output
LDRSB R0,x8 // R0 <-- x8
LDR R1,y32 // R1 <-- y32
LDRD R2,R3,z64 // R3.R2 <-- z64
BL foo
●
●
●
MOV R0,5 // R0 <-- 5
MOV R1,-10 // R1 <-- -10
MOV R2,20 // R3.R2 <-- 20
MOV R3,0
BL foo
int8_t x8 ;
int32_t y32 ;
int64_t z64 ;
●
●
foo(x8, y32, z64) ;
●
●
foo(5, -10, 20) ;
●
●
  Inside foo, you must use the register copies of the actual arguments.

## Slide 14: ARM PROCEDURE CALL STANDARD Registers used to return function result
Register | AAPCS Name | Usage
R0 | A1 | 8, 16 or 32-bit result, or the least-significant half of a 64-bit result
R1 | A2 | The most-significant half of a 64-bit result

## Slide 15: PREPARING THE RETURN VALUE Functions that return an 8, 16 or 32-bit result
Functions must provide a full 32-bit representation of return value, even for 8 and 16-bit results.

## Slide 16: Review Summary
Call functions using Branch with Link (BL)
  Saves the return address in Link Register (LR)
  Copies the target address into Program Counter (PC)
Return from a function using BX LR
Writing functions that call other functions:
  Using BL to call another function changes LR
  Use PUSH {LR} / POP {LR} to preserve LR
Pass parameters using registers R0-R3
  64-bit parameters in consecutive register pair
Return 8, 16 and 32 bit results using R0
  64-bit result returned in R1.R0 register pair

## Slide 17: Review Summary
BX LR
POP {PC}
MOV R0,10
MOV R0,1
MOV R1,2
void f1(void)
  {
  .
  .
  .
  .
  .
  }
f2() ;
f1: .
.
.
.
.
.
.
f2(1, 2) ;
return 10 ;
int32_t f1(void)
PUSH {LR}
BL f2
void f2(void) ;
f2(int32_t, int32_t) ;

## Slide 18: PREPARING THE RETURN VALUE Promoting a return value from 8 to 16 or 32 bits
C Function Call | Compiler Output
uint8_t save8, get8(void) ; uint16_t save16 ; uint32_t save32 ; uint64_t save64 ; ● ● ● save8 = get8() ; save16 = (uint16_t) get8() ; save32 = (uint32_t) get8() ; ● save64 = (uint64_t) get8() ; ● ● ● | ● ● ● BL get8 STRB R0,save8 BL get8 STRH R0,save16 BL get8 STR R0,save32 ● BL get8 MOV R1,0 STRD R0,R1,save64 ● ● ●
Promotion to 64-bits requires extending the result after the call
8, 16 and 32-bit func-tions must always provide a 32-bit result.

## Slide 19: PREPARING THE RETURN VALUE Functions that return 64-bit result
Functions that return a 64-bit result leave it in R0 and R1 before returning.

## Slide 20: REGISTER USAGE CONVENTIONS ARM PROCEDURE CALL STANDARD
Register | AAPCS Name | Usage | Notes
R0 | A1 | Argument / result /scratch register 1 | 
R1 | A2 | Argument / result /scratch register 2 | 
R2 | A3 | Argument / scratch register 3 | 
R3 | A4 | Argument / scratch register 4 | 
R4 | V1 | Variable register 1 | Must preserve original contents
R5 | V2 | Variable register 2 | 
R6 | V3 | Variable register 3 | 
R7 | V4 | Variable register 4 | 
R8 | V5 | Variable register 5 | 
R9 | V6 | Variable register 6 | 
R10 | V7 | Variable register 7 | 
R11 | V8 | Variable register 8 | 
R12 | IP | Intra-Procedure-call scratch register | 
R13 | SP | Stack Pointer | Reserved, Do not use
R14 | LR | Link Register | 
R15 | PC | Program Counter | 

## Slide 21: FUNCTION CODING CONVENTIONS Functions that modify only registers R0 - R3, R12
Using only R0-R3, R12 and no function call |  | Using only R0-R3, R12 and calling another function
f1: ● ● ● OK to modify ● R0-R3 and R12 ● BX LR |  | f2: PUSH {LR} ● ● OK to modify R0–R3, R12 ● BL f3 ● ● OK to modify R0–R3, R12 ● POP {PC}
Function f3 might modify R0 – R3, R12

## Slide 22: FUNCTION CODING CONVENTIONS Functions that modify for example registers R4 and R5
Using R4 and R5 and no function call |  | Using R4 and R5 and calling another function
f1: PUSH {R4,R5} ● ● OK to modify ● R0-R5 and R12 ● POP {R4,R5} BX LR |  | f2: PUSH {R4,R5,LR} ● ● OK to modify ● R0–R5 and R12 ● BL f3 ● ● OK to modify ● R0–R5 and R12 ● POP {R4,R5,PC}
Function f3 might modify R0-R3 and R12, but preserves R4-R11

## Slide 23: FUNCTION CODING CONVENTIONS Two functions with parameters, one calling the other
C Version | Assembly Version
int32_t f1(int32_t x) { return f2(4) + x ; } | f1: PUSH {R4,LR} // Preserve R4 MOV R4,R0 // Keep x safe in R4 MOV R0,4 // R0 <-- f2’s arg BL f2 // R0 <-- f2(4) ADD R0,R0,R4 // R0 <-- f2(4) + x POP {R4,PC} // Restore R4
parameter x
some value
R0
R4
parameter x
parameter x
R0
R4
constant 4
parameter x
R0
R4
f2 return value
parameter x
R0
R4
On entry to function:
After 1st MOV instruction:
After 2nd MOV instruction:
After the BL instruction:
f1 return value
parameter x
R0
R4
After the ADD instruction:
f1 return value
some value
R0
R4
After the POP instruction:

## Slide 24: Lab 1, Part 1: Sample Program
RUN DEMO

## Slide 25: void InitializeHardware(char *, char *) ;
Must be first executable statement
Initializes processor, CPU clock cycle counter, the display and user push button.
Creates stack and heap and initializes static variables.
Formats display area

## Slide 26: uint32_t GetClockCycleCount(void) ;
Returns the number of processor clock cycles since initialization.
start = GetClockCycleCount() ;
// do some calculation here
stop = GetClockCycleCount() ;
printf("Cycles=%d\n", stop-start) ;
Cycles=1788
STM32F429I-DISCO
GetClockCycles

## Slide 27: void WaitForPushButton(void) ;
Causes program to pause and wait for user to push the blue push button on the board.

## Slide 28: void ClearDisplay(void) ;
Sine Function
STM32F429I-DISCO
Erases the scrollable area of the display.

## Slide 29: Lab 1 (Part 2): Decimal/Binary Conversions
void Dec2Bin(float x, int bin[8])
{
// To be implemented by student
// Input Parameter: 0.0 < X < 1.0
// Output Parameter: bin[0] = Least significant bit
// bin[7] = Most significant bit
// Return value: None
}
float Bin2Dec(int bin[8])
{
// To be implemented by student
// Input Parameter: bin[0] = Least significant bit
// bin[7] = Most significant bit
// Return value: 0.0 < float < 1.0
}

## Slide 30: Bin2Dec (The "easier" one)
Use a modified Polynomial Evaluation:
Assume the 8 bits represent an integer.
  E.g., 100100112 = 14710
Convert the integer to fraction:
  Note: 0.10010011 = 10010011/28
  E.g., 147/256 = 0.5742187510

## Slide 31: Dec2Bin (A little more difficult)
Binary Rounding:
  Result must be limited to 8 bits.
  If 9th bit = 1, add 1 to the 8-bit result.
Easier if scaled first:
  0.0 ≤ x < 1.0  0.0 ≤ 28x < 256.0
Extract integer and fractional parts of x:
  Add 1 to integer if fractional part ≥ 0.5
  Convert integer to binary (as your output)