## Slide 1: ELEN 21/COEN 21: Introduction to Logic Design
Lectures 7 & 8: Number representation, arithmetic circuits
Radhika S. Grover
Electrical Engineering Department
Santa Clara University
rgrover@scu.edu

## Slide 2: Binary Number Systems
Overview :
Digital Numbers
Number Base Conversions
Octal and Hexadecimal numbers
Complements
Signed Binary Numbers
Binary Codes
Binary Storage and Registers
Binary Logic
Adders
There are 10 types of people in this world: those who can read binary and those who can’t.

## Slide 3: Decimal number representation
E.g. 7392 represents number
- 7 × 103 + 3 × 102 + 9 × 101 + 2 × 100
This can be obtained as
10 7392
10 739 2
10 73 9
7 3

## Slide 4: Base or radix of a number
E.g. a3a2a1a0.a-1a-2 represents number
a3 × 103 + a2 × 102 + a1 × 101 + a0 × 100 + a-1 × 10-1 + a-2 × 10-2
Decimal number system has base or radix 10 because
- coefficients (a3 a2 a1 etc.) are any of 10 digits (0,1,..,9) and
- coefficients are multiplied by powers of 10.
Generalize this to represent a number N in base-r system.

## Slide 5: Generic number representation
Represent a generic number N with radix-r representation.
N = anan-1...a1a0.a-1a-2…a-m
N = an × rn + an-1 × rn-1 + ….+ a1 × r1 + a0 + a-1 × r-1 + a-2 × r-2
Coefficients aj range from 0 to r-1.
What are the decimal values of (401.1)5 , (127.2)8?

## Slide 6: Binary numbers
The binary number system has base-2:
E.g. (11010.11)2
= 1 × 24 + 1 × 23 + 0 × 22 + 1 × 21 + 0 ×20 + 1 ×2-1 + 1 × 2-2
= (26.75)10
What does binary number 1100 represent?
Digits in a binary number are called bits.

## Slide 7: Counting numbers in different bases
base-5 base-3
0 10 20 0 10 20
1 11 21 1 11 21
2 12 22 2 12 22
3 13 23
4 14 24 Write first 10 numbers in base-2.

## Slide 8: Number base conversions
Convert a number in base r to decimal:
- expand the number in a power series
- add all the terms
Example: convert (127.4)8 to decimal
(127.4)8 = 1 × 82 + 2 × 81 + 7 × 80 + 4 × 8-1
= (87.5)10
octal number system : base-8 system
hexadecimal number system : base-16 system

## Slide 9: Number base conversions cont.
Convert a number in decimal to base r:
- divide the number and all successive quotients by r
- accumulate the remainders
Example: Convert decimal 41 to binary.
2 41
2 20 1
2 10 0
2 5 0
2 2 1
2 1 0
0 1
Solution: (41)10 = (101001)2

## Slide 10: Number base conversions cont.
Convert (.6875)10 to binary.
0.6875 × 2 = 1.3750
0.3750 × 2 = 0.7500
0.7500 × 2 = 1.5000
0.5000 × 2 = 1.0000
Solution: (.6875)10 = (0.1011)2
Convert .625 to binary

## Slide 11: Octal numbers
Converting from binary to octal number:
  (10 110 001 101 011 · 111 100 000 110)2 = (26153.7406)8
  2 6 1 5 3 7 4 0 6
  Partition the binary number into groups of 3 digits each starting from binary point.
  Then proceed to left and right.
  Assign octal digit to each group.
Converting from octal to binary number:
  (673.124)8 = ( 110 111 011 · 001 010 100 )2

## Slide 12: Hexadecimal numbers
Hexadecimal number system: digits are 0, 1, 2, .. , 9, A, B, C, D, E and F
Converting from binary to hexadecimal number:
  (0011 0000 0110 · 1101)2 = (306.D)16
  3 0 6 D
  Conversion is done similarly as was done with octal numbers.
Converting from hexadecimal to binary number:
  (2C6B.F2)16 = (10 1110 0110 1011 · 1111 0010)2
  2 C 6 B F 2

## Slide 13: Complements
Used for simplifying the subtraction operation.
Also used for logical manipulation
Types of complements :
- diminished radix complement or (r-1)’s complement
- radix complement or r’s complement
Examples:
- 1’s complement and 2’s complement for binary numbers
- 9’s complement and 10’s complement for decimal numbers

## Slide 14: Diminished Radix Complement
Given a number N in base r having n digits.
(r-1)’s complement of N is (rn – 1) – N.
For decimal numbers, r = 10, so 9’s complement of N is (10n – 1) – N.
Examples:
9’s complement of 546700 is 999999 – 546700 = 453299.
What is 9’s complement of 012398?
1’s complement of 1011000 is 0100111.
What is 1’s complement of 0101101?

## Slide 15: Radix Complement
Given an n-digit number N in base r.
The r’s complement is rn – N for N ≠ 0, and
0 for N = 0.
Can also be obtained by adding 1 to 9’s complement of N.
Example: 10’s complement of decimal 2389 = 7611.
What is 10’s complement of 012398?
2’s complement of 1101100 is 0010100.
- leave least significant 0’s and first 1 unchanged.
- replace 1’s with 0’s and 0’s with 1’s in all higher significant digits.

## Slide 16: Signed binary numbers
Two types of representations:
Signed-magnitude system
- number has a magnitude and a +/- symbol or sign bit.
- used in ordinary arithmetic.
Signed-complement system
- a negative number is represented by its complement.
- negates a number by taking its complement.
- more convenient on a computer.

## Slide 17: Signed magnitude system for binary numbers
Positive numbers (including zero) can be represented as unsigned numbers.
For signed numbers, represent the sign with a bit placed in the leftmost position.
By convention, sign bit is 0 for positive and 1 for negative numbers.
Example: 01001
is 9 (unsigned binary) or +9 (signed binary)
11001 is 25 (unsigned binary) or -9 (signed binary).

## Slide 18: Signed complement system for binary numbers
Positive numbers always start with a 0 in left-most position.
Complement always starts with 1 representing a negative number.
Two types:
- 1’s complement or 2’s complement
Example: represent -9 with eight bits
signed-magnitude representation: 10001001
signed-1’s-complement representation: 11110110
signed-2’s-complement representation: 11110111

## Slide 19: Arithmetic Addition
Addition of two numbers in signed-magnitude form follows rules of ordinary arithmetic.
- If signs are the same, we add the two magnitudes, and give sum common sign.
- If signs are different, subtract smaller magnitude from larger and give result sign of larger magnitude.
Addition of two numbers in two’s complement:
- add the two numbers including sign bit.
- ignore carry out of sign-bit position

## Slide 20: Arithmetic Addition cont.
Example: Negative numbers are in signed two’s complement form:
+6 00000110 -6 11111010
+13 00001101 +13 00001101
+19 00010011 +7 00000111
+6 00000110 -6 11111010
-13 11110011 -13 11110011
-7 -19

## Slide 21: Arithmetic Subtraction
Subtraction of two signed binary numbers with negative numbers in 2’s complement form:
- Take 2’s complement of the subtrahend (including the sign bit).
- Add it to the minuend (including the sign bit).
Example: 13 – 6 = (13) + (-6)
= 00001101 + 11111010 = 100000111
= 00000111 (+7)
ignore

## Slide 22: Binary codes
n-bit binary code is a group of n bits that:
- Assume 2n distinct combinations of 1s and 0s.
- Each element represents one element of the set that is being coded.
Types of codes:
BCD Code, Gray code, ASCII Character Code, Error detecting code.

## Slide 23: BCD Code
Code most commonly used for the decimal digits.
Is the binary assignment called BCD.
0 0000
1 0001
2 0010
3 0011
4 0100
5 0101
6 0110 (185)10 = (0001 1000 0101)BCD
7 0111 = (10111001)2
8 1000
9 1001
Decimal symbol
BCD digit

## Slide 24: BCD Addition
Addition of two decimal digits in BCD with possible carry from previous less significant pair of digits.
Since each digit does not exceed 9, the sum cannot be greater than 9 + 9 + 1 = 19. (1 is carry-over).
Sum will produce result in range 0 to 19.
In binary this is from 0000 to 10011.
In BCD this is from 0000 to 1 1001.
When binary sum is greater than 1010, this is invalid BCD digit.
Add (0110)2 to binary sum to correct it.

## Slide 25: BCD Addition cont.
Examples:
4 0100 4 0100
+ 5 0101 +8 1000
9 1001 12 1100
+0110
1 0010

## Slide 26: Other Decimal Codes
BCD code has weights of 8, 4, 2, 1
BCD code is a weighted code.
2421 code is a weighted code.
e.g. 1101 when weighted by digits 2421 represents:
2 × 1 + 4 × 1 + 2 × 0 + 1 × 1 = 7
Excess-3 code : binary value + 3
e.g. 0 is represented as 0011 in excess-3
Notes: Excess 3 code can easily compute subtractions involving 9.
Eg excess 3 of 5 = 1000
Need to find 9-5
9-5 = 4; to find this solution invert all bits of 1000 (gives 0111, which is excess 3 code of 4)

## Slide 27: Gray code
Advantage of gray code is that only bit changes when going from one number to the next.
Used in applications where normal sequence of binary numbers may produce an error/ambiguity during transition.
Gray code Decimal equivalent
0000 0
0001 1
0011 2
0010 3
0110 4
0111 5
0101 6
Notes: Position encoders, error correction, Kmaps

## Slide 28: ASCII character code
Standard binary code for the alphanumeric characters is ASCII.
An alphanumeric character set includes 10 decimal digits, 26 letters of alphabet and a number of special characters.
It uses 7 bits to code 128 characters.
E.g. A is represented in ASCII as 1000001.
Each ASCII code can be stored in a single unit called byte (8 bits).

## Slide 29: Error-Detecting code
An extra bit called parity is included with a message to make number of 1’s even or odd.
Parity bit is useful in detecting errors during transmission of information from one location to another.
Example: even parity ASCII
ASCII T = 1010100
with even parity ASCII T = 11010100
Check the parity of each character at receiving end.
If the parity of received character is not even, it means that at least one bit has changed value during the transmission.

## Slide 30: Binary storage and registers
A binary cell is a device that can store one bit of information ( a 1 or a 0).
A register is a group of binary cells.
A register with n cells can store any discrete quantity of information that contains n bits.
Each bit designates the state of one cell in the register.
A register with 16 cells can be in one of 216 possible states.

## Slide 31: Register transfer
A register transfer operation consists of a transfer of binary information from one set of registers into another set of registers.
Transfer may be
- direct from one register to another
- pass through data processing circuits.
Example: transfer of binary information from keyboard into a register in memory unit.

## Slide 32: Register transfer cont.
Keyboard
8 cells
8 cells
8 cells
8 cells
J
O
H
N
CONTROL
Input Register
8 cells
Processor Register
PROCESSOR UNIT
01001010010011111100100011001110
Memory Register
MEMORY UNIT
Shift left

## Slide 33: Summary
Representing numbers in different bases: binary, octal, hexadecimal
Different types of codes