## Slide 1: Chapter 14
Programming Peripheral Devices

## Slide 2: Memory-Mapped I/O
32-bit CPU’s provide a huge 4GB (232) address space
Code and data uses small fraction of memory
A portion of address space is assigned to peripherals
  Peripheral devices may be accessed using pointers
  Any C operator that can be applied to a variable can be used to access a peripheral
System
Private Peripherals (External)
Private Peripherals (Internal)
External Devices (1GB)
External R/W Memory (1GB)
Peripherals (0.5GB)
Read/Write Memory (0.5GB)
Program Code (0.5GB)
E0100000-FFFFFFFF
E0040000-E00FFFFF
E0000000-E003FFFF
A0000000-DFFFFFFF
60000000-9FFFFFFF
40000000-5FFFFFFF
20000000-3FFFFFFF
00000000-1FFFFFFF

## Slide 3: Synchronizing Data Transfers
Peripheral devices are slower than the CPU.
Code must wait until device is ready.
Four synchronization techniques:
  Blocking I/O
  Polled Waiting Loop
  Interrupt-Driven
  Direct Memory Access (DMA)
Hardware stalls the execution of the instruction that transfers data to or from the device until the device is ready.
A loop of instructions is used to repeatedly check the status of the device until it is ready.
When the device becomes ready, it interrupts the program, transfers control to a subroutine that transfers the data, and then resumes the interrupted program.
Instructions are used to initialize a hardware controller that transfers a block of data concurrent with normal instruction execution. The controller interrupts when done.

## Slide 4: THE CRC32 ALGORITHM
uint32_t crc32(void *data, uint32_t bytes) { uint8_t *pu8 = (uint8_t *) data ; uint32_t crc = 0xFFFFFFFF ; // Initial value while (bytes-- != 0) { // Zero-extend and reverse bit order of input data uint32_t u32 = ReverseBits((uint32_t) *pu8++) ; for (int k = 0; k < 8; k++) // Update the CRC { if (((crc ^ u32) & 0x80000000) != 0) { crc = (crc << 1) ^ 0x04C11DB7 ; } else crc = crc << 1 ; u32 = u32 << 1 ; } } return ~ReverseBits(crc) ; // Reverse & invert final result }
The 32-bit Cyclic Redundancy Check (CRC32) is used to detect errors in the transmission of data.
CRC32 is used in Ethernet packets, video files, image files, etc.
CRC32 algorithms differ by:
The initial value of the crc
Possible reversal of data bits
A characterizing “polynomial”
Possible inversion of result

## Slide 5: BLOCKING I/O: THE CRC32 PERIPHERAL
#define pCRC_DR ((volatile uint32_t *) 0x40023000) #define pCRC_CR ((uint32_t *) 0x40023008) #define pRCC_AHB1ENR ((uint32_t *) 0x40023830) uint32_t crc32(void *data, uint32_t bytes) { uint32_t crc, crc_reg, *p32 = data ; *pRCC_AHB1ENR ¦= 1 << 12 ; // Enable CRC clock *pCRC_CR ¦= 0x00000001 ; // Reset the CRC calculator while (bytes >= 4) { *pCRC_DR = ReverseBits(*p32++) ; bytes -= 4 ; } crc_reg = *pCRC_DR ; crc = ReverseBits(crc_reg) ; if (bytes > 0) { uint32_t bits = 8 * bytes ; uint32_t xtra = 32 - bits ; uint32_t mask = (1 << bits) - 1 ; *pCRC_DR = crc_reg ; *pCRC_DR = ReverseBits((*p32 & mask) ^ crc) >> xtra ; crc = (crc >> bits) ^ ReverseBits(*pCRC_DR); } return ~crc ; }
Pointers (address expressions) created to access the device.
CRC32 device must be initialized.
The CRC32 device processes four bytes of data at a time in a loop.
Code following the loop handles any remaining data bytes.
Any access of the CRC Data Register stalls until the device is ready.

## Slide 6
uint32_t crc32(void *data, uint32_t bytes) ; crc32: LDR R3,=1 LDR R2,=0x42470630 // Use bit band address to STR R3,[R2] // enable the CRC Clock LDR R2,=0x42460100 // Use bit band address to STR R3,[R2] // reset the CRC unit LDR R2,=0x40023000 // R2 = pCRC_DR L1: CMP R1,4 // while (bytes >= 4) BLO L2 // { LDR R3,[R0],4 // R3 = *p32++ ; RBIT R3,R3 // R3 = ReverseBits(R3) STR R3,[R2] // *pCRC_DR <-- R3 SUB R1,R1,4 // bytes -= 4 B L1 // } L2: LDR R3,[R2] // crc_reg (R3) <-- *pCRC_DR RBIT R12,R3 // crc (R12) = ReverseBits(R3) CBZ R1,L3 STR R3,[R2] // *pCRC_DR <-- crc_reg LSL R3,R1,3 // bits (R3) = bytes << 3 LDR R1,=1 // R1 = 1 LSL R1,R1,R3 // R1 = 1 << bits SUB R1,R1,1 // mask (R1) = R1 - 1 LDR R0,[R0] // R0 = *p32 AND R0,R0,R1 // R0 &= mask EOR R0,R0,R12 // R0 ^= crc RBIT R0,R0 // R0 = ReverseBits(R0) RSB R1,R3,32 // xtra (R1) = 32 – R3 LSR R0,R0,R1 // R0 >>= xtra STR R0,[R2] // *pCRC_DR <-- R0 LDR R0,[R2] // R0 <-- *pCRC_DR RBIT R0,R0 // R0 = ReverseBits(R0) LSR R12,R12,R3 // R12 = crc >> bits EOR R12,R0,R12 // R12 = (crc >> bits) ^ R0 L3: MVN R0,R12 BX LR
BLOCKING I/O: THE CRC32 PERIPHERAL
CRC32 device is initialized.
The CRC32 device processes four bytes of data at a time in a loop.
Code following the loop handles any remaining data bytes.
Any access of the CRC Data Register stalls until the device is ready.

## Slide 7: POLLED WAITING LOOP: THE RANDOM NUMBER GENERATOR
#define pRCC_AHB2ENR ((uint32_t *) 0x40023834) #define pRNG_CR ((uint32_t *) 0x50060800) #define pRNG_SR ((volatile uint32_t *) 0x50060804) #define pRNG_DR ((volatile uint32_t *) 0x50060808) void RNG_Initialize(void) { *pRCC_AHB2ENR ¦= (1 << 6) ; // Enable RNG clock src *pRNG_CR ¦= (1 << 2) ; // Enable RNG peripheral } uint32_t RNG_ReadValue(void) { while ((*pRNG_SR & 1) == 0) /* Polled waiting loop */ ; return *pRNG_DR ; }
Most devices have multiple "registers" (aka "ports"), each with its own memory address:
Control Register (Write-Only)
Status Register (Read-Only)
Data Register (Read/Write)
The device must be enabled and initialized before use.
Polled waiting loops read the status port and test the "ready" bit to see if the device is ready.
Once the device is ready, the data can be transferred.

## Slide 8: POLLED WAITING LOOP: THE RANDOM NUMBER GENERATOR
// void RNG_Initialize(void) ; RNG_Initialize: LDR R1,=0x42470698 // Address of RCC_AHB2ENR LDR R0,[R1] ORR R0,R0,1 << 6 // Enable RNG clock source STR R0,[R1] LDR R1,=0x50060800 // Address of RNG_CR LDR R0,[R1] ORR R0,R0,1 << 2 // Enable RNG peripheral STR R0,[R1] BX LR // Return // uint32_t RNG_ReadValue(void) ; RNG_ReadValue: LDR R1,=0x50060804 // Address of RNG_SR Poll: LDR R0,[R1] // Poll: Check to see if a new TST R0,1 // random number is available. BEQ Poll LDR R1,=0x50060808 // Address of RNG_DR LDR R0,[R1] // Read a new random number BX LR // Return
Note: There's not much justification for coding this in assembly!
Initialization Code
Waiting Loop Code
Data Transfer Code

## Slide 9: EXCEPTIONS & INTERRUPTS
Problem: Certain events require an immediate response and cannot wait for the processor to finish the current instruction sequence.
Solution: Exceptions cause the processor to suspend execution of the current instruction sequence to execute an exception handler to process the event.
Exceptions include interrupts, reset and hardware faults such as power fail, and fetching an invalid instruction.
Interrupt: A subset of exceptions triggered by a change in a peripheral device.
Exception number: Identifies the event
Exception handler: Processes the event (a function)
Vector table entry: Locates the handler (a table of handler addresses)
Priority number: Can another exception suspend a handler?
Interrupt Enable: Enables/Disables interrupts globally
Interrupt Mask: Enables/Disables interrupts individually
Thread Mode: Processor NOT executing a handler
Handler Mode: Processor IS executing a handler

## Slide 10: INTERRUPT-DRIVEN I/O
Exception Occurs: CPU completes, suspends or abandons the current instruction and then initiates an exception response sequence.
Exception Complete: Code continues where it left off as if nothing happened other than a slight delay.
Exception Response Sequence:
Pushes processor state onto the stack:
  PSR, return address, R0-R3, R12 and LR
Switches to Handler Mode (PSR24  1)
Retrieves the Exception Number
PC  VectorTable [ExceptionNumber]
Exception Handler:
1. Preserve R4-R11 as needed.
2. Process the exception
3. Restore R4-R11 as needed.
4. Return to interrupted code.
Exception Return: When BX LR is executed in Handler Mode, it unstacks and restores the processor registers (and thus previous mode).
Main Program

## Slide 11
#include <stdio.h> #include <stdint.h> #include "library.h" #define TIM2_IRQ 28 // Timer 2 interrupt number #define pTIM2_CR1 ((uint32_t *) 0x40000000) #define pTIM2_DIER ((uint32_t *) 0x4000000C) #define pTIM2_SR ((uint32_t *) 0x40000010) #define pTIM2_CNT ((uint32_t *) 0x40000024) #define pTIM2_PSC ((uint32_t *) 0x40000028) #define pTIM2_ARR ((uint32_t *) 0x4000002C) #define pRCC_APB1ENR ((uint32_t *) 0x40023840) #define pNVIC_ISER0 ((uint32_t *) 0xE000E100) volatile uint32_t tenths = 0 ; // Counts tenths of a second static uint32_t previous = 0 ; // Used to recognize a change void TIM2_IRQHandler(void) // Interrupt Handler { *pTIM2_SR &= ~1 ; // Clear interrupt request tenths++ ; // Increment tenths counter } int main(void) { InitializeHardware(HEADER, PROJECT_NAME) ; *pRCC_APB1ENR ¦= 1 ; // Power up timer 2 *pTIM2_PSC = 18000 ; // Setup prescaler and reload *pTIM2_ARR = 1000 - 1 ; // to interrupt 10 times/sec *pTIM2_DIER = 1 ; // Enable timer to interrupt *pTIM2_CR1 = 1 ; // Enable timer to count *pNVIC_ISER0 = 1 << TIM2_IRQ ; // Unmask timer interrupt asm ("cpsie i") ; // Enable interrupts while (1) { if (tenths == previous) continue ; printf("tenths = %u\n", (unsigned) tenths) ; previous = tenths ; } }
INTERRUPT-DRIVEN I/O: THE SYSTEM TIMER TICK
Data updated by interrupt
Timer Interrupt Handler
Timer Initialization code
Unmasking timer interrupts
Global Interrupt Enable
Interrupted code

## Slide 12: DIRECT MEMORY ACCESS
Transfers data independent of CPU
CPU must initialize …
Source and destination address
Byte count
DMA then transfers data from …
Peripheral Device to Memory
Memory to Peripheral Device
Memory to Memory
Transfer complete when byte count reaches zero.
For example, reading or writing data stored on a disk drive
Speed limited only by speed of the source and destination – no instruction execution overhead.

## Slide 13: DIRECT-MEMORY ACCESS: MEMORY-TO-MEMORY TRANSFER
#define pRCC_AHB1ENR ((uint32_t *) 0x40023830) #define pDMA_S0CR ((uint32_t *) 0x40026410) #define pDMA_S0NDTR ((volatile uint32_t *) 0x40026414) #define pDMA_S0PAR ((void **) 0x40026418) #define pDMA_S0M0AR ((void **) 0x4002641C) void DMASetUp(void *src, void *dst, uint16_t bytes) { *pRCC_AHB1ENR ¦= (1 << 22) ; // Enable DMA Clock *pDMA_S0CR = 0 ; // Disable DMA *pDMA_S0PAR = src ; // Setup source address *pDMA_S0M0AR = dst ; // Setup dest. address *pDMA_S0NDTR = (uint32_t) bytes ; // Setup byte count *pDMA_S0CR = 0x681 ; // Auto++, Mem-To-Mem, Go } int DMABusy(void) { return *pDMA_S0NDTR != 0 ; // remaining bytes? }
Initialization:
Source address
Destination address
Byte Count
Mode = Memory to Memory
Test for Completion:
Byte count == 0 ?

## Slide 14: DIRECT-MEMORY ACCESS: MEMORY-TO-MEMORY TRANSFER
DMASetUp2: LDR R3,=0x40023800 // RCC_BASE LDR R12,[R3,0x30] ORR R12,R12,(1 << 22) // Enable DMA Clock STR R12,[R3,0x30] LDR R3,=0x40026400 // DMA2_BASE LDR R12,=0 // Make sure DMA is disabled STR R12,[R3,0x10] STR R0,[R3,0x18] // Setup src address STR R1,[R3,0x1C] // Setup dst address STR R2,[R3,0x14] // Setup byte count LDR R0,=0x681 // Setup Autoincrement, STR R0,[R3,0x10] // Memory-To-Memory, Start BX LR // Return DMABusy2: LDR R0,=0x40026400 // DMA2_BASE LDR R0,[R0,0x14] // Get remaining byte count BX LR // Return
Initialization:
Source address
Destination address
Byte Count
Mode = Memory to Memory
Test for Completion:
Byte count == 0 ?

## Slide 15: THE CPU CLOCK CYCLE COUNTER
#define pDWT_CTRL ((uint32_t *) 0xE0001000) #define pDWT_CYCCNT ((volatile uint32_t *) 0xE0001004) #define pDEMCR ((uint32_t *) 0xE000EDFC) void StartClockCycleCounter(void) { *pDEMCR ¦= (1 << 24) ; // Enable use of DWT regs (set bit 24) *pDWT_CTRL ¦= (1 << 0) ; // Enable the counter (set bit 0) } uint32_t GetClockCycleCount(void) { return *pDWT_CYCCNT ; // Read the counter }
#include <stdio.h>
#include “library.h”
int main(void)
  {
  uint32_t start, stop ;
  InitializeHardware() ;
  start = GetClockCycleCount() ;
  ...
  // code to time
  ...
  stop = GetClockCycleCount() ;
  printf(“Time = %u Clock Cycles\n”,
  stop - start) ;
  return 0 ;
  }
Function StartClockCycleCounter is called by function InitializeHardware.

## Slide 16: MORE ACCURATE CYCLE COUNTS
Code whose execution time is to be measured
Time actually measured
Execution time of GetClockCycleCount
Execution time of GetClockCycleCount
strt = GetClockCycleCount() ;
stop = GetClockCycleCount() ;
xtra = stop – strt ;
strt = GetClockCycleCount() ;
... // code to be timed
stop = GetClockCycleCount() ;
cycles = (stop – strt) – xtra ;
strt
stop