## Slide 1: Chapter 6
Making Decisions and Writing Loops

## Slide 2: COMPARE INSTRUCTIONS
Instruction | Syntax | Operation | Notes
Compare | CMP Rn,Op2 | Rn – Op2 | Update flags N,Z,C and V
Compare Negative | CMN Rn, Op2 | Rn + Op2 | 
CMP is identical to the SUBS instruction, but discards the actual difference.
The assembler automatically replaces CMP Rn,─constant by CMN Rn,constant
Decisions in assembly require a two instruction sequence. A com-pare instruction compares two operands, followed by a conditional branch instruction that makes the actual decision to branch or not.
Op2 may be a small constant, a register, or a shifted register.

## Slide 3: TEST INSTRUCTIONS
Instruction | Syntax | Operation | Notes
Test | TST Rn, Op2 | Rn & Op2 | Updates flags N and Z; if shifted, Op2 may affect C flag
Test Equivalence | TEQ Rn, Op2 | Rn ^ Op2 | 
TST is used to test whether any of the bits in Rn specified by Op2 are 1’s.
TEQ is used to test whether Rn = Op2 without affecting the C or V flags.

## Slide 4: CONDITIONAL BRANCH INSTRUCTIONS
Equivalent if-then statement in assembly
LDR R0,s32 // CMP requires operand to be in a register CMP R0,10 // Compare s32 to 10 and ... BLE L1 // if (s32 <= 10) goto L1 L1: •••
Equivalent C code using goto and label
int32_t s32 ; if (s32 <= 10) goto L1 ; L1: •••
If-then statement in C
int32_t s32 ; if (s32 > 10) •••
then statement
then statement
then statement
  Decisions in assembly are like an if statement that controls a goto statement.
  A conditional branch instruction is written as “B” followed a condition code.

## Slide 5: CONDITIONAL BRANCH INSTRUCTIONS
Condition | Signed | Unsigned
> | GT (Greater Than) | HI (Higher Than)
>= | GE (Greater Than or Equal) | HS (Higher Than or Same)
< | LT (Less Than) | LO (Lower Than)
<= | LE (Less Than or Equal) | LS (Lower Than or Same)
== | EQ (Equal) | EQ (Equal)
!= | NE (Not Equal) | NE (Not Equal)
Signed: +7 GT -4 ? YES!
01112 > 11002 ?
Unsigned: 7 HI 12 ? NO!
  Signed and unsigned require different condition codes for magnitude comparisons!

## Slide 6: CHOOSING THE CONDITION
  If a condition doesn’t include the equality case, the opposite must. Vice-Versa!
  You can’t use the same condition as used in C to control an if-statement.

## Slide 7: COMPLETE CONDITION LIST
Code | Meaning | Requires
EQ | Equal | Z = 1
NE | Not equal | Z = 0
CS or HS | Carry set, or unsigned ≥ ("Higher or Same") | C = 1
CC or LO | Carry clear, or unsigned < ("Lower") | C = 0
MI | Minus/negative | N = 1
PL | Plus - positive or zero (non-negative) | N = 0
VS | Overflow | V = 1
VC | No overflow | V = 0
HI | Unsigned > ("Higher") | C = 1 && Z = 0
LS | Unsigned ≤ ("Lower or Same") | C = 0 ¦¦ Z = 1
GE | Signed ≥ ("Greater than or Equal") | N = V
LT | Signed < ("Less Than") | N ≠ V
GT | Signed > ("Greater Than") | Z = 0 && N = V
LE | Signed ≤ ("Less than or Equal") | Z = 1 ¦¦ N ≠ V
AL | Always (unconditional) | (Rarely used)
EQ and NE are used for signed and unsigned.
These are used for signed comparisons
These are used for unsigned comparisons
Never used. Included for completeness.

## Slide 8: IF-THEN-ELSE SEQUENCES
Assembly Code
LDR R0,s32 // is s32 > 0 ? CMP R0,0 BLE L2 B L3 // skip over else!! L2: else statement L3: ... // end of the if
C Source Code
int32_t s32 ; if (s32 > 0) then state else else stat
Converted to goto
int32_t s32 ; if (s32 <= 0) goto L2; goto L3; L2: L3:
then statement
then statement
else statement
  Without the unconditional branch, the else statement will always be executed!
then statement
else statement
else statement

## Slide 9: IF-THEN-ELSE SEQUENCES
C Source Code | Assembly Code
int32_t s32 ; if (s32 == 1) statement #1 else if (s32 == 2) statement #2 else if (s32 == 3) statement #3 | LDR R0,s32 // Is s32 > 0 ? CMP R0,1 BNE L2 statement #1 B L4 // skip to end! L2: CMP R0,2 BNE L3 statement #2 B L4 // skip to end! L3: CMP R0,3 BNE L4 statement #3 L4: ... // end of chain
  statement #1
  statement #3
  statement #2
  statement #1
  statement #2
  statement #3
  These unconditional branches insure that only one statement is executed.

## Slide 10: COMPARING 64-BIT INTEGERS Method #1
LDRD R0,R1,a64 // get a64 (R0=LS Half; R1=MS Half)
LDRD R2,R3,b64 // get b64 (R2=LS Half; R3=MS Half)
CMP R1,R3 // compare most-significant halves
BGT L1 // use BHI if operands are unsigned
BLT L2 // use BLO if operands are unsigned
CMP R0,R2 // MS halves ==, compare LS halves
BLS L2 // use BLS for signed and unsigned
L1: // a64 > b64
B L3
L2: // a64 <= b64
L3: ...
then statement
else statement
if (a64 > b64) else C
then statement
else statement
  This solution is based on comparing digits in a most-to-least significant order.

## Slide 11: COMPARING 64-BIT INTEGERS Method #2
LDRD R0,R1,a64 // get a64 (R0 = LS Half; R1 = MS Half)
LDRD R2,R3,b64 // get b64 (R2 = LS Half; R3 = MS Half)
SUBS R0,R0,R2 // subtract LS halves, capture borrow
SBCS R1,R1,R3 // subtract MS halves w/brw; set flags
BLE L1 // use BLS if operands are unsigned
// a64 > b64
B L2
L1: // a64 <= b64
L2: ...
then statement
else statement
if (a64 > b64) else C
then statement
else statement
  Faster approach uses a 64-bit subtraction to eliminate unnecessary branching.

## Slide 12: IT BLOCKS
C Source Code | Corresponding Assembly Code
int32_t a, b, c ; if (a > 0) b = 1 ; else c = 2 ; | LDR R0,a // Is a > 0 ? CMP R0,0 ITTEE GT // controls 4 instructions LDRGT R0,=1 // yes: b  1 STRGT R0,b LDRLE R0,=2 // no: c  2 STRLE R0,c
Every branch taken causes a delay to refill the instruction pipeline, reducing performance. If-Then (IT) blocks avoid this by selectively enabling or disabling the execute phase of one to four instructions.
The "IT Block"
These suffixes specify the condition that enables the instruction.
This specifies the condition that enables the next instruction.
Up to 3 additional instructions can be controlled by appending T’s or E’s.

## Slide 13: IT BLOCKS A fast 64-bit unsigned max function
// uint64_t uMax64(uint64_t u1, uint64_t u2) .globl uMax64 uMax64: SUBS R12,R2,R0 // perform a 64-bit subtract SBCS R12,R3,R1 // set flags, discard result ITT HI // if (u2 > u1) ... MOVHI R1,R3 // then return u2 instead of u1 MOVHI R0,R2 // by copying u2 into R1.R0 BX LR // return

## Slide 14: COMPOUND CONDITIONALS
then statement
if (x < –100 || x > +100)
  if (x < –100) goto L1 ;
  if (x > +100) goto L1 ;
  goto L2 ;
L1:
L2: ...
then statement
LDR R0,x
CMP R0,-100 // if (x < –100)
BLT L1 // goto L1
CMP R0,100 // if (x <= +100)
BLE L2 // goto L2
L1:
L2: ...
then statement
  if (x < –100) goto L1 ;
  if (x <= +100) goto L2 ;
L1:
L2: ...
then statement
One condition per statement, each controlling a goto.
last goto eliminated by reversing the last compare.
C statements now easily map 1-to-1 into assembly
When you see this pattern, the last goto can be eliminated.

## Slide 15: COMPOUND CONDITIONALS
then statement
if (x >= –100 && x <= +100)
  if (!(x >= –100 && x <= +100)) goto L1 ;
L1: ...
then statement
  if (x < –100 || x > +100) goto L1 ;
L1: ...
then statement
  if (x < –100) goto L1 ;
  if (x > +100) goto L1 ;
L1: ...
then statement
LDR R0,x
CMP R0,-100 // if (x < –100)
BLT L1 // goto L1
CMP R0,100 // if (x > +100)
BGT L1 // goto L1
L1: ...
then statement
Invert the entire condition so the if controls a goto.
Use DeMorgan’s Law to replace && by ||.
Separate the conditions as we did before.
C statements now easily map 1-to-1 into assembly

## Slide 16: COMPOUND CONDITIONALS Summary with else statements
Compound Conditional in C | Rewritten with goto’s and labels | Assembly language version
if (x > 0 && x < 9) else | if (x <= 0) goto L1 ; if (x >= 9) goto L1 ; goto L2 ; L1: L2: ... | LDR R0,x CMP RO,0 BLE L1 CMP R0,9 BGE L1 B L2 L1: L2: ...
if (x == 0 ¦¦ x == 9) else | if (x == 0) goto L1 ; if (x != 9) goto L2 ; L1: goto L3 ; L2: L3: | LDR R0,x CMP R0,0 BEQ L1 CMP R0,9 BNE L2 L1: B L3 L2: L3: ...
then statement
else statement
then statement
else statement
then statement
else statement
then statement
else statement
then statement
else statement
then statement
else statement

## Slide 17: WRITING LOOPS
Instruction | Syntax | Operation
Compare and Branch if Zero | CBZ Rn,label | Branch to label If Rn=0
Compare and Branch if Non-Zero | CBNZ Rn,label | Branch to label If Rn≠0
CMP R0,0 CBZ R0,L1
BEQ L1
CMP R0,0 CBNZ R0,L1
BNE L1
Sometimes used at the top of a while or for loop
Sometimes used at the bottom of a do-while loop

## Slide 18: WRITING LOOPS
// uint32_t Factorial(uint32_t n) Factorial: LDR R1,=1 // initialize: Factorial = 1 top: CBZ R0,done // check n: Done if n is 0 MUL R1,R1,R0 // factorial *= n SUB R0,R0,1 // decrement n and update flags B top // branch to top of loop done: MOV R0,R1 // leave result in R0 BX LR // return
Test for completion
Body of the loop
Unconditional branch to repeat the loop.
Loop initialization

## Slide 19: WRITING LOOPS
// uint32_t gcd(uint32_t u1, uint32_t u2) gcd: CMP R0,R1 // continue? (u1 != u2) BEQ done ITE HI // loop body and update: SUBHI R0,R0,R1 // u1 <- u1 – u2 SUBLS R1,R1,R0 // u2 <- u2 – u1 B gcd // branch to top of loop done: BX LR // return: R0 = gcd(u1,u2)
Test for completion
Body of the loop
Unconditional branch to repeat the loop.
This loop needs no initialization

## Slide 20: FOR LOOPS
for (initialization; condition; update)
{
loopBody ;
}
initialization ;
while (condition)
{
loopBody ;
update ;
}
initialization ;
L1: if (!condition) goto L2 ;
loopBody ;
update ;
goto L1 ; // repeat
L2:
initialization ;
while (1)
{
if (!condition) break ;
loopBody ;
update ;
}

## Slide 21: WHILE LOOP WITH COMPOUND CONDITIONAL
while (condition1 && condition2)
  {
  loopBody ;
  }
while (1)
{
if (!condition1 || !condition2) break ;
loopBody ;
  }
while (1)
{
if (!condition1) goto L1 ;
if (!condition2) goto L1 ;
loopBody ;
  }
  L1:
L0: if (!condition1) goto L1 ;
if (!condition2) goto L1 ;
loopBody ;
goto L0 ;
  L1:

## Slide 22: WHILE LOOP WITH COMPOUND CONDITIONAL
while (condition1 || condition2)
  {
  loopBody ;
  }
while (1)
{
if (condition1) goto L1 ;
if (condition2) goto L1 ;
goto L2;
L1: loopBody ;
}
L2:
while (1)
{
if (condition1 || condition2) goto L1 ;
  break ;
  L1: loopBody ;
}
L0: if (condition1) goto L1 ;
if (condition2) goto L1 ;
goto L2 ;
L1: loopBody ;
  goto L0 ;
  L2:

## Slide 23: DO-WHILE LOOP WITH COMPOUND CONDITIONAL
  do
  {
  loopBody ;
  } while (condition1 || condition2) ;
do
{
loopBody ;
if (condition1) continue ;
if (condition2) continue ;
break ;
} while(1) ;
do
{
  loopBody ;
if ( condition1 || condition2) continue ;
break ;
} while (1) ;
L0: loopBody ;
  if (condition1) goto L0 ;
  if (condition2) goto L0 ;

## Slide 24: DO-WHILE LOOP WITH COMPOUND CONDITIONAL
  do
  {
  loopBody ;
  } while (condition1 && condition2) ;
do
{
loopBody ;
if (!condition1 || !condition2) break ;
} while(1) ;
do
{
  loopBody ;
if (condition1 && condition2) continue ;
break ;
} while (1) ;
L0: loopBody ;
  if (!condition1) goto L1 ;
  if (!condition2) goto L1 ;
  goto L0 ;
  L1: