## Slide 1: Chapter 7 Supplement
(More on Manipulating Bits)

## Slide 2: Using ASR to produce 0 or +/- 1
ASR R0,R1,31 // R0 = -1 if R1 < 0, else 0
NEG R0,R0 // R0 = +1 if R1 < 0, else 0

## Slide 3: (1 << k) = 2k (A single 1 shifted left k bits)
(1 << 4) = 00100002
= 1610
= 24
// If k is a constant
LDR R0,1<<4
// If k is a variable
LDR R0,=1 LDR R1,k LSL R0,R0,R1

## Slide 4: 2k-1 (A string of k 1’s)
26 = 0010000002
-000000001
26-1 = 0001111112
Six 1’s
// If k is a constant
LDR R0,(1<<6)-1
// If k is a variable
LDR R0,=1 LDR R1,k LSL R0,R0,R1
SUB R0,R0,1
106 = 00100000010
-000000001
106-1 = 00099999910
Six 9’s

## Slide 5: Is a Power of 2?
TST is a Bitwise-AND that discards the result, but sets the flags
LDR R0,x
SUB R1,R0,1
TST R0,R1
BEQ IsPowerOf2
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Any power of 2 will be all 0’s except for a single 1
DIsclaimer: This code detects x=0 as a power of 2.
These bits of the result will be zero if x is a power of 2
Any 1’s here will cause 1’s to appear in R1 after the SUB

## Slide 6: 2k-2n = 2n(2k-n-1) (A string of k 1’s shifted left n bits)
// If k and n are constants
LDR R0,(1<<7)-(1<<2)
// If k and n are variables
LDR R0,=1 LDR R1,k
LDR R2,n
LSL R1,R0,R1 // 1 << k
LSL R2,R0,R2 // 1 << n
SUB R0,R1,R2
27 = 0010000000
-0000000100
27- 22 = 0001111100
Five 1’s, shifted left by 2 bits

## Slide 7: Bitwise-AND
a | b | a & b
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 & b = 0
1 & b = b
b31 |  | b5 | b4 | b3 | b2 | b1 | b0
b31 |  | b5 | b4 | b3 | b2 | b1 | b0
0 |  | 0 | 1 | 1 | 1 | 0 | 0
0 |  | 0 | 1 | 1 | 1 | 0 | 0
0 |  | 0 | b4 | b3 | b2 | 0 | 0
0 |  | 0 | b4 | b3 | b2 | 0 | 0
AND R1,R0,0b11100
R0
R1

## Slide 8: Extracting Right-Aligned Unsigned Bitfield (Using Bitwise-AND to Insert 0’s)
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 11 | 10 |  |  |  |  |  |  |  |  |  | 0
? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 11 | 10 |  |  |  |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  |  |  |  |  |  |  | 
AND R0,R0,(1 << 11) -1
width = 11

## Slide 9: Using ASR to produce a bitmask
// Selection: if (R0 < 0) R5 = R2 ; else R5 = R4
AND R2,R1,R0,ASR 31 // R2 = R1 if R0 < 0, else 0
NEG R0,R0 // R0 = -R0
AND R4,R3,R0,ASR 31 // R4 = R3 if R0 < 0, else 0
ORR R5,R3,R4 // Either R3 or R4 will be 0

## Slide 10: Extracting Unsigned Bitfields (Without UBFX)
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 15 | 14 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9 | 8 |  |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  |  | 23 | 22 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
LSL R0,R0,8
LSR R0,R0,23
32 – (lsb + width) = 8
32 – len = 23
width = 9
lsb = 15

## Slide 11: Extracting Signed Bitfields (Without SBFX)
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 15 | 14 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9 | 8 |  |  |  |  |  |  |  | 0
s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  |  | 23 | 22 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
LSL R0,R0,8
ASR R0,R0,23
32 – (lsb + width) = 8
32 – len = 23
width = 9
lsb = 15
sign bit

## Slide 12: Bitwise-OR
a | b | a ¦ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
0 | b = b
1 | b = 1
b31 |  | b5 | b4 | b3 | b2 | b1 | b0
b31 |  | b5 | b4 | b3 | b2 | b1 | b0
0 |  | 0 | 1 | 1 | 1 | 0 | 0
0 |  | 0 | 1 | 1 | 1 | 0 | 0
b31 |  | b5 | 1 | 1 | 1 | b1 | b0
b31 |  | b5 | 1 | 1 | 1 | b1 | b0
ORR R1,R0,0b11100
R0
R1

## Slide 13: Using Bitwise-OR to Combine Bitfields
a31 |  | a5 | a4 | 0 | 0 | 0 | 0
a31 |  | a5 | a4 | 0 | 0 | 0 | 0
0 |  | 0 | 0 | b3 | b2 | b1 | b0
0 |  | 0 | 0 | b3 | b2 | b1 | b0
a31 |  | a5 | a4 | b3 | b2 | b1 | b0
a31 |  | a5 | a4 | b3 | b2 | b1 | b0
ORR R2,R1,R0
R0
R2
R1
Must be 0’s
Must be 0’s
a | b | a ¦ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
0 | b = b
1 | b = 1

## Slide 14
Inserting Bitfields (Without BFI)
a31 |  | a5 | ? | ? | ? | a1 | a0
a31 |  | a5 | ? | ? | ? | a1 | a0
? |  | ? | ? | ? | b2 | b1 | b0
? |  | ? | ? | ? | b2 | b1 | b0
a31 |  | a5 | 0 | 0 | 0 | a1 | a0
a31 |  | a5 | 0 | 0 | 0 | a1 | a0
? |  | ? | b2 | b1 | b0 | 0 | 0
? |  | ? | b2 | b1 | b0 | 0 | 0
0 |  | 0 | b2 | b1 | b0 | 0 | 0
0 |  | 0 | b2 | b1 | b0 | 0 | 0
a31 |  | a5 | b2 | b1 | b0 | a1 | a0
a31 |  | a5 | b2 | b1 | b0 | a1 | a0
R0
R1
BIC R0,R0,0b11100
R0
LSL R1,R1,2
AND R1,R1,0b11111
ORR R0,R0,R1
R1

## Slide 15: Exclusive-OR Absolute Value
// uint32_t AbsValue(int32_t s32) AbsValue: // s32 < 0: else: EOR R1,R0,R0,ASR 31 // R1 = ~s32 R1 = s32 SUB R0,R1,R0,ASR 31 // R0 = ~s32 + 1 R0 = s32 BX LR // Return
  Fast! Avoids using making a compare and branch so that the instruction pipeline never stalls.
All 1’s if s32 < 0
All 0’s if s32 ≥ 0
-1 if s32 < 0
0 if s32 ≥ 0

## Slide 16: Exclusive-OR Swap of R0 and R1
// Standard method
// (requires 3rd register)
MOV R2,R0
MOV R0,R1
MOV R1,R2
// Exclusive-OR method
// No extra registers needed
EOR R0,R0,R1
EOR R1,R0,R1
EOR R0,R0,R1
0011
1011
R1
R0
1000
1011
0011
Exclusive-OR is 1 wherever the bits are different

## Slide 17: More Bit-Manipulation Tricks: http://graphics.stanford.edu/~seander/bithacks.html