## Slide 1: Chapter 13
Inline Code

## Slide 2: INLINE CODE
Goal: Optimize execution time
Issue: Call-Return overhead of BL and BX
Solutions: (1) Inline Functions
(2) Inline Assembly
(3) Combining (1) and (2)

## Slide 3: INLINE FUNCTIONS
Function Call | Is NOT an inline function | IS an inline function
 | int32_t Add1(int32_t a) { return a + 1 ; } | static inline int32_t Add1(int32_t a) { return a + 1 ; }
y = Add1(x) ; | LDR R0,x BL Add1 STR R0,y | LDR R0,x ADD R0,R0,1 STR R0,y
Calling a regular function requires time to execute the BL and BX instructions, but for large functions, it saves memory at the expense of speed.
Making the function inline eliminates the BL and BX instructions and their execution, but replicates the function code everywhere a call (BL) would have appeared, saving time at the possible expense of memory.

## Slide 4: INLINE FUNCTIONS
Facts about Inline Functions:
Inline functions are replicated, not called
An inline function is written in C
  Easier to use than inline assembly
  Independent of the target processor
Must be defined and called in same file
More appropriate for small functions
Compiler makes decision to inline or not

## Slide 5: INLINE ASSEMBLY
A way to insert assembly language source code statements directly into a C program
Operations not easily implemented in C:
  Rotates and arithmetic shift right
  Bit-field insertion and extraction
  Bit and byte reversals
  Double length products
Eliminates the need to call an assembly language function.

## Slide 6: INLINE ASSEMBLY
Two forms:
  Basic asm: Gives specific instruction parameters that the compiler cannot modify.
  Extended asm: More difficult to write than basic asm, but sometimes necessary to interact correctly with the compiler’s optimizer.

## Slide 7: INLINE ASSEMBLY Option 1: Basic asm
Syntax:
  asm (
  AssemblerInstructions
  ) ;
Example:
uint32_t x, y ;
...
// Rotate x right by 1 bit:
asm (
"LDR R0,x \n\t"
"ROR R0,R0,1 \n\t"
"STR R0,y "
) ;
One or more lines of code separated by whitespace. All but the last must end with \n\t.
Refernces to labels like “x” and “y” require that they be global (declared outside all functions)

## Slide 8: INLINE ASSEMBLY Option 2: Extended asm
Syntax:
  asm { volatile } (
    AssemblerTemplate
    : OutputOperands
    { : InputOperands
    { : Clobbers } }
    ) ;
Curly braces surround optional components; the curly braces are not part of what is written
Colons separate components
AssemblerTemplate: Instruction templates w/operand placeholders & options
OutputOperands: Specifies C variables to be used as destination operands
InputOperands: Specifies C variables to be used as source operands
Clobbers: A list of other items modified by side effects of the code
Do not write instructions to load an input variable or to store a result. The compiler figures out how to do that from InputOperands and OutputOperands.

## Slide 9: INLINE ASSEMBLY Option 2: Extended asm
Example:
uint32_t x, y ;
// Rotate x right by 1 bit:
asm( "ROR %[dst],%[src],1" // Template
: [dst] "=r" (y) // Output operand
: [src] "r" (x) // Input operand
) ;
Code to load and store the operands is generated by the compiler. Registers to use are chosen by the compiler.

## Slide 10: AssemberTemplate Component
One or more instruction templates, written as strings, separated by whitespace.
Instruction operands specified explicitly:
  "MOV R0,0 \n\t"
Or by reference to the OutputOperands or InputOperands:
  "MOV %[identifier],0 \n\t"

## Slide 11: Input/Output Operand Components
[ identifier ] constraint ( expression),
[ identifier ] constraint ( expression),
...
[ identifier ] constraint ( expression)
identifier corresponds to an input or output operand in the AssemblerTemplate.
constraint specifies what kind of values (variable, integer constant, floating-point constant, etc.) may be used.
expression is a C expression – usually just a variable name.
One or more entries, separated by commas.

## Slide 12: INLINE ASSEMBLY EXAMPLE
int result, value, numbits ;
...
value = ... ;
numbits = ... ;
asm (
  "ASR %[dst],%[src],%[shift]"
  : [dst] "=r" (result)
  : [src] "r" (value),
  [shift] "ri" (numbits)
) ;
printf("%d ASR %d = %d\n", value, numbits, result) ;
AssemblerTemplate
OutputOperand
InputOperands
Operand Constraints

## Slide 13: INLINE ASSEMBLY Operand Constraints
Constraint | Operand is allowed to be ...
r | One of the core registers (R0 through R15)
w | One of the floating-point registers (S0 through S31)
i | An integer constant
X | Any kind of operand is allowed
OperandConstraints are specified as a string containing one or more options, possibly preceded by modifiers (next).

## Slide 14: INLINE ASSEMBLY Constraint Modifiers
Modifier | When used as a prefix to 'r' or 'w' in the constraint string of an OutputOperand
= | The first use of the register is as the write-only output of an instruction. The register may be used by a subsequent instruction as an input or reused as an output. (Only used in the constraint string of an OutputOperand.)
+ | The first use of the register is to provide an input value to an instruction, but is used again later as an output – either by the same or a subsequent instruction. (Only used in the constraint string of an OutputOperand.)
& | An output register that should not be a reused input register – usually because an instruction later in the same asm statement needs one of the input operands. (Only used in conjunction with "=", as in "=&r".)
InputOperands are read-only.

## Slide 15: Constraint Modifier "="
asm
  (
  "MOV %[reg],0 \n\t"
"MSR APSR_nzcvq,%[reg] "
: [reg] "=r" (temp)
: // No InputOperands
: "cc"
  ) ;
1st used as an output
“temp” is a variable in C that may not otherwise be used
“=” tells the compiler that the register’s original contents are irrelevant and may be overwritten.
Used 2nd as an input

## Slide 16: Constraint Modifier "+"
asm
  (
"CMP %[reg],100 \n\t"
"IT HI \n\t"
"MOVHI %[reg],100 "
  : [reg] "+r" (score)
  : // No InputOperands
  ) ;
1st used as an input
Used 2nd as an output
“+” tells the compiler that the operand’s original contents are needed, but are not preserved.
C variable “score” will be compared to 100 and possibly assigned the value 100.

## Slide 17: Constraint Modifier "&"
asm
  (
"SDIV %[quot],%[dvnd],%[dvsr] \n\t"
"MLS %[rem],%[quot],%[dvsr],%[dvnd] " : [quot] "=&r" (quotient),
[rem] “=r” (remainder)
  : [dvnd] “r” (dividend),
  [dvsr] “r” (divisor)
  ) ;
“&” tells the compiler that it shouldn’t reuse a input register whose contents have already been used.
OutputOperand “quot” must not reuse the same register as used for “dvnd” or “dvsr” since both are needed later in the MLS.

## Slide 18: INLINE ASSEMBLY Example: Constraints and Modifiers
static inline int32_t ASR(int32_t value, uint32_t numbits)
  {
  int32_t result ;
  asm ("ASR %[dst],%[src],%[shift]"
  : [dst] "=r" (result) // OutputOperands
  : [src] "r" (value), // InputOperands
  [shift] "r" (numbits)
  ) ;
  return result ;
  }
The "r" requires that the ASR use a register for this operand
The "=" is required because this is an output.

## Slide 19: The Clobbers Component
A comma-separated list of strings, each specifying a resource (a register or the flags) modified by the template as a side-effect (not listed as an OutputOperand).
asm ( "MOV R0,0 \n\t"
"MSR APSR_nzcvq,R0 "
: // No OutputOperands
: // No InputOperands
: "cc", "r0" // Clobbers flags and R0
) ;
In the clobbers list, registers must be specified using lower case.
Using a specific register hinders the optimizer
The optimizer only knows about registers that the compiler has assigned – not any that you specify literally, like R0 here.

## Slide 20: The Clobbers Component
uint32_t newflags ;
...
newflags = 0 ;
...
asm ( "MSR APSR_nzcvq,%[src]"
: // No OutputOperands
: [src] "r" (newflags) // InputOperand
: "cc" // Clobbers flags
) ;
The compiler chooses which register to use for "newflags" and generates instructions to load it with a zero.

## Slide 21: Combining INLINE FUNCTIONS with INLINE ASSEMBLY
Function Call | Constraint = "ir" | Constraint = "r"
y = ASR(x, 5) ; | LDR R0,x ASR R0,R0,5 STR R0,y | LDR R0,x LDR R1,=5 ASR R0,R0,R1 STR R0,y
static inline int32_t ASR(int32_t value, uint32_t numbits)
  {
  int32_t result ;
  asm ("ASR %[dst],%[src],%[shift]"
  : [dst] "=r" (result) // OutputOperands
  : [src] "r" (value), // InputOperands
  [shift] "ir" (numbits)
  ) ;
  return result ;
  }
"ir" allows ASR to use a register or a constant for its 3rd operand.

## Slide 22: 64-bit Operands
int64_t dst, src;
...
// 64-bit arithmetic right shift
asm ( "ASRS %[dstHi],%[srcHi],1 \n\t"
"RRX %[dstLo],%[srcLo] "
: [dstLo] "=r" (((uint32_t *) &dst)[0]),
[dstHi] "=r" (((uint32_t *) &dst)[1])
: [srcLo] "r" (((uint32_t *) &src)[0]),
[srcHi] "r" (((uint32_t *) &src)[1])
: "cc"
) ;

## Slide 23: The Optional Volatile Keyword
Prevents compiler optimizations that may modify, move, or even discard your code.
Only use when needed because it may prevent legitimate optimizations that are beneficial.
Guideline: Don’t use volatile if you have no side effects.

## Slide 24: The Optional Volatile Keyword
int k, temp ;
...
for (k = 0; k < 10000; k++)
{
asm volatile
  (
  "MOV %[register],%[register]"
  : [register] "+r" (temp)
  ) ;
}
Suppose this asm statement was used to simply create a delay.
Without the volatile keyword, the optimizer might consider it useless and remove it (and thus the loop as well).

## Slide 25: Resolving Dependencies (An Ineffective Solution)
Used to prevent optimizer from moving other code relative to your asm statement.
float series, term ;
uint32_t temp ;
...
// Change rounding mode to truncate
asm volatile (
  "VMRS %[reg],FPSCR \n\t"
  "ORR %[reg],%[reg],0x3 << 22 \n\t"
  "VMSR FPSCR,%[reg] "
  : [reg] "=r" (temp)
  ) ;
series += term ;
Programmer wants to change the rounding mode BEFORE performing the floating-point addition (series += term).
Prevents optimizer from moving the asm statement, but does NOT prevent it from moving the floating-point addition!

## Slide 26: Resolving Dependencies (An effective solution)
Used to prevent optimizer from moving other code relative to your asm statement.
float series, term ;
uint32_t temp ;
...
// Change rounding mode to truncate
asm volatile (
  "VMRS %[reg],FPSCR \n\t"
  "ORR %[reg],%[reg],0x3 << 22 \n\t"
  "VMSR FPSCR,%[reg] "
  : [reg] "=r" (temp),
  "=X" (series) // artificial dependency
  ) ;
series += term ;
This OutputOperand component creates an “artificial dependency” that tells the optimizer that the asm statement changes the value of "series" (although it actually does not).
Remove the volatile keyword. It doesn’t solve this dependency problem.

## Slide 27: COMBINING INLINE FUNCTIONS AND INLINE ASSEMBLY
An asm statement simply generates code wherever it appears.
Encapsulate it in a function to be able to use it more than once.
Use an inline function to eliminate the call/return overhead.
Use extended asm to allow the compiler to choose the registers.