## Slide 1: Chapter 2
Binary Number Systems

## Slide 2: Symbols and their values used in positional number systems
System | Radix | Digit Symbols | Corresponding Digit Values
Binary | 2 | 0,1 | 0,1
Decimal | 10 | 0,1,2,3,4, 5,6,7,8,9 | 0,1,2,3,4, 5,6,7,8,9
Hex | 16 | 0,1,2,3,4,5,6,7, 8,9,A,B,C,D,E,F | 0,1,2,3,4,5,6,7, 8,9,10,11,12,13,14,15

## Slide 3: POLYNOMIAL EVALUATION
Representation:
where: are the digit symbols
Interpretation: + +
  where: are the corresponding digit values
  and: is the radix (number base)

## Slide 4: POLYNOMIAL EVALUATION
547
Symbolic representation (What we write)
Numeric interpretation
(What we understand)
Subscript used to indicate the radix (number base)
Digit values (coefficients)
Positional weights (powers of the radix)
= 5×102 + 4×101 + 7×100
= 5×100 + 4×10 + 7×1
= 500 + 40 + 7
= 547
10
The result of polynomial evaluation is always a decimal number, regardless of the radix used in the original representation.

## Slide 5: Converting from ANY Radix to Decimal
Example: Converting from Radix 5 to Decimal
31245  = 3×53 + 1×52 + 2×51 + 4×50
= 3×125 + 1×25 + 2×5 + 4×1
= 375 + 25 + 10 + 4
= 41410
NOTE: Polynomial evaluation may be used to convert from ANY radix to decimal. The positional weights simply become powers of the radix.

## Slide 6: CONVERT BINARY TO DECIMAL (Using Polynomial Evaluation)
10112  = 1×23 + 0×22 + 1×21 + 1×20
= 1×8 + 1×2 + 1×1
= 8 + 2 + 1
= 1110

## Slide 7: EXTENDING POLYNOMIAL EVALUATION TO NUMBERS WITH A FRACTIONAL PART
10.0101112 
= 1×21 + 0×20 + 0×2-1 + 1×2-2 + 0×2-3
+ 1×2-4 + 1×2-5 + 1×2-6
= 1×21 + 1×2-2 + 1×2-4 + 1×2-5 + 1×2-6
= 2 + 1/4 + 1/16 + 1/32 + 1/64
= 2 + 0.25 + 0.0625 + 0.03125 + 0.015625
= 2.35937510
  Tedious! Four divisions and long decimal fractions!

## Slide 8: AN EASIER METHOD
10.0101112
= (1×27 + 0×26 + 0×25 + 1×24 + 0×23
+ 1×22 + 1×21 + 1×20)/26
= (128 + 16 + 4 + 2 + 1)/64
= 151/64
= 2.35937510
6 fractional digits
  Only a single division!
= 100101112 / 26

## Slide 9: Converting Fractions
Sometimes a fractional value has a finite representation in one number base, but not in another:
.333333333333
.0001100110011
This can happen whenever the destination radix is not divisible by one of the prime factors of the source radix.

## Slide 10: Representation Error
Computers store numbers using a fixed number of digits (aka, “fixed precision”)
Some values may not have a finite representation in binary (e.g., )
Limiting the number of digits introduces a representation error:
.0001100 (8 bits) = .0976562510

## Slide 11: CONVERTING DECIMAL TO BINARY
Method 1: Separate problem into two parts:
Integer Part: Use repeated division
Fractional Part: Use repeated multiplication
Method 2: Decompose the decimal number into a corresponding sum of powers of 2.

## Slide 12: CONVERTING DECIMAL TO BINARY Method 1: Integer Part (Repeated Division)
N N÷2 Remainder Result
13 6 1
6 3 0
3 1 1
1 0 1
1.
01.
101.
1101.
NOTE: Repeated division may be used to convert from decimal to ANY radix. Simply divide by the radix.
  Digits are produced right-to-left starting from the radix point.
STOP

## Slide 13: CONVERTING DECIMAL TO BINARY Method 1: Fractional Part (Repeated Multiplication)
Product Whole Fractional
N (2×N) Part Part Result
.1 0.2 0 .2 .0
.2 0.4 0 .4 .00
.4 0.8 0 .8 .000
.8 1.6 1 .6 .0001
.6 1.2 1 .2 .00011
NOTE: Repeated multiplication may be used to convert from decimal to ANY radix. Simply multiply by the radix.
  Digits are produced left-to-right starting from the radix point.
Begins to repeat!

## Slide 14: CONVERTING DECIMAL TO BINARY Method 2: Decomposition
k | 2k
6 | 64
5 | 32
4 | 16
3 | 8
2 | 4
1 | 2
0 | 1
-1 | .5
-2 | .25
-3 | .125
-4 | .0625
Convert 75.310 to Binary:
Whole Part:
75 = 64 + 8 + 2 + 1
= 10010112
Fractional Part (approximation):
.3 = .25 + .0625
= .01012

## Slide 15: INFINITE PRECISION
Placing an infinite number of values on the number line requires a representation that imposes no limit on the number of digits.
Incrementing any number always moves to the right, producing a result that is always greater than the previous.

## Slide 16: THE EFFECT OF FIXED PRECISION (Using a number circle instead of a line)
  Overflow: Occurs when an arithmetic result is beyond the min or max limits.
Labels inside the circle are symbolic representations.
Fixed Precision
Fixed # of digits
Finite # of values
min and max limits
min
max
Wrap Around
=
Labels outside the circle are the corresponding numeric interpretations.

## Slide 17: TWO’S COMPLEMENT REPRESENTATION OF SIGNED BINARY INTEGERS
  Overflow: No longer occurs between 0000 and 1111.
There are several possible ways to represent signed binary numbers.
Two’s complement is the most common.
Most-Significant Bit: 0 if positive, 1 if negative.
min
max
  Negative Values: Not simply a 1 followed by magnitude bits.
Wrap Around

## Slide 18: Changing the Sign of a Two’s Complement Number (Method 1)
If +2010 = 000101002
Then -2010 = ????????2
  Change every bit: 00010100
  11101011
  Then add 1: +1 11101100
. . .
  Simply changing the most-significant bit is NOT the same and doesn’t work!
  Consider what happens when the starting value is a full-scale negative value, such as -12810 = 100000002

## Slide 19: Changing the Sign of a Two’s Complement Number (Method 2)
If +2010 = 000101002
Then -2010 = ????????2
Copy right-to-left 00010100
through first 1:
Copy opposite of all remaining bits:
. . .
. . .
100
11101

## Slide 20: CONVERTING SIGNED DECIMAL TO TWO’S COMPLEMENT
Positive values:
  Convert as if unsigned
  Zero extend (add 0’s on the left) to fill out the representation to the desired number of bits
  Note: Most-significant bit must be 0
Negative values:
  Find corresponding positive representation as above
  Find the "2’s complement" of the result.

## Slide 21: CONVERTING SIGNED DECIMAL TO TWO’S COMPLEMENT
Example: Find the 8-bit 2’s complement representation of -2510
Convert the magnitude to unsigned binary:
      2510 = 16 + 8 + 1  110012
Zero extend to 8 bits:
      11001 00011001
Find the 2’s complement:
      00011001  111001112

## Slide 22: CONVERTING TWO’S COMPLEMENT TO SIGNED DECIMAL
Method 1:
Positive values (most-significant bit is 0)
  Same as unsigned (use polynomial evaluation)
Negative values (most-significant bit is 1)
  Use Two’s Complement procedure to find the representation of the corresponding positive value.
  Find decimal magnitude using polynomial evaluation
  Add a leading minus sign

## Slide 23: Converting Two’s Complement to Signed Decimal (Method 1)
Original 2’s complement number: 100011002
Negative  find positive equivalent: 011101002
Polynomial evaluation:
64+32+16+4 = 11610
Add a leading minus sign:
−11610

## Slide 24: CONVERTING TWO’S COMPLEMENT TO SIGNED DECIMAL
Method 2:
Use polynomial evaluation, but make the weight of the most-significant bit position negative.

## Slide 25: Converting Two’s Complement to Signed Decimal (Method 2)
Original 2’s complement number: 100011002
Polynomial evaluation: −128+8+4
= −11610

## Slide 26: HEX AS A SHORTHAND FOR BINARY
Hexadecimal (radix 16) numbers require far fewer digits than their equivalent binary (radix 2) representation.
Conversion between binary and hex is trivial due to power relationship (16 = 24). Each hex digit corresponds to a group of four binary digits. Groups are independent of each other.
Hex is used as a convenient short-hand for binary that reduces transcription errors.

## Slide 27: Hex/Binary Table

## Slide 28: Convert Hex to Binary
Convert F1.2C16 to Binary:
F 1 . 2 C
1111 0001 . 0010 11002

## Slide 29: Convert Binary to Hex
Original binary number: 1011010.10010112
Split into groups of 4, starting at radix point:
101 1010 . 1001 011
Pad with 0’s to complete the groups:
0101 1010 . 1001 0110
3. Replace each group by equivalent hex digit:
5 A . 9 616
  Be sure to form groups working outward from the radix point!

## Slide 30: Converting from Octal to Hex
Hard way:
Convert octal to decimal using polynomial evaluation
Convert decimal to hex using repeated division/multiplication
Easy way:
Convert from octal to binary using short-cut (8 = 23)
Convert from binary to hex using short-cut (16 = 24)

## Slide 31: Converting -25.7510 to 2’s Comp.
-25: 25 = 16 + 8 + 1
   011001
-25 = 100111
.75: .75 = .5 + .25
 .11
Combining results:
 100111.112
Checking (poly eval):
= -24.2510
Correct Method:
+25.75 = 16 + 8 + 1 + .5 + .25
= 011001.112
Remove the binary point:
 01100111
Find the negative representation:
 100110012 (-10310)
Restore the binary point:
 100110.01 (-103/4 = -25.7510)

## Slide 32: Review Problems
Unsigned:
Convert 110101.0101012 to hex (base 16)
Convert unsigned FA.CE16 to base 8
Convert unsigned 7849 to base 3
Convert unsigned 256 to decimal
Convert unsigned 2510 to base 7
Signed:
Convert -75.7510 to signed 2’s complement
Convert 1001.01102 from 2’s comp. to decimal

## Slide 33: Convert 110101.0101012 to Hex
Use power relationship (16 = 24)
Form groups of 4 bits, starting at radix point:
0011 0101 . 0101 0100
0011 0101 . 0101 0100
Use Table to convert each group:
0011 0101 . 0101 0100
3 5 . 5 416
Hex | Binary | Hex | Binary
0 | 0000 | 8 | 1000
1 | 0001 | 9 | 1001
2 | 0010 | A | 1010
3 | 0011 | B | 1011
4 | 0100 | C | 1100
5 | 0101 | D | 1101
6 | 0110 | E | 1110
7 | 0111 | F | 1111

## Slide 34: Convert FA.CE16 to base 8
1st: Base 16 to base 2 (16=24)
F A . C E16
1111 1010 . 1100 11102
11111010.110011102
2nd: Base 2 to base 8 (8=23)
11111010.110011102
011 111 010 110 011 100
011 111 010 110 011 100
3 7 2 6 3 48
.
.
.

## Slide 35: Convert 7849 to base 3
Use power relationship (9 = 32)
Each base 9 digit corresponds to 2 base 3 digits
Use table to convert each digit:
7 8 49
21 22 113
Base 9 | Base 3
0 | 00
1 | 01
2 | 02
3 | 10
4 | 11
5 | 12
6 | 20
7 | 21
8 | 22

## Slide 36: Convert unsigned 256 to decimal
Base R to Decimal  polynomial evaluation:
256 = 2x61 + 5x60
= 2x6 + 5x1
= 12 + 5
= 1710

## Slide 37: Convert unsigned 2510 to base 7
Whole #10 to Base R  repeated division (by 7):
25÷7  Q=3, R=4 3
2  Q=0, R=3
STOP
47
347
3÷7

## Slide 38: Convert -75.7510 to 2’s complement
1st: Get Binary Magnitude
7510 = 64 + 8 + 2 + 1
= 26 + 23 + 21 + 20
= 10010112
.7510 = .5 + .25
= 2-1 + 2-2
= .112
75.7510 = 1001011.112
2nd: Convert to 2’s Complement
+75.7510 = 01001011.112
Find ─75.7510:
Ignore “.”: 0100101111
2’s Comp: 1011010001
Restore “.”: 10110100.01
The minimum number of bits is 10.

## Slide 39: Convert 2’s Comp. 1001.01102 to decimal
Method #1
1001.0110 (< 0) - Find pos. equiv:
Ignore “.” 10010110
2’s Comp: 01101010
Restore “.” 0110.1010
Get decimal = 4+2+.5+.125
= 6.62510
Add minus sign -6.62510
Method #2
Use poly. eval. w/neg. 1st term:
1001.0110:
= -8 + 1 + .25 + .125
= -7 + .375
= -6.62510