## Slide 1: Chapter 5
Integer Arithmetic

## Slide 2: CONDITION FLAGS Processor Status Register (PSR)
26
0
29
28
30
31
27
N
Z
C
V
Q
reserved
DSP overflow and saturation flag: A value of 1 indicates that a saturated arithmetic instruction limited its result.
Overflow flag: A value of 1 indicates a 2’s complement overflow during an addition, subtraction or compare.
Carry or Borrow flag: A value of 1 indicates a carry out from addition or NO borrow out during subtraction.
Zero flag: A value of 1 indicates a result (or difference) of zero
Negative flag: A value of 1 indicates a negative result
This subset is the Application Processor Status Register (APSR)

## Slide 3: ADDITION AND SUBTRACTION
Binary
0011
+1010
11012
  A single ADD (or SUB) instruction works for both unsigned and 2’s comp.
Unsigned Interpretation
3
+10
1310
2’s Comp. Interpretation
(+3)
+(-6)
-310

## Slide 4: ADDITION Carries and Overflow
C4 | C3 | Unsigned | 2’s Comp
0 | 0 | OK | OK
0 | 1 | OK | Overflow
1 | 0 | Overflow | Overflow
1 | 1 | Overflow | OK
 | C4 | C3 | C2 | C1 | C0 |  | 
Carries | 1 | 1 | 1 | 0 | 0 | Unsigned | 2’s Comp
A |  | 1 | 0 | 1 | 1 | 11 | (-5)
B | + | 0 | 1 | 1 | 0 | +6 | +(+6)
S |  | 0 | 0 | 0 | 1 | 1 | +1
Ci | Ai | Bi | ∑ | Ci+1 | Si
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 2 | 1 | 0
1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 2 | 1 | 0
1 | 1 | 0 | 2 | 1 | 0
1 | 1 | 1 | 3 | 1 | 1
  Overflow detection:
  Unsigned: C flag = 1
  2’s Comp: V flag = 1

## Slide 5: SUBTRACTION Carries and Overflow
 | C4 | C3 | C2 | C1 | C0 |  | 
Carries | 1 | 0 | 0 | 1 | 1 |  | 
A |  | 1 | 1 | 0 | 0 |  | 
~B | + | 1 | 0 | 0 | 1 |  | 
A-B |  | 0 | 1 | 1 | 0 | 6 | +6
 |  |  |  |  |  | Unsigned | 2’s Comp
A |  | 1 | 1 | 0 | 0 | 12 | (─4)
B | ─ | 0 | 1 | 1 | 0 | ─ 6 | ─(+6)
C4 | C3 | Unsigned | 2’s Comp
0 | 0 | Overflow | OK
0 | 1 | Overflow | Overflow
1 | 0 | OK | Overflow
1 | 1 | OK | OK
  Overflow detection:
  Unsigned: C flag = 0
  2’s Comp: V flag = 1

## Slide 6
Instruction | Format | Operation | Flags
Add | ADD{S} Rd,Rn,Op2 | Rd  Rn + Op2 | N,Z,C,V
Add with Carry | ADC{S} Rd,Rn,Op2 | Rd  Rn + Op2 + Carry | N,Z,C,V
Subtract | SUB{S} Rd,Rn,Op2 | Rd  Rn − Op2 | N,Z,C,V
Subtract with Carry | SBC{S} Rd,Rn,Op2 | Rd  Rn − Op2 − ~Carry | N,Z,C,V
Reverse Subtract | RSB{S} Rd,Rn,Op2 | Rd  Op2 − Rn | N,Z,C,V
ADDITION AND SUBTRACTION
  "S" must be appended to affect the flags!
  "Op2" can be a constant, a register, or a shifted register.

## Slide 7: ADDITION AND SUBTRACTION y = x + 5 ;
// This works but is inefficient
LDR R0,x // R0 <-- x
LDR R1,=5 // R1 <-- 5
ADD R2,R0,R1 // R2 <-- R0 + R1
STR R2,y // R2 --> y
// Don’t need a register for constant
LDR R0,x // R0 <-- x
ADD R1,R0,5 // R1 <-- R0 + 5
STR R1,y // R1 --> y
// Reuse registers whenever possible
LDR R0,x // R0 <-- x
ADD R0,R0,5 // R0 <-- R0 + 5
STR R0,y // R0 --> y
// This won’t work – WHY?
LDR R0,x+5
STR R0,y

## Slide 8
// int64_t Add64(int64_t num1, int64_t num2) ; Add64: ADDS R0,R0,R2 // R0 = sum bits 31-0 ADC R1,R1,R3 // R1 = sum bits 63-32 BX LR // Return
MULTIPLE-PRECISION ADDITION
  Use an ADC so that the carry is included in the second sum.
  Append "S" to ADD so it will record any carry out.
R1
R0
R2
R3
num1
num2
1st: ADDS
2nd: ADC
R1
R0

## Slide 9: BINARY MULTIPLICATION
1100
×1101
100111002
0011
×0010
00000110
The product may require as many digits as the total # of digits in the two operands.
A "double length product" uses the full product width:
2N bits  N bits × N bits
A "single length product" keeps only least-significant half: N bits  N bits × N bits
12
×13
15610 =
3
×2
610 =

## Slide 10: BINARY MULTIPLICATION
1100
×1101
12
×13
15610
-4
×-3
+1210
Unsigned
2’s comp
100111002
Binary
000011002
The signed and unsigned products are different for identical operand patterns.
But the least-significant halves of both products will always be the same.

## Slide 11: MULTIPLICATION IN C
The data type (and size) of the product is the same as operands. Thus: 32 bits × 32 bits  32 bits.
Consider how integer multiplication works in C:
  int32_t a, b ;
  int32_t c ;
  a * b ;
  uint32_t x, y ;
  uint32_t z ;
  z = x * y ;
The result is often stored in a variable of the same type, so a single-length product is sufficient.
C =
Since the result is a single-length product, the same instruction can be used for signed and unsigned.
int32_t

## Slide 12: MULTIPLICATION IN C
The product of two 32-bit integers is also a 32-bit integer. C is not able to produce a double length product from single length operands!
Consider how integer multiplication works in C:
  uint32_t a32, b32 ;
  uint64_t c64 ;
  c64 = a32 * b32 ;
  c64 = a32 * c64 ;
Storing 32-bit product in a 64-bit variable simply extends the 32-bit result.
a32 is promoted to 64-bits to match c64; the 64x64 product requires a function

## Slide 13: MULTIPLICATION IN C
Consider how integer multiplication works in C:
  int8_t a8 ;
  int16_t b16 ;
  int32_t c32 ;
  c32 = a8 * b16 ;
On a 32-bit CPU, 8 and 16-bit operands are first promoted to 32 bits
Thus the product of a8 and b16 will becomes a 32x32 single-length product.
All integer multiplications produce either a single 32×32 instruction, or else a 64x64 library function call.

## Slide 14: MULTIPLICATION For Single-Length Products
Instruction | Format |  | Operation
32-bit Multiply | MUL{S} | Rd,Rn,Rm | Rd  (int32_t) Rn×Rm
32-bit Multiply with Accumulate | MLA | Rd,Rn,Rm,Ra | Rd  Ra + (int32_t) Rn×Rm
32-bit Multiply & Subtract | MLS | Rd,Rn,Rm,Ra | Rd  Ra – (int32_t) Rn×Rm
MULS affects flags N and Z. No other multiply instruction affects the flags.
All multiply instructions require their operands to be in registers. No constants or memory operands.
Note: MLA and MLS use the product of the middle two registers.

## Slide 15: MULTIPLICATION For Double-Length Products
Instruction | Format |  | Operation
64-bit Unsigned Multiply | UMULL | Rdlo,Rdhi,Rn,Rm | RdhiRdlo  (uint64_t) Rn×Rm
64-bit Unsigned Multiply with Accumulate | UMLAL | Rdlo,Rdhi,Rn,Rm | RdhiRdlo  RdhiRdlo + (uint64_t) Rn×Rm
64-bit Signed Multiply | SMULL | Rdlo,Rdhi,Rn,Rm | RdhiRdlo  (int64_t) Rn×Rm
64-bit Signed Multiply with Accumulate | SMLAL | Rdlo,Rdhi,Rn,Rm | RdhiRdlo  RdhiRdlo + (int64_t) Rn×Rm

## Slide 16: MULTIPLICATION OVERFLOW
Double-Length Products (signed or unsigned):
Overflow is not possible
Single-Length Unsigned Products:
Overflow occurs when the most-significant half of the double-length product is non-zero.
Single-Length Signed Products:
Overflow occurs when the most-significant half of the double-length product is not a sign-extension of the least-significant half.
1110 14
0111 ×7
0110 00102 9810
1110 (-2)
0111 ×(+7)
1111 00102 -1410
The overflow flag (V) is not affected. Recognizing overflow is virtually impossible if only a single-length product is available.
Overflow during multiplication means that the result exceeds the product’s range of representation.

## Slide 17: MULTIPLICATION Single-Length 64x64-Bit Product
AHI (Upper Half)
32 bits
32 bits
ALO (Lower Half)
BHI (Upper Half)
BLO (Lower Half)
  A = 232AHI + ALO
  B = 232BHI + BLO
  A×B = (232AHI + ALO)(232BHI + BLO)
  = 264AHIBHI + 232(AHIBLO + ALOBHI) + ALOBLO
Not used
Not used
AHIBHI
× 264
  ALOBLO
Not used
AHIBLO
× 232
Not used
ALOBHI
× 232
  3rd: UMULL(ALOBLO)
2nd: MLA(ALOBHI)
1st: MUL(AHIBLO)

## Slide 18: MULTIPLICATION Single-Length 64x64-Bit Product
// int64_t Mult64x64(int64_t a, int64_t b) ;
Mult64x64:
// R1.R0 = a
// R3.R2 = b
MUL R1,R1,R2 // R1 = Ahi x Blo
MLA R1,R0,R3,R1 // R1 += Alo x Bhi
UMULL R0,R2,R0,R2 // R2.R0 = Alo x Blo
ADD R1,R1,R2 // R1 += MSHalf of Alo x Blo
BX LR

## Slide 19: DIVISION IN C
Consider how integer division works in C:
  int8_t a8 ;
  int16_t b16 ;
  int32_t c32 ;
  int64_t d64 ;
  ... = a8 / b16 ;
  ... = d64 / c32 ;
8 and 16-bit operands are first promoted to 32 bits; this becomes a single 32÷32 divide instruction that produces a 32-bit quotient.
c32 is promoted to 64 bits to match d64; this becomes a library function call for 64÷64 division that returns a 64-bit quotient.
All integer divisions produce either a single 32÷32 instruction, or else a library function call for 64÷64.

## Slide 20: SINGLE-LENGTH DIVISION
11110000
÷00000100
111111002
(-16)
÷(+4)
-410 =
2’s complement:
11110000
÷00000100
001111002
240
÷4
6010 =
Unsigned:
Two different instructions are required for signed versus unsigned division.
Result produced by SDIV instruction
Result produced by UDIV instruction
Instruction | Format | Operation
Unsigned Divide | UDIV Rd,Rn,Rm | Rd  (uint32_t) Rn ÷ Rm
Signed Divide | SDIV Rd,Rn,Rm | Rd  (int32_t) Rn ÷ Rm

## Slide 21
Operation | Quotient | Remainder
(+14) ÷ (+3) | +4 | +2
(+14) ÷ (-3) | -4 | +2
(-14) ÷ (+3) | -4 | -2
(-14) ÷ (-3) | +4 | -2
COMPUTING A REMAINDER
remainder = dividend – divisor × quotient
LDR R0,dividend
LDR R1,divisor
SDIV R2,R0,R1 // R2=R0/R1
STR R2,quotient
MLS R3,R1,R2,R0 // R3 = R0 – R1*R2
STR R3,remainder

## Slide 22: DIVISION OVERFLOW
The smaller range of a single-length dividend drastically reduces the number of operand combinations that result in an overflow, leaving only the following possibilities:
Unsigned or 2's complement: Division by zero
2's complement: Full-scale negative (-232) divided by -1,
There is no hardware detection of overflow during integer division. V flag (overflow) is not affected.
Overflow during division means that the result exceeds the quotient’s range of representation.

## Slide 23: SATURATING ARITHMETIC
Instruction | Format |  | Operation
Signed Saturate | SSAT | Rd,n,Op2 | Rd  max(min(−2n−1, Op2), 2n−1−1) Op2 = Rm or Rm,ASR # or Rm,LSL #
Unsigned Saturate | USAT | Rd,n,Op2 | Rd  max(min(0, Op2), 2n−1) Op2 = Rm or Rm,ASR # or Rm,LSL #
Think of these as "clipping" instructions. Given a value, these instructions can limit it to the range of an N-bit representation.
LDRB R0,rgb_red // This code doubles the intensity of the
USAT R0,8,R0,LSL 1 // 8-bit red RGB component of a pixel, and
STRB R0,rgb_red // limits the result to avoid overflow.
The Q flag is set when saturation occurs; no other flags are affected.

## Slide 24
Instruction | Format |  | Operation | Operands
Saturating Add | QADD QADD8 QADD16 | Rd,Rn,Rm Rd,Rn,Rm Rd,Rn,Rm | Rd  max(min(−231, Rn+Rm), 231−1) Rd  max(min(−27, Rn+Rm), 27−1) Rd  max(min(−215, Rn+Rm), 215−1) | 1×32 4×8 2×16
Saturating Subtract | QSUB QSUB8 QSUB16 | Rd,Rn,Rm Rd,Rn,Rm Rd,Rn,Rm | Rd  max(min(−231, Rn−Rm), 231−1) Rd  max(min(−27, Rn−Rm), 27−1) Rd  max(min(−215, Rn−Rm), 215−1) | 1×32 4×8 2×16
Unsigned Saturating Add | UQADD UQADD8 UQADD16 | Rd,Rn,Rm Rd,Rn,Rm Rd,Rn,Rm | Rd  max(min(0, Rn+Rm), 232−1) Rd  max(min(0, Rn+Rm), 28 −1) Rd  max(min(0, Rn+Rm), 216−1) | 1×32 4×8 2×16
Unsigned Saturating Subtract | UQSUB UQSUB8 UQSUB16 | Rd,Rn,Rm Rd,Rn,Rm Rd,Rn,Rm | Rd  max(min(0, Rn-Rm), 232−1) Rd  max(min(0, Rn-Rm), 28 −1) Rd  max(min(0, Rn-Rm), 216−1) | 1×32 4×8 2×16
SATURATING ARITHMETIC
Each instruction works on a single 32-bit value, two 16-bit values, or four 8-bit values all at once. The Q flag is set when saturation occurs; no other flags are affected.
These instructions are used to process video (three 8-bit RGB values/pixel) or audio (two 16-bit values per sample).

## Slide 25
Instruction | Format |  | Operation
Move (copy) the contents of a general-purpose register into the APSR flags. | MSR | APSR_nzcvq,Rn | NZCVQ  Rn (bits 31-27) (Bits 26-0 of PSR are unaffected)
Move (copy) the contents of the APSR into a general-purpose register. | MRS | Rd,APSR | NZCVQ  Rd (bits 31-27) (Bits 26-0 of Rd are filled with 0’s)
SATURATING ARITHMETIC
Accessing the Q Flag (Saturated)
The saturating instructions set the Q flag when saturation occurs, but never clear the Q flag. These two instructions, when combined with bit manipulation instructions from Chapter 7, can be used to clear the Q flag.