## Slide 1: ELEN/COEN 21: Introduction to Logic Design
Lectures 9 & 10: Comparators, multipliers and other combinational circuits
Radhika S. Grover
Electrical Engineering Department
Santa Clara University

## Slide 2: Combinational Logic
Overview:
Binary Adder-Subtractor
Decimal Adder
Binary Multiplier
Magnitude Comparator

## Slide 3: Block diagram of Combinational Circuits

## Slide 4: Carry Propagation
Carry has to propagate through the full adders to get the final sum.
The longest propagation delay time in an adder is the time it takes the carry to propagate through the full adders.
This is a limiting factor on the speed with which two numbers can be added.

## Slide 5: Carry lookahead
Technique to reduce the carry propagation time in a parallel adder.
Basic idea: generate the carries for subsequent stages using previous input bits directly (instead of waiting for the addition from the previous stages to complete).
Uses carry propagate and carry generate terms.

## Slide 6: Carry Lookahead
Pi = Ai Bi
Gi = AiBi
Pi is carry propagate
Gi is carry generate
The output sum Si = Pi Ci
Output carry Ci+1 = Gi + PiCi
Write the Boolean equations from each stage:
C0 = input carry
C1 =
C2 =
C3 =

## Slide 7: 4-bit adder with carry lookahead

## Slide 8: Carry Lookahead Adder
All output carries are generated after a delay through _______ levels of logic gates.
Outputs S1 through S3 have equal propagation times.
How is this better than the carry propagate adder?

## Slide 9: 4-bit adder subtractor
Addition subtraction operation can be combined into one circuit with one common binary adder.
Done by including an exclusive-OR gate with each full adder.
Only one of circuit needed for addition/subtraction for both signed and unsigned numbers (interpretation of result is different).

## Slide 10: 4-bit adder subtractor

## Slide 11: Overflow
Add two n-bit numbers and sum is n+1 bit -> overflow.
Overflow is a problem because the number of bits for result is finite.
Overflow can occur only if the two numbers added are both positive or negative.
Example:
Carry: 0 1 1 0
+70 0 1000110 -70 1 0111010
+80 0 1010000 -80 1 0110000
+150 1 0010110 -150 0 1101010
Negative number!
Positive number!

## Slide 12: Detecting overflow
Overflow has occurred if:
Carry out of sign bit position ≠ Carry into sign bit position
Carry: 0 1 1 0
+70 0 1000110 -70 1 0111010
+80 0 1010000 -80 1 0110000
+150 1 0010110 -150 0 1101010
Negative number!
Positive number!
What kind of circuit can detect overflow?

## Slide 13: Decimal Adder
BCD Adder: Adds two decimal digits in BCD with an input carry from previous stage.
Each input digit does not exceed 9, the output sum cannot be greater than 9 + 9 + 1 = 19.
BCD Digits are first added in a 4-bit binary adder (result ranges from 0 to 19).
If the output sum is greater than 9, add a binary 6 (0110) to convert it to BCD.

## Slide 14: Decimal Adder cont.
Condition for a correction can be given by:
C = K + Z8Z4 + Z8Z2
When C=1, it is necessary to add 0110 to the binary sum and provide an output carry to next stage.

## Slide 15: Decimal Adder cont.

## Slide 16: Binary Multiplier

## Slide 17: 4-bit by 3-bit binary multiplier

## Slide 18: Magnitude Comparator
A = A3A2A1A0
B = B3B2B1B0
Let xi = AiBi + Ai’ Bi’ for i = 0, 1, 2, 3
i.e. xi = 1 only if pair of bits in position i are equal.
(A = B) = x3x2x1x0
(A > B) = A3B3’ + x3A2B2’ + x3x2A1B1’ + x3x2x1A0B0’
(A < B) = A3’B3 + x3A2’B2 + x3x2A1’B1 + x3x2x1A0’B0

## Slide 19: 4-bit magnitude comparator