## Slide 1: ELEN 21/COEN 21: Introduction to Logic Design
Lectures 3 & 4 (Part 2): Boolean algebra
Radhika S. Grover
Electical Engineering Department
Santa Clara University
rgrover@scu.edu

## Slide 2: Consensus Theorem
XY + X’Z + YZ = XY + X’Z (YZ is redundant)
  Proof: XY + X’Z + YZ = XY + X’Z + (X + X’)YZ
  = (XY + XYZ) + (X’Z + X’YZ)
  = XY(1 + Z) + X’Z(1 + Y) = XY + X’Z
  Finding consensus terms:
  1. Find a pair of terms, one of which contains a variable and the other its complement
  A’C’D + A’BD + BCD + ABC + AC’D
  2. Ignore the variable and its complement; the left variables composite the consensus term
  (A’BD) + (ABC) = BD*BC = BCD (redundant term)

## Slide 3: Example
a’b’ + ac + bc’ + b’c + ab
= a’b’ + ac + bc’ + ab
= a’b’ + ac + bc’

## Slide 4: Dual Form Of Consensus Theorem
Consensus Theorem:
  XY + X’Z + YZ = XY + X’Z (YZ is redundant)
  (X + Y)( X’ + Z)(Y + Z) = (X + Y)(X ’+ Z)
  (Y + Z) is redundant
  e.g.
  (a + b + c’)(a + b + d’)(b + c + d’) = (a + b + c’)(b + c + d’)
dual